## Slide 1: On Common Test Conditions document
Roman Chernyak, Lien-Fei Chen, Xiaozhong Xu, Shan Liu (Tencent)
JVET-AD0242

## Slide 2: Problem statement
JVET-AD0242
Two missing parts were identified in the recent version CTC document JVET-Y2017:
Missing specific description of PSNRs and bitrates averaging process for parallel RA simulation 
May lead to slightly different simulation results if implemented differently
Missing sequence-specific LastValidFrame parameter 
May lead to visible difference in simulation results if not specified in simulation
Note: neither of the proposed changes intend to affect the current testing methodology:
the purpose of this document is to align the CTC document with the actual testing process

## Slide 3: Aspect 1. Parallel RA results averaging
JVET-AD0242
To illustrate the problem here are ECM7 encoder output snippet for ParkRunning sequence encoding at QP 37:
POC 0 LId: 0 TId: 0 ( IDR_N_LP, I-SLICE, QP 34 ) 1295744 bits [Y 37.6155 dB U 33.1435 dB V 35.2663 dB] [xY 4042cec82f3a009f xU 4040925e441ee8f0 xV 4041a21713abeb9f] [ET 27076 ] [L0] [L1]
POC 32 LId: 0 TId: 0 ( TRAIL, B-SLICE, QP 36 ) 1068480 bits [Y 36.9685 dB U 32.7667 dB V 34.7934 dB] [xY 40427bf9388b7dd9 xU 4040622302f7769c xV 4041658e333ebd6e] [ET 22740 ] [L0 0] [L1 0c]
…
SUMMARY --------------------------------------------------------
Total Frames | Bitrate Y-PSNR U-PSNR V-PSNR YUV-PSNR xY-PSNR xU-PSNR xV-PSNR
65 a 7180.4923 33.9864 31.5198 33.6546 33.3503 4040fe41e4cb14fa 403f85122f276db1 4040d3c8fc7373ad
Two types of information need to be collected for each RA segment:
Bitrates (bits)  highlighted in yellow
PSNRs  highlighted in blue
Ambiguity: from where to take bitrates (bits) information?
Method 1: use bits number from each frame (integer number of bits)
Method 2: use encoder summary bitrate (floating point bitrate rounded to 4 decimal digits)

## Slide 4: Aspect 1. Parallel RA results averaging (cont’d)
JVET-AD0242
To illustrate the problem here are ECM7 encoder output snippet for ParkRunning sequence encoding at QP 37:
POC 0 LId: 0 TId: 0 ( IDR_N_LP, I-SLICE, QP 34 ) 1295744 bits [Y 37.6155 dB U 33.1435 dB V 35.2663 dB] [xY 4042cec82f3a009f xU 4040925e441ee8f0 xV 4041a21713abeb9f] [ET 27076 ] [L0] [L1]
POC 32 LId: 0 TId: 0 ( TRAIL, B-SLICE, QP 36 ) 1068480 bits [Y 36.9685 dB U 32.7667 dB V 34.7934 dB] [xY 40427bf9388b7dd9 xU 4040622302f7769c xV 4041658e333ebd6e] [ET 22740 ] [L0 0] [L1 0c]
…
SUMMARY --------------------------------------------------------
Total Frames | Bitrate Y-PSNR U-PSNR V-PSNR YUV-PSNR xY-PSNR xU-PSNR xV-PSNR
65 a 7180.4923 33.9864 31.5198 33.6546 33.3503 4040fe41e4cb14fa 403f85122f276db1 4040d3c8fc7373ad
 | Bitrates | xY-PSNR | xU-PSNR | xV-PSNR
Method 1 (frame-by-frame data) | 6570.3413 | 33.907 | 31.5785 | 33.6755
Method 2 (summary data) | 6570.3414 | 33.907 | 31.5785 | 33.6755
Difference | 0.0001 | 0 | 0 | 0
Two methods of averaging comparison (PSNR numbers as informational)
It is proposed to clearly specify method 2 (as totally precise) in the next version of the CTC document

## Slide 5: Aspect 2. Missing LastValidFrame parameter
JVET-AD0242
The adopted proposal JVET-Y0155 introduces a parameter LastValidFrame that potentially modifies a range of frames to be coded for temporal filtering based on the sequence content (to exclude the frame that contains copyright notices) for each test sequence.
However, this information is not present in the recent CTC document (JVET-Y2017), which may lead to difference in the simulation results.
It is proposed to add the corresponding value of LastValidFrame to the Table 1, e.g., as below
Class | Sequence name | Frame count | Low delay frame count | LastValidFrame | Frame rate | Bit depth | Intra | Random access | Low-delay
A1 | Tango2 | 294 | - | n/a | 60 | 10 | M | M | -
A1 | FoodMarket4 | 300 | - | n/a | 60 | 10 | M | M | -
A1 | Campfire | 300 | - | n/a | 30 | 10 | M | M | -
A2 | CatRobot | 300 | - | n/a | 60 | 10 | M | M | -
A2 | DaylightRoad2 | 300 | - | n/a | 60 | 10 | M | M | -
A2 | ParkRunning3 | 300 | - | n/a | 50 | 10 | M | M | -
B | MarketPlace | 600 | 300 | n/a | 60 | 10 | M | M | M
B | RitualDance | 600 | 300 | n/a | 60 | 10 | M | M | M
B | Cactus | 500 | 250 | n/a | 50 | 8 | M | M | M
B | BasketballDrive | 500 | 250 | 499 | 50 | 8 | M | M | M

## Slide 6: Miscellaneous editorial changes to the text
JVET-AD0242
During this document preparation several minor issues in the CTC document were observed and corresponding fixes can be found in the attached document.
It is proposed to incorporate these changes in the next version of the CTC document