## Slide 1
JVET-AD0315
Non-EE2: Directional DC modes
K. Kim (Kyle), D. Kim, J. Son, J. Kwak
April, 2023
WILUS Inc.

## Slide 2: DC mode in ECM-8.0
Prediction of DC mode is same as VVC.
  For square blocks, the DC intra prediction mode uses the mean sample value of the reference samples to the left and above the block for prediction generation.
  For Non-square blocks, the DC intra prediction mode uses the reference samples only along the longer side of a rectangular block to calculate the mean value.

## Slide 3: Proposed method
This contribution proposes two additional DC modes, similar to the directional planar mode in ECM-8.0.
  Explicitly signaling method of which sample is used for prediction generation.
  If the directional mode of the current block is Above DC mode, the mean sample value of the above neighboring samples of the current block is used for prediction generation.
    The Left DC mode works the same way.
  If the current block is not applied the two additional DC mode, the existing DC mode is used for prediction generation.
    The existing DC mode has not been changed.
Directional mode
width == height ?
width > height ?
DC is generated by both above and left reference pixels.
DC is generated by above reference pixels.
DC is generated by left reference pixels.
no
no
yes
yes
Above DC mode ?
yes
Left DC mode ?
yes
no
DC is generated by left reference pixels.
no
DC is generated by above reference pixels.
Proposed method

## Slide 4: Proposed method
By using two additional DC modes, it becomes possible to enable the cases.
Square
block
Square
block
Reference sample used to calculate the mean value
Non-square
block
Non-square
block

## Slide 5: Proposed method
Signaling for two additional DC mode
  Encoder tests two additional DC modes (Above DC, Left DC) regardless of whether the current block is a square or non-square block.
  In the encoder side, the best DC mode is selected in terms of RDO.
  To avoid confusion with existing DC mode and MPM list construction, the two additional DC modes are signalled with a sub-mode of the directional planar mode, as shown in Table.
    The other mechanism is same as the existing DC mode (Ex. Derivation of transform kernel, MPM list derivation, …)
Directional mode | Binarization
Planar | 0
Horizontal Planar | 10
Vertical Planar | 110
Above DC | 1110
Left DC | 1111

## Slide 6: Experimental results
Anchor: ECM-8.0
  Under CTC
We use anchor result for several results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | 0.05% | -0.02% | 103% | 100%
Class A2 | -0.02% | -0.03% | 0.02% | 103% | 100%
Class B | -0.03% | -0.01% | 0.00% | 105% | 101%
Class C | -0.03% | -0.06% | 0.03% | 106% | 101%
Class E | -0.02% | -0.03% | 0.13% | 106% | 101%
Overall | -0.03% | -0.02% | 0.03% | 105% | 101%
Class D | -0.06% | -0.22% | 0.06% | 107% | 101%
Class F | 0.05% | -0.13% | -0.08% | 102% | 101%
Class TGM | 0.01% | 0.02% | 0.08% | 102% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.05% | -0.12% | 0.00% | 102% | 101%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.01% | 0.14% | 0.05% | 103% | 102%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!

## Slide 7: Conclusion
This contribution proposes two additional DC modes.
  No template matching methods.
  Does not require more processing on the neighboring reconstructed samples than VVC.
It is recommended to further investigate the proposed method in the next round of EE2.

## Slide 8: THANK YOU