## Slide 1: EE1: Summary report of exploration experiment on neural network-based video coding
E. Alshina, F. Galpin, Y. Li, D. Rusanovskyy, M. Santamaria, J. Ström, L. Wang and Z. Xie

## Slide 2: EE1 tests: plan and submitted documents
Test | Architecture | Training | Usage in a codec | Tester/Trainer | Cross-check | Proposal Doc | Cross-check Doc
EE1-0 | Unified filter (UF) as in JVET-AD0380 |  |  | Bytedance, Nokia, Qualcomm Tencent, OPPO |  | JVET-AE0191 | 
EE1-1.1* | Separate Y and UV | Aligned to JVET-AD0380 |  | Bytedance | training +test |  | 
EE1-1.2 | Decomposed CONV |  |  | Qualcomm | training +test | JVET-AE0164 | 
EE1-1.3 | Filter “head” |  |  | Qualcomm | training +test |  | 
EE1-1.4* | 4 sub-tests: temporal filter, residual, filter “head”, back bone blocks design | Not aligned to JVET-AD0380 |  | Bytedance | training +test |  | 
 |  | Not aligned to JVET-AD0380 |  | Tencent | training +test | JVET-AE0160 | 
EE1-1.5 | 3 sub-tests: filter “head”, residual block and split network design |  |  | Tencent | training +test | JVET-AE0160 | 
EE1-2* | JVET-AD0380 | Training set | JVET-AD0380 | Tencent | training +test |  | 
EE1-3.1* | JVET-AD0380 |  | flipping | OPPO | test only |  | 
EE1-3.2* |  |  | adjustment | OPPO | test only |  | 
EE1-3.3* |  |  | RDO | Bytedance | training +test |  | 
EE1-4.1 | Improved Low OP | Not JVET-AD0380 JVET-AD0380 | as in NNVC-5.0 | Dolby/Ittiam | test only | JVET-AE0067 | JVET-AE0183
EE1-4.2* | Simplified UF |  | JVET-AD0380 | Bytedance | training +test |  | 
EE1-4.3* | Simplified UF |  |  | Tencent | training +test |  | 
EE1-4.4 | Simplified UF |  |  | Qualcomm | training+test | JVET-AE0165 | 
EE1-5.1 | NN-inter |  |  | Tencent/WHU | training+test | JVET-AE0112 | JVET-AE0229
EE1-6.1 | NN-intra |  |  | Inter Digital | training +test | JVET-AE0144 | 
EE1-7.1 | JVET-AD0380 | JVET-AC0196, JVET-AD0380 | Super-resolution | Tencent | training +test |  | 
* Those EE tests are supposed to be conducted on top of the HOP model, which is apparently not available yet. Therefore, it is recommended to continue investigating these tests in the next round of EE.

## Slide 3: Unified filter design for High Operation point (HOP)
EE1-0

## Slide 4: NNVC 5.0 SW complexity / performance
 |  |  | Random Access vs VVC |  |  | All Intra vs VVC |  | 
HOP filter: past and future | Parameters, M | kMAC/pixel | BD-rate Y | BD-rate Cb | BD-rate Cr | BD-rate Y | BD-rate Cb | BD-rate Cr
EE1-0 (after stage II training)* | 1.5 | 477 | -9.5% | -22.4% | -22.1% | -7.8% | -18.8% | -20.0%
NNVC-filter set#0 (fully trained) | 1.9 | 615 | -9.8% | -21.1% | -20.5% | -7.5% | -16.8% | -17.4%
NNVC-filter set#1 (fully trained) | 3.1 | 673 | -9.6% | -20.9% | -21.5% | -7.4% | -18.3% | -19.9%
* ~1% gain is expected after Stage III training
Thanks a lot for productive collaborative work on EE1-0!

## Slide 5: What does it mean “unified design”?
Agreed during BoG and documented
  NN structure
    order of layers
    number of channels for each layer
    extra inputs (prediction, QP, ...)
  NN tool usage aspect
    on/off, QP adaptation, blending, ...
  Training procedure
    Number of stages, epochs, learning rate scheduler.....
Joint training (conducted in parallel by several parties)
Testing during training (at least after each stage)
Single modification in each EE test / sub-test

## Slide 6: EE1-0 High Operation Point NN-filter
 |  |  | Random Access vs VVC |  |  | All Intra vs VVC |  | 
Contribution | Parameters, M | kMAC/pixel | BD-rate Y | BD-rate Cb | BD-rate Cr | BD-rate Y | BD-rate Cb | BD-rate Cr
EE1-0 (stage I) I-frames only | 1.5 | 477 | -2.5% | -10.4% | -9.4% | -7.8% | -19.2% | -20.2%
EE1-0 (stage I) IPB-frames | 1.5 | 477 | -4.2% | -17.4% | -16.2% | -7.8% | -19.2% | -20.2%
EE1-0 (stage II) | 1.5 | 477 | -9.5% | -22.4% | -22.1% | -7.8% | -18.8% | -20.0%
EE1-0 (stage III)* | 1.5 | 477 |  |  |  |  |  | 
NNVC-filter set#0 (fully trained) | 1.9 | 615 | -9.8% | -21.1% | -20.5% | -7.5% | -16.8% | -17.4%
NNVC-filter set#1 (fully trained) | 3.1 | 673 | -9.6% | -20.9% | -21.5% | -7.4% | -18.3% | -19.9%
* ~1% gain is expected after Stage III training
Training Model stage I (Intra model)
  All Intra coding of DIV2K data coding with vanilla VTM (NN Tools off) ~ 10 days
  Training data dumping and DIV2K unified database creation size of 2.6TB
  Model stage I training from scratch for Intra data (40 epochs, 10 days) + test 5 days
Training Model stage II (Intra & Inter model)
  Random Access coding of BVI and TVD data with NNVC5.0 (NN Tools off, HOP Stage I model enabled for Intra Slices) ~ 10 days
  Training data dumping, BVI and TVD data unified databases creation size of 1.5TB
  Model stage II training with DIV2K, BVI and TVD databases (20 epochs, 10 days) + test 5 days
Training stage III (Intra & Inter model)
  Random Access coding of BVI and TVD data with NNVC5.0 (NN Tools off, HOP Stage II model enabled for Intra and B slices) ~ 10 days
  Training data dumping, BVI and TVD data unified databases creation size of 1.5TB
  Model stage III training with DIV2K, BVI and TVD databases (20 epochs, 10 days) + test 5 day
SW preparation: Ahg 14, NNVC SW coordinators
SADL up-dated (faster encoding /decoding)
Training: Bytedance, InterDigital, Qualcomm, Tencent, OPPO => training cross-check (deviation in average BD-rate is 0.0x%)
Testing: after each stage (or even after same epoch) => early detection of bugs in training
Procedure: regular exchange training status, test results in mail list, “best” models after each stage of the training decided based RA test partial results (class C,D) after at least one cross-check, communication in mail list but all decision announced to JVET reflector.
now

## Slide 7
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 33,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Back Bone Block, C
Back Bone Block, C
...
CONV
3  3
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N
CONV 3  1 CC21
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 1  3 CC31
CONV 3  1 C31C
PReLU
Back Bone Block C
[C,h,w]
Crop
IPB [1]
CONV 33,d5
PReLU
EE1-0 Unified Filter
Parameters selection:
d1 =12*16 C = 4*16 N = 24
d2 = 2*16 C1 =10*16 d6 = 3*16
d3 = 1*16 C21= 2*16
d4 = 1*16 C22= 2*16
d5 = 1*16 C31= 4*16
kMAC/pxl 477
Params: 1.45 M
Suggestion: complete training Stage III and adopt to NNVC-5.0, use as basis pending EE1 tests round.

## Slide 8
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 33,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Back Bone Block, C
Back Bone Block, C
...
CONV
3  3
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
Crop
N
CONV 3  1 CC21
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 1  3 CC31
CONV 3  1 C31C
PReLU
Back Bone Block C
[C,h,w]
Crop
IPB [1]
CONV 33,d5
PReLU
EE1-0 Unified Filter
Parameters selection:
d1 =12*16 C = 4*16 N = 24
d2 = 2*16 C1 =10*16 d6 = 3*16
d3 = 1*16 C21= 2*16
d4 = 1*16 C22= 2*16
d5 = 1*16 C31= 4*16
kMAC/pxl 477
Params: 1.45 M
Suggestion : “skip connection” missed in filter diagram  need to add.
2

## Slide 9: NN-filter modification for High Operation point (HOP)
EE1-1.x

## Slide 10
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 33,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
BBB, T1
...
CONV
3  3
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N:
CONV 3  1 CC21
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 3  1 CC31
CONV 1  3 C31C
PReLU
Back Bone Block T1
Crop
IPB [1]
CONV 33,d5
PReLU
EE1-1.2
C31= 3*16
CONV 1  3 CC21
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 3  1 C21C22
CONV 1  3 CC31
CONV 3  1 C31C
PReLU
Back Bone Block T2
C31= 3*16
BBB, T2
BBB, T1
BBB, T2
kMAC/pxl 426
Params: 1.3 M
Parameters selection:
d1 =12*16 C = 4*16 N = 12
d2 = 2*16 C1 =10*16 d6 = 3*16
d3 = 1*16 C21= 2*16
d4 = 1*16 C22= 2*16
d5 = 1*16 C31= 3*16
All intra cfg performance almost the same as EE1-0 (HOP)
Suggestion : review in the BOG to plan study in EE1, e.g. provide results with 3 stages training, perform training cross-check.

## Slide 11
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 33,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N
Crop
IPB [1]
CONV 33,d5
PReLU
EE1-5 split architecture
RB, Y
RB, Y
...
CONV
3  3
PReLU
CONV
3  3, 4
RB, UV
RB, UV
...
CONV
3  3
PReLU
CONV
3  3, 8
Pixel Shuffle
Pixel Shuffle
2
Parameters selection:
d1 =12*16 C = 4*16 N = 24
d2 = 2*16 C1 =10*16 d6 = 3*16
d3 = 1*16 C21= 2*16
d4 = 1*16 C22= 2*16
d5 = 1*16 C31= 4*16
CONV 3  1 CC21
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 3  1 CC31
CONV 1  3 C31C
PReLU
RB v1
==Back Bone Block (HOP)
PReLU
gCONV 3  1 CC21
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
gCONV 1  3 C21C22
CONV 3  1 CC31
CONV 1  3 C31C
PReLU
RB v2
depth-wise separable
PReLU
CONV 1  1 C22C22
gCONV 3  1 CC21
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
gCONV 1  3 C21C22
CONV 3  1 CC31
CONV 1  3 C31C
PReLU
RB v3
group convolutions
PReLU
EE1-5 residual blocks

## Slide 12: EE1-5 test results
Test | Architec-ture | Res Block | Params, M | kMAC /pixel | Train. strategy | Training set | Random Access vs NNVC-5.0 anchor |  |  | All Intra vs NNVC-5.0 anchor |  | 
 |  |  |  |  |  |  | Y | Cb | Cr | Y | Cb | Cr
NNIntra & EE1-0 (HOP) | HOP | HOP | 1.5 | 477 | Filter set#0 | Filter set#0 |  |  |  |  |  | 
NNIntra & EE1-1.5.1-subtest 1 | Filter set#0 | HOP | 1.4 | 461 |  |  | -5.1% | -14.6% | -14.5% | -3.1% | -12.4% | -13.5%
NNIntra & EE1-1.5.1-subtest 2 | Filter set#0 | v2 | 1.2 | 402 |  |  | -4.8% | -14.9% | -14.1% | -2.8% | -12.0% | -13.0%
NNIntra & EE1-1.5.1-subtest 3 | Filter set#0 | v3 | 1.3 | 408 |  |  | -5.0% | -14.2% | -13.8% | -2.9% | -11.8% | -13.0%
NNIntra & EE1-1.5.2-subtest 1 | HOP | HOP | 1.5 | 480 |  |  | -3.6% | -12.1% | -13.7% | -2.3% | -11.4% | -12.2%
NNIntra & EE1-1.5.2-subtest 2 | HOP+Split | HOP | 0.9 | 316 |  |  | -3.1% | -11.6% | -11.5% | -2.0% | -10.6% | -11.5%
Training strategy, training set different from unified procedure.
Not easy to compare results with EE1-0 and other tests in EE1
Suggestion : review in the BOG to plan study in EE1, e.g. utilizing HOP unified dataset and training process

## Slide 13: NN-filter for Low Operation point (LOP)
EE1-4.x

## Slide 14: EE1.4.1: LOP split architecture
LOP in NNVC-5.0
kMAC/pxl 16
Params: 0.21 M
EE1-4.1
kMAC/pxl 10
Params: 0.13 M
Model/Exp | K | Ky | Kc | M | My | Mc | Ry | Rc | Nc | kmac
split luma chroma (16L, 16C) | 32 | 16 | 16 | 64 | 48 | 16 | 16 | 16 | 6 | 9.9
Contribution | Random Access vs VVC |  |  | All Intra vs VVC |  | 
 | Y | Cb | Cr | Y | Cb | Cr
NNIntra & EE1-4.1 | -6.2% | -10.9% | -9.4% | -7.5% | -11.0% | -10.8%
NNIntra & LOP NNVC-5.0 | -6.6% | -7.7% | -7.3% | -7.8% | -8.6% | -8.9%
NNIntra | -1.8% | -0.5% | -0.9% | -3.6% | -3.2% | -3.3%
LOP NNVC5.0 | -5.2% | -7.5% | -6.6% | -4.6% | -5.7% | -5.7%
Suggestion: to continue study in EE1, provide quantized model and cross-check training

## Slide 15
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 33,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Back Bone Block, C
Back Bone Block, C
...
CONV
3  3
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N
CONV 3  1 CC21
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 1  3 CC31
CONV 3  1 C31C
PReLU
Back Bone Block C
[C,h,w]
Crop
IPB [1]
CONV 33,d5
PReLU
kMAC/pxl 477
Params: 1.45 M
EE1-0 Unified HOP Filter
Parameters selection:
d1 =12*16 C = 4*16 N = 24
d2 = 2*16 C1 =10*16 d6 = 3*16
d3 = 1*16 C21= 2*16
d4 = 1*16 C22= 2*16
d5 = 1*16 C31= 4*16

## Slide 16
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 33,d3
CONV 11,d4
CONV 11,d4
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Back Bone Block, C
Back Bone Block, C
...
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N
Crop
IPB [1]
CONV 33,d5
EE1-4.4 Unified LOP Filter
kMAC/pxl 18.7
Params: 0.05 M
sepCONV 1  3 CC31
sepCONV 3  1 C31C
CONV
1  1, C
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
sepCONV 1  3 CC31
sepCONV 3  1 C31C
PReLU
Back Bone Block C
[C,h,w]
Contribution | Random Access vs VVC |  |  | All Intra vs VVC |  | 
 | Y | Cb | Cr | Y | Cb | Cr
NNIntra & EE1-4.4 |  |  |  | -7.7% | -13.6% | -14.3%
NNIntra & LOP NNVC-5.0 | -6.6% | -7.7% | -7.3% | -7.8% | -8.6% | -8.9%
NNIntra | -1.8% | -0.5% | -0.9% | -3.6% | -3.2% | -3.3%
LOP NNVC5.0 | -5.2% | -7.5% | -6.6% | -4.6% | -5.7% | -5.7%
Suggestion : review in the BOG to plan study in EE1, e.g for architecture optimization, provide results with HOP 3 stages training, perform training cross-check.

## Slide 17: NN-Inter
EE1-5.x

## Slide 18: EE1-5: NN-based inter prediction with lower complexity
Modifications (compared to previous EE1 tests):
a) Remove the PFRB module and ResBlocks.
b) Replace the IFRNet module with the small IFRNet module
c) Implement the float32 SADL inference process
 | 986 kMAC/pxl; 19.3 M parameters |  |  |  |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-4.0 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Class A1 | -3.7% | -8.0% | -8.1% | -4.1% | -9.4% | -9.0% | 157% | 65726%
Class A2 | -5.4% | -11.7% | -9.4% | -6.2% | -11.5% | -9.2% | 147% | 60992%
Class B | -4.1% | -10.3% | -9.8% | -4.7% | -11.2% | -10.8% | 159% | 79960%
Class C | -5.7% | -13.4% | -13.6% | -7.3% | -13.5% | -14.3% | 123% | 47989%
Class E |  |  |  |  |  |  |  | 
Overall | -4.7% | -11.0% | -10.4% | -5.6% | -11.5% | -11.0% | 146% | 63562%
Class D | -7.2% | -14.2% | -15.6% | -6.8% | -14.8% | -15.2% | 113% | 32008%
 | 504 kMAC/pxl; 14.9 M parameters |  |  |  |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-4.0 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Class A1 |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  | 
Class B | -3.2% | -7.3% | -6.6% | -3.9% | -9.3% | -8.4% | 700% | 1030222%
Class C | -4.5% | -7.0% | -7.2% | -6.0% | -9.7% | -10.0% | 441% | 761956%
Class E |  |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  |  | 
Class D | -5.5% | -5.9% | -6.5% | -5.7% | -10.4% | -10.1% | 751% | 1300136%
NOW:
BEFORE:
Suggestion: get opinion of cross-checker.

## Slide 19: NN-Inter
EE1-6.x

## Slide 20: EE1-6.1: neural network-based intra prediction with reduced complexity
architecture | NN-Intra in NNVC-5.0 | EE1-6
Number of hidden layers | For 16x16, 3. For the other six neural networks, 2. | Same.
Number of neurons per hidden layer | 1216. | For 4x4, 8x4, and 16x16, 1216 for the last hidden layer, and 640 for the other hidden layers. For the other four neural networks, 1216.
Biases | For all layers. | Only for the layer returning and the layer returning and .
kMAC/ pxl (max) | 7.8 | 4.8
Total parameters, M | 1.5 | 1.3
architecture | NN-Intra in NNVC-5.0 | EE1-6
Number of hidden layers | For 16x16, 3. For the other six neural networks, 2. | Same.
Number of neurons per hidden layer | 1216. | For 4x4, 8x4, and 16x16, 1216 for the last hidden layer, and 640 for the other hidden layers. For the other four neural networks, 1216.
Biases | For all layers. | 
kMAC/ pxl (max) | 7.8 | 4.8
Total parameters, M | 1.5 | 1.3
all layers are fully-connected (no convolutions)
Performance degradation compared to NN-Intra inNNVC-5.0
All Intra: ~0.2%
Random Access: ~0.1%
Suggestion: looking at Bytedance’s training cross-check to decide.

## Slide 21: EE1 recommendations:
Present unified HOP filter (JVET-AE0191) in details;
Adopt HOP filter from JVET-AE0191 (after training is finished) to NNVC-6.0;
Continue investigating pending EE tests of this round (supposed to be conducted on top of the HOP model) in the next round of EE;
Conduct BoG to review input contributions and plan EE1 tests, identify potential for joint training in the next EE1 round (could be two designs for LOP and HOP).
Conduct training cross-check for low-complexity NN-Intra (EE1-6)