## Slide 1: AHG12: Spatial CABAC tuning JVET-AE0058
Jani Lainema, Alireza Aminlou, Pekka Astola, Ramin G. Youvalari, Döne Bugdayci Sansli

## Slide 2
Introduction
CABAC contexts are updated in scan order
Scan order has “spatial discontinuities” especially when moving to a new CTU
  Jump from bottom-right corner of the previous CTU to the top-left corner of the new CTU
  CABAC contexts tuned for the last CU in previous CTU are typically not ideal when suddenly moving away from that neighborhood

## Slide 3
Proposal
Finetune contexts when starting a new CTU
  Feed in N bins from the bottom CUs of above CTU to the context update process
  Inverse bin order to simulate approaching top-left corner of the new CTU from bottom-right corner of the above CTU
Tested configurations
  Test 1: N = 512, update shorter window estimator
  Test 2: N = 1024, update both estimators
  Both tests with max. 32 bins used per context
    Avoid using large portion of the update bins for a few very active contexts

## Slide 4
Results
Test 1: N = 512, update shorter window estimator
 | All Intra Main10 |  |  |  | 
 | Over ECM-9.0 Full |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04 % | -0.04 % | -0.05 % | 98 % | 96 %
Class A2 | -0.04 % | 0.01 % | 0.02 % | 97 % | 98 %
Class B | -0.04 % | 0.04 % | -0.05 % | 99 % | 98 %
Class C | -0.02 % | -0.06 % | -0.03 % | 100 % | 97 %
Class E | -0.06 % | 0.05 % | 0.11 % | 99 % | 96 %
Overall | -0.04 % | 0.00 % | -0.01 % | 99 % | 97 %
Class D | 0.00 % | -0.01 % | -0.04 % | 101 % | 92 %
Class F | -0.02 % | -0.10 % | 0.19 % | 99 % | 96 %
TGM | -0.07 % | -0.12 % | -0.07 % | 98 % | 99 %
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 Full |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05 % | -0.34 % | 0.01 % | 101 % | 98 %
Class A2 | -0.06 % | -0.25 % | -0.07 % | 101 % | 97 %
Class B | -0.08 % | -0.07 % | 0.07 % | 100 % | 102 %
Class C | -0.03 % | -0.14 % | -0.12 % | 100 % | 101 %
Class E |  |  |  |  | 
Overall | -0.06 % | -0.18 % | -0.02 % | 100 % | 100 %
Class D | 0.07 % | -0.28 % | 0.07 % | 101 % | 101 %
Class F | -0.08 % | -0.34 % | -0.26 % | 100 % | 101 %
TGM | -0.03 % | 0.00 % | -0.03 % | 101 % | 101 %

## Slide 5
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 Full |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06 % | -0.30 % | -0.02 % | 101 % | 97 %
Class A2 | -0.10 % | -0.08 % | -0.06 % | 100 % | 98 %
Class B | -0.06 % | -0.18 % | -0.04 % | 101 % | 102 %
Class C | -0.06 % | -0.17 % | -0.15 % | 101 % | 101 %
Class E |  |  |  |  | 
Overall | -0.07 % | -0.18 % | -0.07 % | 101 % | 100 %
Class D | 0.00 % | -0.35 % | 0.15 % | 102 % | 100 %
Class F | -0.09 % | -0.15 % | -0.13 % | 101 % | 101 %
TGM | 0.02 % | 0.00 % | 0.00 % | 101 % | 101 %
 | All Intra Main10 |  |  |  | 
 | Over ECM-9.0 Full |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05 % | -0.09 % | -0.08 % | 99 % | 101 %
Class A2 | -0.04 % | -0.08 % | -0.08 % | 99 % | 100 %
Class B | -0.06 % | 0.03 % | -0.03 % | 99 % | 99 %
Class C | -0.05 % | -0.01 % | -0.07 % | 99 % | 101 %
Class E | -0.06 % | -0.04 % | 0.08 % | 99 % | 99 %
Overall | -0.05 % | -0.03 % | -0.04 % | 99 % | 100 %
Class D | 0.01 % | 0.00 % | -0.03 % | 100 % | 99 %
Class F | -0.06 % | -0.13 % | -0.03 % | 99 % | 101 %
TGM | -0.08 % | -0.12 % | -0.08 % | 97 % | 99 %
Results
Test 2: N = 1024, update both estimators

## Slide 6
Summary
Consistent coding efficiency gains
  Test 1: AI { -0.04%, 0.00%, -0.01%, 99%, 97%} RA { -0.06%, -0.18%, -0.02%, 100%, 100%}
  Test 2: AI { -0.05%, -0.03%, -0.04%, 99%, 100%} RA { -0.07%, -0.18%, -0.07%, 101%, 100%}
Negligible processing increase
  Worst case / Test 1: 0.03 context updates per sample for CTU size of 128x128
  Worst case / Test 2: 0.06 context updates per sample for CTU size of 128x128
Proposed to study the technique in the next round of EEs