## Slide 1: JVET-AF0043: Status of EE1-1.0 (LOP.2) Training Stage 3 training and inference
Stage 1 and Stage 2 results were presented at AhG11/14 Telcos: 08/09 and 08/30/2023
Data provided by:
  D. Rusanovskyy, Y. Li (Qualcomm)
  T. Shao, P. Yin, S. McCarthy(Dolby)
  J. N. Shingala, A. Shyam, A. Suneja, S. P. Badya (Ittiam)
  J. Li, Y. Li, C. Lin, K. Zhang, L. Zhang (Bytedance)
  R. Chang, L. Wang, X. Xu, S. Liu (Tencent)

## Slide 2: EE1-0 Review
EE1-0 targeted joint training of LOP ILF, based on HOP architecture.
  HOP original dataset
  HOP training framework (scripts, configuration, strategy)
EE study plan:
  For Stage 1 and 2:
    Subtest EE1-0.1: Test LOP filter architecture defined in JVET-AE0281
    Subtest EE1-0.2: Optimize the headblock design of JVET-AE0281
    Subtest EE1-0.3: Optimize Luma/Chroma performance using parameters:
      NY, NC, CY, CUV, CY21, CUV21
  For Stage 3:
    Unified (single) LOP.2 model to be trained.
  Sub-test EE1-0.4: Filter usage aspects for final model:
    Combine interfaces for usage of HOP and LOP filters
    Adaptive block sizes, on/off control at low block level
Reporting process:
  Stage 1 results were presented at AhG11/14 Telco, 08/09/2023
  Stage 2 results were presented at AhG11/14 Telco, 08/30/2023
  Description, configurations, test results were made available from JVET-AF0043.
  Software, models were made available through EE1-0 SW repository.

## Slide 3: Summary of EE1-0 results
Results for 3 stages training of LOP2 In-Loop Filter are presented.
LOP2.3 filter architecture was selected:
  Architecture of JVET-AE0281 with modified parameters.
  Complexity: 17kMAC/pixel (Excel).
  Model size: 1 model, 0.05M parameters.
Independent dataset production and training:
  Bytedance, Dolby, Ittiam, Qualcomm, Tencent.
Comparative inference results (AI and RA) :
  Vs. VTM, NN-Intra OFF: {-4.7%, -9.8, -10.1%} and {-5.3%, -10.9%,-10.4%}.
  Vs. NNVC6.0, NN-Intra ON: {-0.2%, -4.6%, -4.6%} and {-0.3%,-4.3%,-4.3%}.
  Additionally, EE1-0.4: {-0.0%, -0.5%, -0.2%} and {-0.0%,-1.3%,-0.3%}.

## Slide 4
Rec [3]
CONV 33,d1
CONV
1  1, d6
PReLU
CONV2
33, CY +CUV
PReLU
Back Bone Block, CY
Back Bone Block, CY
...
PReLU
CONV
3  3, 4
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
NY
Crop
JVET-AE0281: EE1-0 LOP2.0 filter
sepCONV
13 CYCY21
sepCONV
31 CY21CY
CONV
1  1, CY
Back Bone Block, CUV
Back Bone Block, CUV
...
PReLU
CONV
3  3, 2
sepCONV
13 CUVCUV21
sepCONV
31 CUV21CUV
CONV
1  1, CUV
NC
Pred [3]
CONV 33,d2
BS [3]
QPbase
[1]
QPslice[1]
IPB [1]
Headblock |  |  |  | Backbone |  | 
d1 | 12 |  |  |  | Luma | Chroma
d2 | 8 |  |  | N | 12 | 6
d3 | 4 |  |  | C | 16 | 16
d4 | 2 |  |  | C1 | 64 | 48
d5 | 2 |  |  | C21 | 16 | 16
d6 | 24 |  |  |  |  | 
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV 11,d5
[C,h,w]
CONV 1  1 C1+C
CONV 1  1 CC1
sepCONV 1  3 CC21
sepCONV 3  1 C21C
PReLU
Back Bone Block C
[C,h,w]
CONV 1  1 CC
Complexity: 17.6 kMAC/pixel

## Slide 5
Rec [3]
CONV 33,d1
CONV
1  1, d6
PReLU
CONV2
33, CY +CUV
PReLU
Back Bone Block, CY
Back Bone Block, CY
...
PReLU
CONV
3  3, 4
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
NY
Crop
JVET-AF0043: EE1-0 LOP2.3 Filter.
sepCONV
13 CYCY21
sepCONV
31 CY21CY
CONV
1  1, CY
Back Bone Block, CUV
Back Bone Block, CUV
...
PReLU
CONV
3  3, 2
sepCONV
13 CUVCUV21
sepCONV
31 CUV21CUV
CONV
1  1, CUV
NC
Pred [3]
CONV 33,d2
BS [3]
QPbase
[1]
QPslice[1]
IPB [1]
Headblock |  |  |  | Backbone |  | 
d1 | 12 |  |  |  | Luma | Chroma
d2 | 8 |  |  | N | 14 | 4
d3 | 4 |  |  | C | 16 | 16
d4 | 2 |  |  | C1 | 64 | 32
d5 | 2 |  |  | C21 | 16 | 16
d6 | 24 |  |  |  |  | 
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV 11,d5
[C,h,w]
CONV 1  1 C1+C
CONV 1  1 CC1
sepCONV 1  3 CC21
sepCONV 3  1 C21C
PReLU
Back Bone Block C
[C,h,w]
CONV 1  1 CC
Complexity: 17.0 kMAC/pixel

## Slide 6: EE1-0 Training Process
HOP training framework was used.
  Stage 1 dataset of HOP was used (DIV2K).
  Stage 2 and 3 datasets are LOP2-based (BVI and TVD).
Changes to HOP training framework (yellow highlight):
Network Information in Training Stage |  | 
Mandatory | GPU Type | Nvidia GeForce RTX4090 / A100
 | Framework: | Pytorch v2.0.1
 | Number of GPUs per Task | 1
 | Epoch: | Stage1: 130 epochs Stage2/3: 60 epochs
 | Batch size: | Stage1: 64 Stage2/3: 128
 | Loss function: | L1, L2
 | Training time (for 1 model): | ~7 to 10 days per stage
 | Training data information: | DIV2K, BVI-DVC, TVD
Optional |  | 
 | Number of iterations | 
 | Patch size | 144x144
 | Learning rate: | Stage1: 1e-4 Stage2/3: 4e-4
 | Learning rate update strategy | Stage1: 120,123,126, mse-epoch:126 Stage2/3: 55, 57, 58, mse-epoch:58
 | Optimizer: | ADAM
 | Preprocessing: | flipped, rotated
 | Mini-batch selection process: | random cropped
 | Training data update strategy: | 
 | Other information: | 

## Slide 7: Conclusion of LOP.2 Stage 1 training
Stage 1 Reporting:
    Presented on 08/09/2023 Telco, uploaded as JVET-AF0043
  Training scripts and models were shared on EE1-0 branch
Agreed training configurations:
    Stage 1 and Stage 2 schedulers.
    Luma/Chroma weights: 12:1:1.
    Stage 2 dataset produced with float model LOP2.0 (JVET-AE0281)
 | EE1-0.1_st1_float vs vtm Train YUV loss = 12:1:1 |  | 
 | All Intra |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -3.99% | -9.83% | -11.36%
Class A2 | -4.11% | -11.88% | -9.67%
Class B | -4.01% | -11.44% | -10.61%
Class C | -4.38% | -12.32% | -13.08%
Class E | -5.98% | -11.67% | -13.49%
Overall | -4.43% | -11.48% | -11.61%
Class D | -4.70% | -11.12% | -13.39%
 | EE1-0.1_st1_int16 vs vtm Train YUV loss = 12:1:1 |  | 
 | All Intra |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.03% | -9.82% | -11.24%
Class A2 | -4.02% | -11.84% | -9.55%
Class B | -3.97% | -11.35% | -10.44%
Class C | -4.25% | -12.33% | -13.05%
Class E | -5.89% | -11.59% | -13.50%
Overall | -4.37% | -11.43% | -11.52%
Class D | -4.53% | -11.04% | -13.23%

## Slide 8: Conclusion of LOP.2 Stage 2 training
Stage 2 Reporting:
    Presented on 08/30/2023 Telco, uploaded as JVET-AF0043
  Training scripts and models were shared on EE1-0 branch.
Agreed training configurations:
    Stage 3 scheduler, identical to Stage 2.
    Use of batch_size=128 and lr=10e-4.
    Model was quantized with Q11, Q10 applied to layers with detected overflow.
    LOP2.3 agreed : 17.0 kMAC/pixel, 0.05M parameters.
    Selected Stage 2 int16 model was shared for Stage 3 dataset production.
 | st2.lop2.3_bs128_int16 vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.25% | -9.31% | -9.68% | -5.32% | -8.76% | -9.40%
Class A2 | -4.18% | -10.62% | -8.58% | -5.27% | -11.62% | -7.93%
Class B | -4.19% | -10.45% | -10.63% | -4.44% | -11.39% | -10.96%
Class C | -4.29% | -11.50% | -11.15% | -4.60% | -11.30% | -9.13%
Class E | -6.11% | -9.91% | -11.64% |  |  | 
Overall | -4.54% | -10.43% | -10.41% | -4.83% | -10.89% | -9.56%
Class D | -4.14% | -9.77% | -10.55% | -5.40% | -10.59% | -9.19%

## Slide 9: Stage 3 dataset production:
Stage 3 dataset preparation:
    Stage 3 dataset production followed HOP guidelines.
    EE1-0 SW was used to dump training data:
      EE1-0 SW branch
      --NnIntraPred=0 --NnlfOption=4 --NnlfHop=1
      --NnlfHopModelName=“model_stage2_int16.sadl”
      Model was shared on EE1.0 repository
    Dataset was produced independently by participants (Bytedance, Dolby, Ittiam, Qualcomm and Tencent)
      Information was communicated through EE1-0 SW repository and emails.
      md5 sum values, bitrate and PSNR for encoded bitstreams were shared.
      md5 sums values for resulting Stage3 datasets were x-checked.
    Cross-checked resulting MD5 sums values for Stage 3 dataset files are listed below:
bvi: "md5": "65ac747164496c00a770f85979450bcb"
bvi_valid: "md5": "ccee848c9b64ecf0dfc0f8bede74a388"
tvd: "md5": "6bbbf5fd63e5339057c221138a34580d"
tvd_valid: "md5": "78c2c968923639a50bb370aee8bc299d"

## Slide 10: Stage 3 training:
LOP2.3 was independently trained by participants:
  Bytedance, Dolby, Ittiam, Qualcomm and Tencent.
  Validation loss function, resulting models in sadl and ckpt format were shared.
HOP training framework was used:
    Datasets: HOP Stage 1 (DIV2K) and LOP Stage 3 dataset (BVI, TVD).
    Parameters: batch_size=128 and lr=10e-4, nEpochs: 60, scheduler: {55, 57, 58, mse-epoch:58}.
Example of Validation loss:
  L1 validation losses (Source: Ittiam).
  L2 did not exhibit animalities.

## Slide 11: Stage 3 inference:
LOP2.3 inference was independently tested and cross-checked by proponents:
  Bytedance, Dolby, Ittiam, Qualcomm and Tencent.
    Original HOP interface was tested.
Quantization:
  Overflow-constrained layer-wise quantization used (Q=9..11)
Best performing model results selected:
    Selection based on NN-Intra disabled vs VTM.
 | LOP2.3_float vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.44% | -8.52% | -7.71% | -5.87% | -6.84% | -8.55%
Class A2 | -4.42% | -10.06% | -8.60% | -5.69% | -11.25% | -8.63%
Class B | -4.33% | -9.83% | -10.11% | -5.02% | -11.69% | -11.42%
Class C | -4.61% | -10.47% | -11.02% | -5.19% | -11.93% | -12.30%
Class E | -6.42% | -9.57% | -12.08% |  |  | 
Overall | -4.78% | -9.75% | -9.99% | -5.37% | -10.70% | -10.52%
Class D | -4.96% | -8.72% | -11.69% | -6.20% | -9.40% | -12.34%
 | LOP2.3_int16 vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.49% | -8.63% | -8.37% | -5.82% | -7.47% | -8.49%
Class A2 | -4.35% | -10.00% | -8.58% | -5.57% | -11.66% | -8.74%
Class B | -4.31% | -9.80% | -10.07% | -4.97% | -11.76% | -11.01%
Class C | -4.54% | -10.55% | -11.13% | -5.13% | -11.92% | -12.21%
Class E | -6.35% | -9.57% | -12.01% |  |  | 
Overall | -4.74% | -9.77% | -10.10% | -5.30% | -10.92% | -10.37%
Class D | -4.87% | -8.87% | -11.72% | -6.08% | -9.49% | -12.22%

## Slide 12: Stage 3 inference:
Best performing int16 model was tested with NN-Intra ON:
  Anchor1: VTM.
  Anchor2: NNVC6.0.
  Test: stage3_lop2.3, NN-Intra ON.
Observation:
  EE1-0 LOP2.3 filter outperforms LOP1 filter.
 | nnIntra_LOP2.3_int16 vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -8.48% | -12.25% | -11.85% | -7.83% | -8.69% | -10.02%
Class A2 | -7.03% | -12.49% | -11.22% | -6.81% | -12.08% | -9.51%
Class B | -7.27% | -12.52% | -12.94% | -6.53% | -12.55% | -11.74%
Class C | -7.43% | -13.33% | -14.02% | -6.56% | -13.24% | -13.37%
Class E | -10.61% | -14.09% | -15.46% |  |  | 
Overall | -8.02% | -12.91% | -13.13% | -6.86% | -11.87% | -11.38%
Class D | -7.52% | -11.44% | -14.56% | -7.29% | -10.65% | -13.34%
 | nnIntra_LOP2.3_int16 vs NNVC6.0 |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.02% | -5.38% | -3.45% | -0.65% | -3.94% | -4.17%
Class A2 | -0.44% | -4.79% | -3.53% | -0.27% | -6.52% | -4.57%
Class B | -0.26% | -4.21% | -4.56% | -0.25% | -4.55% | -4.45%
Class C | -0.09% | -3.88% | -4.38% | 0.07% | -2.75% | -3.98%
Class E | -0.36% | -5.37% | -7.17% |  |  | 
Overall | -0.23% | -4.62% | -4.60% | -0.25% | -4.34% | -4.29%
Class D | 0.06% | -3.45% | -5.51% | 0.32% | -1.05% | -3.75%

## Slide 13: EE1-0.4 inference:
Sub-test EE1-0.4 Filter Usage (Bytedance):
  HOP filter interface is altered with Zero-padding at picture boundaries.
  Bug-fix 70 and 72 impact.
Observations:
  Noticeable chroma gain.
  Impact is observed in bug-fix version as well.
 | EE1-0.4 vs original HOP interface, nnIntra ON, BugFix ON |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.02% | -0.50% | -0.09% | -0.04% | -1.19% | -0.18%
Class A2 | -0.01% | -0.20% | -0.04% | -0.01% | -0.65% | -0.07%
Class B | -0.02% | -0.58% | -0.25% | 0.00% | -1.43% | -0.35%
Class C | -0.03% | -0.49% | -0.20% | -0.02% | -1.41% | -0.39%
Class E | -0.03% | -0.71% | -0.12% |  |  | 
Overall | -0.02% | -0.51% | -0.15% | -0.02% | -1.22% | -0.27%
Class D | -0.06% | -1.23% | -0.40% | -0.04% | -3.46% | -0.83%
Class F | -0.01% | -0.60% | -0.46% | 0.01% | -0.91% | -0.40%
 | EE1-0.4 vs original HOP interface, nnIntra ON, BugFix OFF |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.02% | -0.45% | -0.11% | -0.05% | -1.47% | -0.34%
Class A2 | -0.01% | -0.20% | -0.04% | -0.01% | -0.46% | -0.02%
Class B | -0.02% | -0.57% | -0.26% | -0.03% | -1.64% | -0.56%
Class C | -0.03% | -0.58% | -0.24% | 0.00% | -1.41% | -0.28%
Class E | -0.05% | -0.81% | -0.09% |  |  | 
Overall | -0.03% | -0.53% | -0.16% | -0.02% | -1.31% | -0.33%
Class D | -0.09% | -1.21% | -0.38% | -0.03% | -4.20% | -0.93%
Class F | -0.01% | -0.45% | -0.32% | -0.02% | -0.89% | -0.47%

## Slide 14: Additional tests:
Fast Stage 3 test:
  LOP2 training on HOP Stage 3 dataset.
  Training was conducted with earlier models LOP2.1 and YUV weight: 6:1:1.
Observations:
  Fast Stage3 training underperform around 0.3% bd-rate gain in Luma.
  Proposed to be further studied.
 | fastSt3.lop2_float vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.26% | -9.93% | -10.69% | -5.63% | -9.68% | -10.86%
Class A2 | -4.14% | -11.24% | -9.27% | -5.24% | -12.98% | -9.02%
Class B | -4.12% | -10.97% | -11.88% | -4.64% | -13.11% | -12.63%
Class C | -4.35% | -11.76% | -12.66% | -4.88% | -13.98% | -13.18%
Class E | -5.94% | -10.61% | -12.30% |  |  | 
Overall | -4.50% | -10.96% | -11.49% | -5.02% | -12.63% | -11.70%
Class D | -4.57% | -11.15% | -12.89% | -5.74% | -14.27% | -14.49%
 | LOP2.3_float vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.44% | -8.52% | -7.71% | -5.87% | -6.84% | -8.55%
Class A2 | -4.42% | -10.06% | -8.60% | -5.69% | -11.25% | -8.63%
Class B | -4.33% | -9.83% | -10.11% | -5.02% | -11.69% | -11.42%
Class C | -4.61% | -10.47% | -11.02% | -5.19% | -11.93% | -12.30%
Class E | -6.42% | -9.57% | -12.08% |  |  | 
Overall | -4.78% | -9.75% | -9.99% | -5.37% | -10.70% | -10.52%
Class D | -4.96% | -8.72% | -11.69% | -6.20% | -9.40% | -12.34%

## Slide 15: Additional tests:
Adjustment of the training strategy (Stage 3):
  LOP training altered HOP strategy by increasing batch_size by 2x and learning rate by 4x.
  Ablation study on batch_size=64 and lr=0.0004 was conducted.
Observations:
  Mixed results are observed: gain ~0.07% for Luma RA, with some 0.3-2.2% penalty in chroma.
  Proposed to be further studied.
 | LOP2.3_bs64_int vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.43% | -7.91% | -7.22% | -5.87% | -7.28% | -6.58%
Class A2 | -4.23% | -9.21% | -7.53% | -5.63% | -10.47% | -6.66%
Class B | -4.24% | -8.90% | -9.19% | -4.86% | -10.82% | -8.40%
Class C | -4.35% | -9.26% | -9.62% | -5.06% | -10.57% | -8.02%
Class E | -6.21% | -8.53% | -9.57% |  |  | 
Overall | -4.62% | -8.80% | -8.74% | -5.27% | -9.97% | -7.59%
Class D | -4.56% | -8.55% | -9.61% | -5.98% | -9.70% | -7.69%
 | LOP2.3_int16 vs vtm |  |  |  |  | 
 | All Intra |  |  | Random Access |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -4.46% | -8.36% | -7.03% | -5.84% | -6.66% | -8.72%
Class A2 | -4.21% | -9.48% | -7.90% | -5.54% | -10.29% | -7.95%
Class B | -4.17% | -9.54% | -9.72% | -4.75% | -11.21% | -10.62%
Class C | -4.39% | -10.28% | -10.10% | -5.04% | -11.65% | -10.92%
Class E | -6.19% | -9.14% | -10.43% |  |  | 
Overall | -4.61% | -9.43% | -9.17% | -5.20% | -10.24% | -9.79%
Class D | -4.68% | -9.05% | -10.66% | -5.91% | -11.26% | -12.05%

## Slide 16: Conclusion of EE1-0 results
LOP2.3 filter architecture was jointly trained:
  Architecture of JVET-AE0281 with modified parameters.
  Complexity: 17kMAC/pixel (Excel).
  Model size: 1 model, 0.05M parameters.
Independent dataset production and training:
  Bytedance, Dolby, Ittiam, Qualcomm, Tencent.
Comparative inference results (AI and RA) :
  Vs. VTM, NN-Intra OFF: {-4.7%, -9.8, -10.1%} and {-5.3%, -10.9%,-10.4%}.
  Vs. NNVC6.0, NN-Intra ON: {-0.2%, -4.6%, -4.6%} and {-0.3%,-4.3%,-4.3%}.
  Additionally, EE1-0.4: {-0.0%, -0.5%, -0.2%} and {-0.0%,-1.3%,-0.3%}.
Proposed:
  Adopt LOP2.3 filter to NNVC and enabled it as LOP anchor.
  Consider to maintained HOP and LOP filter interface aligned.