## Slide 1
JVET-AF0134 AHG12: AMVP with SbTMVP mode
Ru-Ling Liao, Jie Chen, Yan Ye, Xinwei Li
Alibaba group
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3

## Slide 2
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3
Introduction
AMVP with SbTMVP mode was proposed in JVET-AC0103 and JVET-AD0152
  RA: -0.06% luma gain with 102% encT and 100% decT over ECM-8.0
  LB: -0.22% luma gain with 102% encT and 100% decT over ECM-8.0
It was commented that the results did not provide attractive benefit in terms of compression, compared to the increased encoder
Improvement to coding efficiency and complexity are proposed

## Slide 3
Overview to AMVP with SbTMVP
Apply SbTMVP to normal AMVP
Collocated block is obtained using MVP with a signaled MVD
Only one collocated picture is used
Number of non-zero MVD is set to 16, 32 or 64 according to low delay condition and POC distance between current picture and collocated picture
OBMC is always applied to this mode
AMVR, LIC, MHP are not applied to this mode

## Slide 4
Proposed methods
Two collocated pictures for low delay picture, and one collocated picture for non-low delay picture
The reference picture indices of subblocks are fixed to 0
The number of non-zero MVD is always set to 16
AMVR is enabled for picture resolution ≥ 1280x720
  one flag to indicate MVD resolution to be 4-pel or 64-pel
Notes: {4, 8, 12, 16}-pel or {64, 128, 192, 256}-pel

## Slide 5
Simulation results
It is recommend to further study this proposal in EE2
Thanks to Dolby for cross-checking

## Slide 6
Thanks
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3