## Slide 1: Inter Picture Dependency SEI message
JVET-AF0140-v1
Gilles Teniou, Stephan Wenger, Shan Liu (Tencent, US)
AHG9

## Slide 2: Abstract
Video decoder implementations rely more and more on mixed software/hardware configurations.
  E.g. Cloud-based decoders using GPUs
Many scenarios require the fastest possible decoding process (e.g., de-linearized TV content on VoD portals)
Parallel decoding may already be enabled at slices, tiles and subpicture level under some constraints.
A generic complementary approach is to exploit the picture-based decoding parallel processing when possible
  The (in)dependency of the following picture in decoding order therefore needs to be signaled.
It is proposed to create a dedicated SEI message.

## Slide 3: Problem statement
Parallel decoding is already enabled at different levels:
  Slice level (after entropy decoding): when constraints on independent slices are met.
  Tiles and Sub-picture level: if cross-tiles prediction and entropy dependencies are avoided.
  Wavefront Parallel Processing (WPP) also allows creation of picture partitions that can be processed in parallel.
When computing resources are available, a faster decoding may be implemented at the Picture Unit level, for cases in which the dependencies with the previous picture unit in decoding order are correctly signaled.

## Slide 4: Picture level decoding process (1/3)
Assume the following coding structure with the reference pictures dependencies illustrated in blue
  A default decoder configuration addresses the pictures sequentially in decoding order
However, identifying if the following picture in decoding order needs the current one or not, would allow to instantiate a parallel picture decoder when such a dependency does not exist.

## Slide 5: Picture level decoding process (2/3)
The table below illustrates the possible decoding picture parallelization options
  Could be further parallelized when the reference picture is not used by the next one
Current PU decoding order | Dependent of latest PU | Parallel decoding with the previous PU? | Number of parallel instances of PU decoder
0 | - | no | 1
1 | 0 | no | 1
2 | 1 | no | 1
3 | 2 | no | 1
4 | 3 | no | 1
5 | 4 | no | 1
6 | 4 | yes | 2
7 | 3 | yes | 3
8 | 7 | no | 1
9 | 7 | yes | 2
10 | 2 | yes | 3
11 | 10 | no | 1
12 | 11 | no | 1
13 | 11 | yes | 2
14 | 10 | yes | 3
15 | 14 | no | 1
16 | 14 | yes | 2

## Slide 6: Picture level decoding process (3/3)
In this scenario, the decoding process of the Picture Units could be instantiated as follow with multiple picture decoder instances.
PU Decoder instance | t0 | t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9
1 | 0 | 1 | 2 | 3 | 4 | 5 | 8 | 11 | 12 | 15
2 |  |  |  |  |  | 6 | 9 |  | 13 | 16
3 |  |  |  |  |  | 7 | 10 |  | 14 | 

## Slide 7: Proposed generic approach
At the encoder:
  For each Picture Unit, if the previous PU has not been used as a reference picture, set a flag current_picture_independent to a non null value.
    could be the identifier of the decoder instance, the the id of the latest picture used as a reference.
At the decoder:
  Interpret the inter
  Picture dependency (IPD)
  SEI message when present

## Slide 8: Proposed syntax (1/2)
ipd_update_flag
  equal to 0 indicates that the number picture decoders is not present
  equal to 1 indicates that the number of picture decoders is present and signalled in simulataneous_decoded_picture_minus1.
When simulataneous_decoded_picture_minus1 is present:
  NbPictureDecoders = Max(simulataneous_decoded_picture_minus1+1, NbPictureDecoders)
Inter_picture_dependency(payloadSize) { | C | Descriptor
ipd_update_flag | 5 | u(1)
if(ipd_update_flag) { |  | 
simultaneous_decoded_picture_minus1 | 5 | ue(v)
} |  | 
current_picture_dependency_id | 5 | ue(v)
or |  | 
current_picture_serial_number | 5 | ue(v)
picture_dependency_serial_number | 5 | ue(v)
} |  | 
3 proposed implementations described in the attached contribution

## Slide 9: Proposed syntax (2/2)
current_picture_dependency_id
  May indicate if the current picture is independent from the previous one in decoding order, and signal the recommended picture decoder instance to use.
  May indicate the picture order count of the latest required picture to be fully decoded
  Or
current_picture_serial_number indicates the serial number of the current picture unit.
picture_dependency_serial_number indicates the serial number of the latest picture in decoding order required to be decoded before being able to decode the current picture unit.
Inter_picture_dependency(payloadSize) { | C | Descriptor
ipd_update_flag | 5 | u(1)
if(ipd_update_flag) { |  | 
simultaneous_decoded_picture_minus1 | 5 | ue(v)
} |  | 
current_picture_dependency_id | 5 | ue(v)
or |  | 
current_picture_serial_number | 5 | ue(v)
picture_dependency_serial_number | 5 | ue(v)
} |  | 
3 proposed implementations described in the attached contribution
current_picture_independency_id equal to 0 indicates that the current picture unit requires the availability the decoded previous picture in decoding order.

## Slide 10: Thank you