## Slide 1: AHG9: SEI messages for common image metadata formats (JVET-AF0141) A.Hinds, S. Wenger (Tencent)
JVET: 32nd Meeting, Hannover, DE, 13-20 October 2023

## Slide 2: Background
Most (all?) digital cameras store metadata in the captured imagery
Commonly stored metadata formats
  EXIF: jointly specified by Camera & Imaging Products Association, and Japan Electronics and Information Technology Industries Association
  JFIF: specified as ITU-T T.871 | ISO/IEC 10918-5
  XMP: original spec from Adobe; codified as ISO 16684
These formats are rich in information about the context of the capture process, and the image source.

## Slide 4: (small) Example of EXIF*
Components Configuration : Y, Cb, Cr, -
Shutter Speed Value : 1/470
Aperture Value : 2.0
Brightness Value : 8.039639763
Exposure Compensation : 0
Metering Mode : Multi-segment
Flash : Off, Did not fire
Focal Length : 6.0 mm
Subject Area : 2001 1507 2311 1396
Run Time Flags : Valid
Run Time Value : 552212352209125
Run Time Scale : 1000000000
Run Time Epoch : 0
Acceleration Vector : 0.008597208188 -0.8052845599 -0.5863212344
*Complete example submitted as attachment to JVET-AF0141

## Slide 5: Example of XMP
XMP Toolkit : XMP Core 5.4.0
Creator Tool : 11.4.1
Region Type : Face
Region Area Y : 0.34899999999999998
Region Area W : 0.070000000000000007
Region Area X : 0.46699999999999997
Region Area H : 0.094000000000000028
Region Area Unit : normalized
Region Extensions Angle Info Yaw : 45
Region Extensions Angle Info Roll : 270
Region Extensions Confidence Level : 1000
Region Extensions Time Stamp : 2147483647
Region Extensions Face ID : 3
Region Applied To Dimensions H : 3024
Region Applied To Dimensions W : 4032
Region Applied To Dimensions Unit : pixel

## Slide 6: Proposed syntax (EXIF)
exif_metadata( payloadSize ) { | Descriptor
exif_cancel_flag | u(1)
if (!exif_cancel_flag) { | 
exif_persistence_flag | u(1)
exif_mode_id | u(8)
if(exif_mode_id == 0) { | 
for( i = 1; i < payloadSize; i++ ) | 
exif_data_payload_byte | b(8)
} | 
else if(exif_mode_id == 1) { | 
exif_data_URI | st(v)
} | 
} | 
} | 

## Slide 7: Proposed syntax (JFIF)
jfif_metadata( payloadSize ) { | Descriptor
jfif_cancel_flag | u(1)
jfif_type_id | u(8)
if (!jfif_cancel_flag) { | 
jfif_persistence_flag | u(1)
if(jfif_type_id == 0) { | 
for( i = 1; i < payloadSize; i++ ) | 
jfif_data_payload_byte | b(8)
} | 
else if(jfif_type_id == 1) { | 
for( i = 1; i < payloadSize; i++ ) | 
jfif_extension_payload_byte | b(8)
} | 
else if(jfif_type_id == 2) { | 
for( i = 1; i < payloadSize; i++ ) | 
jfif_header_payload_byte | b(8)
} | 
} | 
} | 

## Slide 8: Proposed syntax (XMP)
xmp_metadata( payloadSize ) { | Descriptor
xmp_cancel_flag | u(1)
if (!xmp_cancel_flag) { | 
xmp_persistence_flag | u(1)
for( i = 1; i < payloadSize; i++ ) | 
xmp_data_payload_byte | b(8)
} | 
} | 
} | 

## Slide 9: Questions?
Thank you