## Slide 1: Local Film Grain Synthesis using Annotated regions
JVET-AF0142-v1
Gilles Teniou, Stephan Wenger (Tencent, US)
AHG9

## Slide 2: Abstract
Film Grain Synthesis (aka FGS) is a tool aimed at maintaining the original film grain while preserving the encoding efficiency due to its random nature and complexity.
While being used to maintain the artistic intent or to mitigate visual artefacts, film grain is not necessarily applicable to the entire picture.
This contribution proposes to address the film grain synthesis applied locally on a picture by using the annotated regions as a mask.

## Slide 3: Problem statement
Film Grain Synthesis is not necessarily applicable in the entire picture.
  For example, a scene composited of a movie and user graphics would only require film grain on the movie parts. Other graphics objects such as logos, incrusted subtitles, info banner… should be preserved from applying film grain.
One approach to signal the areas where film grain synthesis is applicable is to use annotated regions, already defined in H.274.
  When an annotated region contains a specific label indicating that the film grain synthesis is active, the decoder can apply those values to the only identified regions.

## Slide 4: Principle illustration
Film
Grain
disabled
Film
Grain
enabled
Assume the following scenario relying a on virtual desktop where the entire screen is sent to the user as a single video stream.
Film grain synthesis, if signaled, should only be applicable to the region identified.
Such information is easily signaled with annotated regions defined by rectangle coordinates together with associated label.

## Slide 5: Proposed approach
The labels "FGS-E" and "FGS-D" are defined as Film Grain Synthesis Enabled and Film Grain Synthesis Disabled respectively.
In the presence of Film Grain Characteristics (FGC) and Annotated Regions (AR) SEI messages:
  If "FGS-E" or "FGS-D" are defined
    For each annotated region
      If the associated label is "FGS-E”
        Apply the simulated film grain values as defined in the FGC SEI message within the current region coordinates
      If the associated label is "FGS-D”
        Leave the input image unchanged within the current region coordinates
    Leave the input image unchanged in areas not covered by annotated regions (note: could be the opposite)
  Else ("FGS-E" and "FGS-D" are undefined)
    Apply the simulated film grain values as defined in the FGC SEI message on the entire picture

## Slide 6: Example (1/4)
Assume a windowed movie on top of which some graphic objects are overlayed (TV channel logo and info banner).
Here, 3 regions are identified:
  R0: The movie on which the film grain synthesis is applied
  R1: The program information banner that has not any film grain
  R2: The TV channel logo on which there is no film grain neither
JVET
TV
JVET 9pm You’re watching: Casablanca (1942)
TV 10:40pm Next: Paris Blues (1961)
R0: FGS enabled
R2: FGS Disabled
R1: FGS Disabled

## Slide 7: Example (2/4)
The annotated region SEI message is used with
  2 labels defined: "FGS-E" and "FGS-D" standing for "FGS enabled" (label_idx=0) and "FGS disabled" (label_idx=1) respectively
  3 annotated regions (ar_objects) are signaled
    annotated region 0 has FGS enabled
      ar_object_label_idx[0] = 0
    annotated region 1 has FGS disabled
      ar_object_label_idx[1] = 1
    annotated region 0 has FGS disabled
      ar_object_label_idx[2] = 1
NOTE: The order of ar_objects matters as it defines the latest labelling of pixels in case of regions overlap
AR 0
AR 1
AR 2
JVeT
TV
JVET 9pmYou’re watching: Casablanca (1942)
TV 10:40pmNext: Paris Blues (1961)
Annotated region 0
Annotated region 1
Annotated region 2
ar_object_label_idx[0] = 0
ar_object_label_idx[1] = 1
ar_object_label_idx[2] = 1

## Slide 8: Example (3/4)
annotated_regions (payloaSize) {
ar_cancel_flag = 0
[…]
ar_object_label_present_flag = 1 // labels present
ar_num_label_updates = 2 // 2 labels defined
ar_label_idx[0]=0
ar_label_idx[1]=1
ar_label[0]= “FGS-E” // label for FGS enabled
ar_label[1]= “FGS-D” // Label for FGS disabled
ar_num_object_updates =3 // 3 regions signaled
ar_object_idx[0]=0
ar_object_idx[1]=1
ar_object_idx[2]=2
For the 3 objects ar_object_label_update_flag = 1 // active region has a label
ar_object_label_idx[0] = 0 // annotated region 0 has FGS enabled
ar_object_label_idx[1] = 1 // annotated region 1 has FGS disabled
ar_object_label_idx[2] = 1 // annotated region 0 has FGS disabled
[
Three ar_bounding_box_update_flags
Three bounding boxes coordinates
]
AR 0
AR 1
AR 2
JVeT
TV
JVET 9pmYou’re watching: Casablanca (1942)
TV 10:40pmNext: Paris Blues (1961)
Annotated region 0
Annotated region 1
Annotated region 2
ar_object_label_idx[0] = 0
ar_object_label_idx[1] = 1
ar_object_label_idx[2] = 1

## Slide 9: Example (4/4)
Interpretation of Film Grain Characteristics SEI message
  If there is an annotated region SEI message associated to the current picture, check the presence of “FGS-E” and “FGS-D” labels.
  If those labels are not defined, apply FGS on the entire picture, otherwise:
Annotated region 0
Annotated region 1
Annotated region 2
    Check the label of each annotated objects
      For each of them:
        If the label corresponds to FGS-E, apply FGS as defined in FGC SEI message within the bounding box of the region
        If the label corresponds to FGS-D, keep the input image unchanged in the bounding box of the region
AR 0
AR 1
AR 2
JVeT
TV
JVET 9pmYou’re watching: Casablanca (1942)
TV 10:40pmNext: Paris Blues (1961)
Annotated region 0
Annotated region 1
Annotated region 2
ar_object_label_idx[0] = 0
ar_object_label_idx[1] = 1
ar_object_label_idx[2] = 1

## Slide 10: Proposed new text (as part of the Film Grain Characteristics SEI messages)
If the current PU contains an Annotated Regions (AR) SEI message (as defined in clause 8.18.1), then the following applies:
Let AnnotatedFgsLabelDefined indicate the presence of a label equal to "FGS-E" or "FGS-D" for the identification of Film Grain Synthesys Enabled and Film Grain Synthesys Disabled regions respectively. AnnotatedFgsLabelDefined is by default set to 0.
  AnnotatedFgsLabelDefined is equal to 1 when at least one ar_label[ar_label_idx[ i ]] is equal to "FGS_E" or "FGS-D", where i=0..ar_num_label_updates − 1.
Let AnnotatedFgsLabelEnabledIdx indicate the label index of the ar_label corresponding to Film Grain synthesis annotated region.
  If ar_label[ar_label_idx[ i ]] is equal to "FGS-E", where i=0..ar_num_label_updates – 1, AnnotatedFgsLabelEnabledIdx is set to ar_label_idx[ i ].
Let AnnotatedFgsLabelDisabledIdx indicate the label index of the ar_label corresponding to Film Grain synthesis annotated region.
  If ar_label[ar_label_idx[ i ]] is equal to "FGS-D", where i=0..ar_num_label_updates – 1, AnnotatedFgsLabelDisabledIdx is set to ar_label_idx[ i ].
Let AnnotatedFgsObjectPresentFlag indicate the presence of at least one annotated region labelled for Film Grain Synthesys. AnnotatedFgsObjectPresentFlag is by default set to 0.
  When AnnotatedFgsObjectPresentFlag is set to 0, the default equations (21) and (22) apply depending on fg_blending_mode_id.
  When AnnotatedFgsObjectPresentFlag is set to 1, AnnotatedFgsObjectLabelIdx is set to the corresponding ar_label_idx and the following applies:
    If ar_object_label_idx[ ar_object_idx[ i ] ] is equal to AnnotatedFgsEnabledLabelIdx (where i=0..ar_num_object_updates – 1), the simulated film grain values are only applied to the annotated region of index ar_object_idx[ i ], meaning for x and y comprised into the bounding box of the ar_object_idx[ i ]. Elsewhere, the input image is unchanged.
    If ar_object_label_idx[ ar_object_idx[ i ] ] is equal to AnnotatedFgsDiabledLabelIdx (where i=0..ar_num_object_updates – 1), the simulated film grain values are not applied to the annotated region of index ar_object_idx[ i ], meaning for x and y comprised into the bounding box of the ar_object_idx[ i ] resulting in the input image unchanged.
NOTE: There may be 0 or more annotated regions with the label "FGS-E". In such a case, the simulated film grain values are only applied to those regions. The application or not of the simulated film grain values may be reverted by a different label from an object with a higher index. This may happen in case of overlapping regions with opposite labels.
See the attached contribution for more details on impacts on the VSEI specification

## Slide 11: Thank you