## Slide 1: JVET-AF0156 AHG6: ECM software optimizations
Fabrice Urban, Tangi Poirier, Fabrice Le Léannec

## Slide 2: Introduction
ECM memory consumption has reached a critical level
Memory profiling (JVET-AE0180) shows high memory comes from:
  ALF encoder
  Picture Buffers
  Re-use CU routines
  Encoding library
In ECM-10, memory usage is reduced about 5GB (from 25 to 20)
  Refactor ALF covariance matrices storage (triangular matrices)
  Allocate ALF covariance matrices according to filter shape
  Condition on PIC_RECON_WRAP buffer allocation

## Slide 3: Summary of this contribution
Several ECM optimizations integrated after ECM-10.0 was tagged
Targeting memory and runtime reduction
MR516, MR525, MR523, MR527, MR517, MR518, MR520, MR526, MR521, MR528, MR529
Bit-accurate results with ECM 10.0
Worst-case memory reduction (AI, RA, LDB): 1 GB, 4 GB, 3.3 GB

## Slide 4: MR516: MAX_CTU_SIZE
The encoder allocates temporary working buffers for one CTU, in particular in the Reuse CU management.
MAX_CTU_SIZE value 256 is always considered, i.e. 4 times the required memory when CTU size 128 is used
MR516: use actual CTU size provided by encoder configuration instead of MAX_CTU_SIZE
memory reduction: 2.8 GB for non-classs-A sequences

## Slide 5: MR525: Coding Structure (CS)
CS structure :
  used at top-level to represent coded pictures
  used at substructure level, e.g. for partitioning RD exploration
CS for top-level pictures allocated with a lifetime equal to Encoder Picture Buffer in ECM (i.e. several pictures)
Some data only needs being allocated for current picture
Some memory is deallocated right after a picture is coded: m_coeffs, m_coeff_signs, m_pltIdx, m_runType
MR525: extends deallocation after a picture is encoded:
  Integer buffers (of picture size): m_cuIdx, m_puIdx, m_tuIdx
  Boolean buffers (of picture size): m_isDecomp, mcMask, mcMaskChroma
Memory reduction: up to 1.6 GB (RA, class A)

## Slide 6: MR523: Picture Buffer
Picture structure:
  Several Pel buffers to store several versions of a picture (original reconstructed, filtered, etc.)
  All buffers allocated during picture allocation, for several pictures
MR523: allocate some buffers only for current picture being encoded
  Already done for PIC_RESIDUAL and PIC_PREDICTION
  Extended to:
    PIC_TRUE_ORIGINAL, PIC_FILTERED_ORIGINAL, PIC_TRUE_ORIGINAL_INPUT, and PIC_FILTERED_ORIGINAL_INPUT (RPR case)
Memory reduction: up to 1.5 GB (RA, class A)

## Slide 7: MR527: Sign Prediction
In ECM:
  Template matching used to determine most likely sign of some transform coefficient
MR527 Code optimization:
  Use static_vector instead of std::vector for predSignsXY variable
  16-bit values instead of 32-bit values to represent positions in PositionWithLevel data structure
  Use floorLog2 instead of loops where appropriate
  Duplicate corner sample in template to have even template size
  Avoid function calls in tight loops:
    Remove SIMD code
    Define an inline chroma sample reshape function
  Use 8-bit values instead of 32-bit values to store the sign prediction type (m_coeffSigns field which is part of every TU). Main contributor to memory reduction.
  Reduce size of m_signPredTemplate by storing only vectors used for current block (512KB  4KB)

## Slide 8: Results
Optimization | RA peak memory saving (MB and %) |  |  |  |  | AI peak memory saving (MB and %) |  |  |  | 
 | Class A | Class B | Class C | Class D | Class F | Class A | Class B | Class C | Class D | Class F
MAX_CTU | -61 | -2857 | -2850 | -2856 | -3049 | -4 | -2856 | -2855 | -2856 | -2897
 | 0% | -30% | -54% | -65% | -43% | 0% | -40% | -60% | -68% | -56%
CS | -1636 | -395 | -97 | -20 | -220 | -130 | -35 | -9 | -2 | -12
 | -9% | -4% | -2% | -0% | -3% | -1% | 0% | 0% | 0% | 0%
PIC_Buf | -1523 | -397 | -84 | -21 | -118 |  |  |  |  | 
 | -8% | -4% | -1% | 0% | -1% |  |  |  |  | 
sign_pred | -695 | -579 | -551 | -544 | -592 | -596 | -560 | -545 | -544 | -546
 | -4% | -6% | -10% | -12% | -8% | -7% | -8% | -12% | -13% | -10%
CU | -246 | -192 | -187 | -175 | -198 | -246 | -200 | -182 | -174 | -179
 | -1% | -2% | -4% | -4% | -3% | -3% | -3% | -4% | -4% | -3%
PU | -74 | -8 | -7 | -7 | -14 | -9 | -10 | -7 | -7 | -6
 | 0% | 0% | 0% | 0% | 0% | 0% | 0% | 0% | 0% | 0%
MCTF | -93 | -9 | -1 | 0 | -27 |  |  |  |  | 
 | -1% | 0% | 0% | 0% | -0% |  |  |  |  | 
DBF | -84 | -8 | 0 | -1 | -28 | -3 | -3 | 0 | -1 | -1
 | 0% | 0% | 0% | 0% | 0% | 0% | 0% | 0% | 0% | 0%
Impact of individual optimizations on memory consumption
Peak memory usage is reduced by ~4GB for worst-case (RA, class A)

## Slide 9: Behavior relative to ECM-10.0
Memory reduction leads to less initialization and copy, and better cache management
 runtime is reduced
 | All Intra Main 10 |  |  |  |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  |  |  |  | 
 |  |  |  | Encoder |  |  | Decoder |  | 
 | Y | U | V | run time | VMPeak | VMPeak Diff | run time | VMPeak | VMPeak Diff
Class A1 | 0.00% | 0.00% | 0.00% | 94.4% | 88.2% | -1066 | 82.2% | 91.2% | -155
Class A2 | 0.00% | 0.00% | 0.00% | 93.0% | 88.0% | -1086 | 79.6% | 91.0% | -161
Class B | 0.00% | 0.00% | 0.00% | 94.3% | 57.4% | -3094 | 81.4% | 94.9% | -48
Class C | 0.00% | 0.00% | 0.00% | 94.5% | 36.4% | -3020 | 87.9% | 97.5% | -18
Class E | 0.00% | 0.00% | 0.00% | 94.7% | 44.5% | -3032 | 88.9% | 97.3% | -21
Overall | 0.00% | 0.00% | 0.00% | 94.2% | 57.4% | -2394 | 83.9% | 94.6% | -75
Class D | 0.00% | 0.00% | 0.00% | 96.0% | 29.8% | -3002 | 83.2% | 99.0% | -7
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3215 | #NUM! | 96.9% | -25
Class TGM | 0.00% | 0.00% | 0.00% | 95.1% | 56.8% | -3269 | 85.3% | 94.2% | -57
 | Random Access Main 10 |  |  |  |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  |  |  |  | 
 |  |  |  | Encoder |  |  | Decoder |  | 
 | Y | U | V | run time | VMPeak | VMPeak Diff | run time | VMPeak | VMPeak Diff
Class A1 | 0.00% | 0.00% | 0.00% | 93.3% | 78.7% | -4078 | 78.3% | 77.0% | -835
Class A2 | 0.00% | 0.00% | 0.00% | 94.1% | 77.8% | -4368 | 82.4% | 71.9% | -959
Class B | 0.00% | 0.00% | 0.00% | 94.9% | 60.2% | -3903 | 78.9% | 81.8% | -275
Class C | 0.00% | 0.00% | 0.00% | 97.1% | 40.3% | -3167 | 91.7% | 92.5% | -66
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 95.0% | 60.1% | -3835 | 82.7% | 81.5% | -460
Class D | 0.00% | 0.00% | 0.00% | 94.3% | 32.0% | -3043 | 86.5% | 97.4% | -19
Class F | 0.00% | 0.00% | 0.00% | 97.3% | 51.5% | -3568 | 84.4% | 88.9% | -137
Class TGM | 0.00% | 0.00% | 0.00% | 94.9% | 67.5% | -3890 | 77.7% | 87.5% | -192

## Slide 10: Behavior relative to ECM-10.0
 | Low delay B Main 10 |  |  |  |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  |  |  |  | 
 |  |  |  | Encoder |  |  | Decoder |  | 
 | Y | U | V | run time | VMPeak | VMPeak Diff | run time | VMPeak | VMPeak Diff
Class A1 |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 94.6% | 58.7% | -3360 | 88.5% | 90.1% | -146
Class C | 0.00% | 0.00% | 0.00% | 94.9% | 37.7% | -3080 | 80.4% | 95.5% | -38
Class E | 0.00% | 0.00% | 0.00% | 95.9% | 45.8% | -3179 | 80.0% | 93.6% | -66
Overall | 0.00% | 0.00% | 0.00% | 95.0% | 47.6% | -3222 | 83.6% | 92.8% | -89
Class D | 0.00% | 0.00% | 0.00% | 96.1% | 30.5% | -3018 | 84.2% | 98.3% | -12
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3338 | #NUM! | 93.2% | -80
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3586 | #NUM! | 89.3% | -161

## Slide 11: Conclusion
ECM software optimizations targeting mainly memory usage reduction.
Runtime is also decreased due to less memory access.
Encode side (over ECM-10.0):
  worst-case memory reduced by (AI, RA, LDB): 1.0 GB, 4 GB, 3.3 GB
  average encoding time (AI, RA, LDB): 94.2%, 95%, 95%.
Decoder side:
  memory reduced by up to (AI, RA, LDB): 0.15 GB, 1 GB, 0.15 GB
  average decoding time (AI, RA, LDB): 83.9%, 82.7%, 83.6%.
We encourage further work on memory and run time reduction.
Ahg6 plans to tag ECM-10.1

## Slide 12: Memory reduction since ECM-9.1
 | Over ECM-9.1 encoder |  |  |  |  | 
 | AI |  | RA |  | LDB | 
 | VMPeak | VMPeak Diff | VMPeak | VMPeak Diff | VMPeak | VMPeak Diff
Class A1 | 65.3% | -4199 | 62.4% | -8950 |  | 
Class A2 | 65.3% | -4189 | 62.0% | -9342 |  | 
Class B | 40.5% | -6131 | 43.5% | -7677 | 40.8% | -6885
Class C | 31.9% | -3686 | 34.5% | -4070 | 32.5% | -3872
Class E | 35.6% | -4412 |  |  | 35.9% | -4785
Overall | 42.5% | -4697 | 44.0% | -6833 | 35.6% | -4953
Class D | 28.3% | -3221 | 29.7% | -3391 | 28.6% | -3296
Class F | 35.5% | -4741 | 41.3% | -5605 | 38.8% | -4974
Class TGM | 40.5% | -6310 | #DIV/0! | 8089 | #DIV/0! | 6527

## Slide 13: Aside material

## Slide 14: Results of ECM master branch (@525ca76d) (Oct 03, 2023)
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  |  | 
 |  |  |  | Encoder |  |  | Decoder
 | Y | U | V | run time | VMPeak | VMPeak Diff | run time
Class A1 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | -1057 | #VALUE!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | -1050 | #VALUE!
Class B | -0.01% | -0.15% | -0.16% | 97.9% | 57.4% | -3091 | 83.5%
Class C | 0.00% | 0.03% | 0.03% | 98.1% | 36.4% | -3020 | 88.9%
Class E | 0.01% | 0.06% | -0.15% | 99.4% | 44.5% | -3031 | 92.2%
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | -2507 | #VALUE!
Class D | 0.00% | -0.09% | -0.06% | 97.2% | 29.8% | -3001 | 85.7%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3219 | #VALUE!
Class TGM | -0.21% | -0.24% | -0.27% | 97.7% | 56.8% | -3271 | 88.0%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  |  | 
 |  |  |  | Encoder |  |  | Decoder
 | Y | U | V | run time | VMPeak | VMPeak Diff | run time
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -4015 | #VALUE!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -4236 | #VALUE!
Class B | -0.05% | -0.01% | -0.20% | 96.2% | 60.2% | -3902 | 80.8%
Class C | 0.01% | 0.06% | -0.07% | 98.0% | 40.4% | -3166 | 94.3%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3708 | #VALUE!
Class D | -0.01% | -0.23% | -0.16% | 95.4% | 32.0% | -3043 | 87.8%
Class F | 0.03% | 0.10% | 0.17% | 98.9% | 51.4% | -3569 | 87.6%
Class TGM | -0.10% | -0.16% | -0.06% | 96.1% | 67.5% | -3891 | 80.5%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  |  | 
 |  |  |  | Encoder |  |  | Decoder
 | Y | U | V | run time | VMPeak | VMPeak Diff | run time
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3360 | #VALUE!
Class C | -0.04% | -0.60% | -0.32% | 96.3% | 37.7% | -3080 | 82.1%
Class E | -0.03% | 1.00% | -1.48% | 98.7% | 45.8% | -3178 | 82.8%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3185 | #VALUE!
Class D | 0.09% | -0.25% | -0.55% | 98.3% | 30.5% | -3018 | 86.1%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3332 | #VALUE!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -3681 | #VALUE!

## Slide 15: MR517: Coding Unit structure (CU)
In ECM:
  CU structure contains a lot of data stored for every CU in the encoder
  Temporary buffers are kept for the partitioning exploration and the final decision
  Some data is only needed for current CU being coded.
MR517: move following data from CU structure to IntraPrediction class.
Buffer type and name | size
int tmpXdisp[MTMP_NUM]; | 19*4 = 76 Bytes
int tmpYdisp[MTMP_NUM]; | 19*4 = 76 Bytes
IntraTMPFusionInfo tmpFusionInfo[TMP_GROUP_IDX << 1]; | 88*6 = 528 Bytes
int64_t tmpFlmParams[TMP_FLM_PARAMS][MTMP_NUM]; | 6*19*8 = 912 Bytes
int tmpNumCand; | 4 Bytes
TmrlMode tmrlList[MRL_LIST_SIZE]; | 2*20 = 40 Bytes
TOTAL | 1636 Bytes / CU
Memory reduction: more than 0.2 GB
Runtime reduction

## Slide 16: MR518: Prediction Unit (PU)
In ECM:
  PU structure contains prediction information stored for every PU (IntrapredictionData and InterPredictionData)
  Some of the data is only needed only for current PU being coded.
MR518: move following data from PU structure to IntraPrediction class.
Small memory reduction
Associated copies are removed
MPM flag and index computation are moved outside of CABAC functions
Buffer type and name | size
uint8_t intraMPM[NUM_MOST_PROBABLE_MODES]; | 22 Bytes
uint8_t intraNonMPM[NUM_NON_MPM_MODES]; | 45 Bytes
TOTAL | 67 Bytes / PU

## Slide 17: MR520: MCTF
In ECM:
  MCTF allocates new pictures for motion compensated frames,
  But original pictures can be overwritten.
MR520:
  avoid temporary memory allocation for motion compensated pictures.
  Input frame is overwritten instead
Memory reduction: up to 100 MB (depends on number of frames used in temporal filter)

## Slide 18: MR526: Deblocking Filter
In ECM:
  DBF stores information on filter length and transform edge status on a per-sample basis.
  However, this information is only needed on a 4x4 luma basis.
MR526:
  data structures are shrunk
  memory usage slightly reduced
  Run time reduced: clearing this data occurs for every CU
Note: this change is also present in VTM

## Slide 19: MR521: upper part only of covariance matrix
MR521: only compute triangular part of covariance matrix as it is symmetric and stored in a triangular format
Improved run time by avoiding unnecessary memory access and redundant computations
ALF encoder time reduced

## Slide 20: MR528: CABAC context initialization
MR528:
  Repacking data of BinProbModel_Std class (grouping by size)
  BinProbModel_Std class size reduced from 14 to 12 Bytes  CtxStore class reduced from 11914 to 10212 Bytes
  Split Ctx grouped into one ContextSet for better readability
  Using initialization with SubCtx for bit estimation related to the Geo mode.
Improved run time by reducing initialization and copy of CABAC contexts

## Slide 21: MR529: Use transposed buffer
Template Matching cost estimation:
  left side template considered as a column of 1xN samples.
  leads to do some operations such as SAD, weightedAverage and linearTranform on a sample-by-sample basis.
MR529: consider the left side template as a row enables usage of SIMD function for these operations.
Technique already used in some other parts of ECM
Reduced run time by enabling more SIMD operations