## Slide 1
Lei Zhao, Kai Zhang, Li Zhang
ByteDance Inc.
Non-EE2: CIIP with subblock-based motion compensation
JVET-AF0170

## Slide 2: Introduction
CIIP in ECM-10.0
  The intra prediction signal is generated with TIMD or PDPC (i.e., CIIP-PDPC)
  The inter prediction signal is generated with a regular merge candidate or a TM-refined merge candidate (i.e., CIIP-TM)
Proposed method
  CIIP with subblock-based motion compensation is presented, where the inter prediction signal of CIIP may be generated based on affine or SbTMVP motion compensation

## Slide 3: Proposed method
CIIP is improved by allowing subblock-based inter prediction
  A subblock-based merge candidate may be used to generate the inter signal of CIIP, where the same subblock-based merge candidate list used by affine and SbTMVP is utilized
  When CIIP flag is true and CIIP-TM flag is false, a subbock-based CIIP flag is signalled
  If subblock-based CIIP flag is true, TIMD is used to generate intra signal by default thus no CIIP-PDPC flag signalled any more

## Slide 4: Simulation results
Experimental results (ECM10.0 as the anchor)
 | Random access Main10 |  | Random access Main10 |  | 
 | Over ECM-10.0 |  | Over ECM-10.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.23% | -0.03% | 102.5% | 93.3%
Class A2 | -0.03%* | 0.02% | -0.10% | 100.5% | 96.9%
Class B | -0.08% | 0.06% | -0.09% | 99.1% | 100.5%
Class C | -0.08% | -0.15% | -0.05% | 100.5% | 100.4%
Class E |  |  |  |  | 
Overall | -0.07% | -0.06% | -0.07% | 100.4% | 98.3%
Class D | -0.06% | 0.07% | -0.13% | 102.0% | 100.7%
Class F | -0.03% | -0.07% | -0.11% | 100.7% | 100.2%
 | Low delay B Main10 |  | Low delay B Main10 |  | 
 | Over ECM-10.0 |  | Over ECM-10.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08%* | 0.00% | -0.33% | 101.2% | 100.5%
Class C | -0.07% | -0.57% | -0.25% | 101.5% | 100.7%
Class E | -0.11% | -0.09% | -0.24% | 100.7% | 100.0%
Overall | -0.08% | -0.21% | -0.28% | 101.2% | 100.4%
Class D | -0.07% | 0.13% | -0.28% | 101.1% | 100.3%
Class F | 0.33% | 0.30% | 0.91% | 102.4% | 102.1%
Class A1/A2 decoder runtime may not be accurate

## Slide 5: Conclusion
CIIP with subblock-based motion compensation is presented
0.07%/0.08% coding gain in RA/LDB configurations with 100.4%/98.3% and 101.2%/100.4% complexity
Recommend to study the proposed method in EE