## Slide 1: Non-EE2: Non-EE2: Sample distance-based weighting for CIIP (JVET-AF0171)
Jie Zhao and Seung Hwan Kim
LG Electronics

## Slide 2: Background
In ECM10’s CIIP mode, the prediction samples are generated by weighting an inter prediction signal, where
  inter prediction signal is predicted using CIIP-TM merge candidate
  intra prediction signal is predicted using TIMD derived intra prediction mode.
If the derived intra mode is an angular mode, the weights (wIntra, wInter) are:
  for near-horizontal modes (2 <= angular mode index < 34), the current block is vertically divided as shown in Figure 1(a);
  for near-vertical modes (34 <= angular mode index <= 66), the current block is horizontally divided as shown in Figure 1(b).
  the (wIntra, wInter) for different sub-blocks are shown in Table 1.
The sub-block index | (wIntra, wInter)
0 | (6, 2)
1 | (5, 3)
2 | (3, 5)
3 | (2, 6)
Table 1. The weights used for CIIP angular modes

## Slide 3: Proposed Method
Trying to improve the CIIP weighting
  In current sub-block based weighting, the weight change at the boundary of sub-blocks are not gradual, so it may cause blocking artefacts, higher residuals and less compression efficiency.
  In addition, categorizing angular modes to only near-horizontal and near-vertical modes are too rough to capture the detailed pixel value variations.
  Propose to use sample distance and finer representation of the angles to derive the weights
The angles are categorized as near-horizontal, near-vertical and near-diagonal three cases.
  near –horizontal : (2 <= angular mode index < 34 - 6),
  near-vertical modes (34+6 < angular mode index <= 66)
  near diagonal (34-6 <= angular mode index <= 34+6)
In our test, the weighs wIntra and wInter are derived as:
  near –horizontal : wIntra = ((width - x) * 64 + 32) / width – 4
  near-vertical modes: wIntra = ((height - y) * 64 + 32) / height – 4
  near diagonal modes: wIntra = ((height - y + width - x) * 64 + 32) / (width + height) - 4;
  wIntra is clipped to within [4, 60], and wInter = 64-wIntra.
  In the above formula, offset 32/width – 4, 32/ height – 4, and 32/ (width + height) – 4 are added. Its effect is to make the weight adaptive to the block size. So for smaller block, it gives more weight to intra. Experiments show that by adding this offset, performance is slightly better.

## Slide 4: Experimental Results
Test follows ECM10 Common Test condition
Small gain -0.03% in RA
It shows that coding efficiency may be improved by modifying how to derive the CIIP weight.
We will further study this approach
 | Random Access Main 10 |  |  |  | 
 | Over ECM-10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.04% | 0.09% | 100.2% | 99.6%
Class A2 | 0.02% | 0.00% | 0.00% | 100.0% | 100.3%
Class B | -0.04% | 0.11% | 0.06% | 100.2% | 100.1%
Class C | -0.04% | -0.03% | -0.02% | 100.1% | 100.3%
Class E |  |  |  |  | 
Overall | -0.03% | 0.04% | 0.03% | 100.1% | 100.1%
Class D | -0.01% | 0.16% | 0.00% | 100.0% | 100.1%
Class F | -0.03% | -0.01% | -0.04% | 99.7% | 99.9%
Class TGM | -0.01% | -0.02% | -0.01% | 99.6% | 99.7%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.04% | -0.27% | -0.10% | 100.8% | 101.7%
Class E | 0.02% | -0.09% | 0.44% | 100.3% | 100.5%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.03% | -0.35% | -0.28% | 99.1% | 101.0%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!