## Slide 1: JVET-AF0184 Non-EE2: Search range optimization for Intra TMP
Gleb Verba, Zhi Zhang, Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction and Proposed method
ECM-10.0: rectangular area
Proposed method:
Square search area with increased multiplier + upper bound :
Axis areas – long narrow rectangular areas beyond the main search rectangle along horizontal and vertical directions.
Cross-shape regions around candidates derived for IBC Merge.

## Slide 3: Area in the proposed design
1
4
0
2
5
3
CTU
CU
hor axis area
ver axis area
IBC Merge candidates
BV areas
32
9
1
4
0
2
5
3
CTU
CU
Current design
Proposed design:
Square search area
Axis areas
IBC Merge cand. areas

## Slide 4: Results
 | All Intra Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | 0.00% | -0.05% | 0.07% | 105.5% | 106.3% | 100.1%
Class A2 | -0.11% | -0.21% | -0.16% | 105.8% | 116.4% | 100.0%
Class B | -0.09% | -0.16% | -0.26% | 105.6% | 114.1% | 100.0%
Class C | -0.03% | -0.09% | 0.06% | 103.5% | 106.6% | 100.0%
Class E | -0.05% | -0.07% | -0.14% | 104.9% | 113.7% | 100.0%
Overall | -0.06% | -0.12% | -0.10% | 105.0% | 111.4% | 100.0%
Class D | 0.02% | 0.02% | 0.00% | 101.7% | 103.1% | 100.0%
Class F | -0.48% | -0.55% | -0.48% | 102.1% | 109.4% | 100.0%
Class TGM | -0.53% | -0.52% | -0.43% | 102.8% | 115.1% | 100.0%

## Slide 5: Areas around IBC Merge candidates ONLY
The added areas is cross-shaped area using IBC Merge BV as center.
The added areas are checked after search areas existing in ECM-10.
Early terminate search: for each added area, if its central square 9x9 does not provide candidates with TM cost lower than a threshold, the rest of the area is skipped.
IBC Merge candidates
BV areas
32
9
1
4
0
2
5
3
CTU
CU

## Slide 6: Results: areas around IBC Merge candidates ONLY
 | All Intra Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | -0.01% | -0.03% | -0.02% | 102.1% | 103.1% | 100.0%
Class A2 | -0.10% | -0.14% | -0.11% | 102.2% | 107.5% | 100.0%
Class B | -0.10% | -0.03% | -0.15% | 101.9% | 106.7% | 100.0%
Class C | -0.02% | 0.01% | 0.04% | 100.3% | 102.5% | 100.0%
Class E | -0.04% | 0.02% | 0.01% | 100.4% | 103.9% | 100.0%
Overall | -0.06% | -0.03% | -0.05% | 101.4% | 104.8% | 100.0%
Class D | 0.01% | -0.11% | 0.02% | 99.5% | 100.5% | 100.0%
Class F | -0.21% | -0.13% | -0.15% | 98.9% | 103.0% | 100.0%
Class TGM | -0.35% | -0.31% | -0.26% | 99.8% | 109.2% | 100.0%