## Slide 1: Non-EE2:enhancements on local illumination compensation
Xiaoyu Xiu, Changyue Ma, Ning Yan, Hong-Jheng Jhu, Che-Wei Kuo, Wei Chen, Xianglin Wang

## Slide 2: Introduction
Local illumination compensation (LIC)
  Addressing the illumination variations in prediction blocks based on one linear model
  The scale and the offset are estimated based on the top and left neighboring reconstructed samples

## Slide 3: Proposal
  Non-local illumination compensation (NLIC)
  One linear model is derived by minimizing the difference between the reconstruction and prediction samples of each inter CU, after it is decoded.
  Up to 6 NLIC candidates, obtained from adjacent and non-adjacent neighbors, are included in the regular/subblock merge list
      The NLIC candidates are reordered with other existing merge candidates
      The final reordered list length is kept unchanged.
  When one NLIC candidate is selected, the associated linear model is used together with its motion.
  LIC with multiple templates
  Two extra LIC template modes, i.e., top-only and left-only, are introduced to the LIC
  Applicable to uni-pred AMVP CUs

## Slide 4: Performance evaluation
  * represents the data including unavailable test points which are pasted from the anchors
  NLIC
 | Random Access Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1* | -0.05% | -0.01% | -0.02% | 99.8% | 102.2% | 100.1%
Class A2* | 0.00% | -0.02% | 0.01% | 100.1% | 101.0% | 100.2%
Class B | -0.11% | -0.03% | -0.08% | 101.4% | 103.1% | 100.2%
Class C | -0.13% | -0.07% | -0.04% | 100.2% | 103.9% | 100.2%
Class E |  |  |  |  |  | 
Overall* | -0.08% | -0.03% | -0.04% | 100.5% | 102.7% | 100.2%
Class D | -0.05% | 0.22% | 0.02% | 100.3% | 101.8% | 100.1%
 | Low delay B Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B* | -0.19% | 0.15% | -0.55% | 100.5% | 101.0% | 99.7%
Class C* | -0.31% | -0.53% | -0.34% | 101.0% | 102.9% | 100.1%
Class E | -0.19% | 0.16% | 0.02% | 102.1% | 102.8% | 100.1%
Overall* | -0.23% | -0.07% | -0.34% | 101.1% | 102.1% | 99.9%
Class D | -0.09% | 0.04% | -0.42% | 101.4% | 101.8% | 100.1%

## Slide 5: Performance evaluation
  * represents the data including unavailable test points which are pasted from the anchors
  NLIC + LIC with multi-template
 | Random Access Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1* | -0.07% | 0.07% | -0.12% | 101.7% | 102.7% | 100.3%
Class A2* | -0.05% | -0.18% | -0.21% | 101.2% | 102.2% | 100.0%
Class B | -0.15% | -0.14% | -0.12% | 103.1% | 102.8% | 100.1%
Class C | -0.17% | -0.18% | -0.04% | 101.4% | 103.1% | 100.2%
Class E |  |  |  |  |  | 
Overall* | -0.12% | -0.12% | -0.12% | 102.0% | 102.7% | 100.1%
Class D | -0.05% | 0.09% | -0.24% | 101.9% | 103.7% | 100.1%
 | Low delay B Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B* | -0.24% | -0.24% | -0.43% | 102.2% | 103.7% | 99.9%
Class C | -0.29% | -0.29% | -0.27% | 101.6% | 104.9% | 100.1%
Class E | -0.29% | 0.12% | -0.22% | 102.5% | 102.5% | 100.1%
Overall* | -0.27% | -0.17% | -0.33% | 102.1% | 103.8% | 100.0%
Class D | -0.04% | -0.08% | -0.65% | 102.8% | 103.9% | 100.1%

## Slide 6: Closing
Proposal
  Non-local illumination compensation (NLIC)
  LIC with multiple templates
  Performance
    RA: {0.12%, 0.12%, 0.12%} BD-rate savings, Enc/Dec: 102.0%/102.7%
    LDB: {0.27%, 0.17%, 0.33%} BD-rate savings, Enc/Dec: 102.1%/103.8%
  Recommendation
  Study the proposed method in the context of EE2