## Slide 1: JVET-AG0110 AhG12: 16 States TCQ with State Exchange
Muhammet Balcilar, Karam Naser, Ya Chen,
Franck Galpin, Fabrice Le Leannec

## Slide 2: Overview
state | quantizer used | next state | 
0 |  | 0 | 2
1 |  | 5 | 7
2 |  | 1 | 3
3 |  | 6 | 4
4 |  | 2 | 0
5 |  | 4 | 6
6 |  | 3 | 1
7 |  | 7 | 5
 | quantizer used |  | 
0 |  | 0 | 2
1 |  | 5 | 7
2 |  | 1 | 3
3 |  | 6 | 4
4 |  | 2 | 0
5 |  | 4 | 6
6 |  | 3 | 1
7 |  | 7 | 5
2 Scalar Quantizers
8 states and their transition table
The best trellis path that gives lowest RD cost

## Slide 3: Proposal
Pseudo code
// New state transition
m_prevStates[ 0].checkRdCosts( spt, pqData[0], pqData[2], decisions[0], decisions[2]);
m_prevStates[ 1].checkRdCosts( spt, pqData[3], pqData[1], decisions[5], decisions[7]);
m_prevStates[ 2].checkRdCosts( spt, pqData[0], pqData[2], decisions[1], decisions[3]);
m_prevStates[ 3].checkRdCosts( spt, pqData[3], pqData[1], decisions[6], decisions[4]);
m_prevStates[ 4].checkRdCosts( spt, pqData[0], pqData[2], decisions[10], decisions[8]);
m_prevStates[ 5].checkRdCosts( spt, pqData[3], pqData[1], decisions[12], decisions[14]);
m_prevStates[ 6].checkRdCosts( spt, pqData[0], pqData[2], decisions[11], decisions[9]);
m_prevStates[ 7].checkRdCosts( spt, pqData[3], pqData[1], decisions[15], decisions[13]);
m_prevStates[ 8].checkRdCosts( spt, pqData[0], pqData[2], decisions[8], decisions[10]);
m_prevStates[ 9].checkRdCosts( spt, pqData[3], pqData[1], decisions[13], decisions[15]);
m_prevStates[10].checkRdCosts( spt, pqData[0], pqData[2], decisions[9], decisions[11]);
m_prevStates[11].checkRdCosts( spt, pqData[3], pqData[1], decisions[14], decisions[12]);
m_prevStates[12].checkRdCosts( spt, pqData[0], pqData[2], decisions[2], decisions[0]);
m_prevStates[13].checkRdCosts( spt, pqData[3], pqData[1], decisions[4], decisions[6]);
m_prevStates[14].checkRdCosts( spt, pqData[0], pqData[2], decisions[3], decisions[1]);
m_prevStates[15].checkRdCosts( spt, pqData[3], pqData[1], decisions[7], decisions[5]);
// state exchange if decided to apply
for (int i=0;i<8;i++)
{
if (decisions[i+8].rdCost<decisions[i].rdCost)
std::swap(decisions[i+8],decisions[i]);
}
state | quantizer used | next state | 
0 |  | 0 | 2
1 |  | 5 | 7
2 |  | 1 | 3
3 |  | 6 | 4
4 |  | 10 | 8
5 |  | 12 | 14
6 |  | 11 | 9
7 |  | 15 | 13
8 |  | 8 | 10
9 |  | 13 | 15
10 |  | 9 | 11
11 |  | 14 | 12
12 |  | 2 | 0
13 |  | 4 | 6
14 |  | 3 | 1
15 |  | 7 | 5
 | quantizer used |  | 
0 |  | 0 | 2
1 |  | 5 | 7
2 |  | 1 | 3
3 |  | 6 | 4
4 |  | 10 | 8
5 |  | 12 | 14
6 |  | 11 | 9
7 |  | 15 | 13
8 |  | 8 | 10
9 |  | 13 | 15
10 |  | 9 | 11
11 |  | 14 | 12
12 |  | 2 | 0
13 |  | 4 | 6
14 |  | 3 | 1
15 |  | 7 | 5
No changes on SQs
New states and their transitions
Some changes in the code

## Slide 4
Simulation results
 | Random Access Main 10 |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | -0.05% | -0.18% | 0.05% | 101.3% | 98.2% | 101.7%
Class A2 | -0.09% | -0.11% | -0.09% | 101.4% | 98.3% | 102.5%
Class B | -0.11% | 0.08% | 0.06% | 100.2% | 99.9% | 100.4%
Class C | -0.06% | -0.14% | -0.18% | 101.0% | 100.0% | 100.9%
Class E |  |  |  |  |  | 
Overall | -0.08% | -0.07% | -0.04% | 100.9% | 99.3% | 101.2%
Class D | -0.08% | -0.30% | -0.42% | 101.8% | 100.8% | 100.5%
Class F | -0.02% | 0.00% | -0.24% | 102.2% | 103.5% | 101.1%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #DIV/0!
 | Low delay B Main 10 |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B* | -0.18% | 0.65% | 0.24% | 100.8% | 101.8% | 100.6%
Class C | -0.05% | 0.36% | -0.58% | 102.8% | 99.7% | 100.9%
Class E | -0.22% | 0.86% | -0.51% | 99.0% | 98.9% | 104.1%
Overall | -0.15% | 0.61% | -0.22% | 101.0% | 100.3% | 101.6%
Class D | -0.22% | 0.10% | -0.91% | 101.8% | 100.4% | 99.1%
Class F | -0.29% | -0.05% | 0.30% | 102.9% | 98.6% | 100.8%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #DIV/0!

## Slide 5: Conclusion
AI configuration results do not show good trade-off and the tool is disabled for it.
Simple changes in the code.
Brings consistent gain on CTC sequences.
Propose to study in next EE round.