## Slide 1: Non-EE2: CCALF with Chroma Fixed Filter Input JVET-AH0062
Nan Song, Zhenyu Dai, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction – CCALF filter shape in current ECM
Cross 9x9 (0…21) for SAO Luma Input
Cross 3x3 (22…26) for Luma Residual Input

## Slide 3: Proposed – CCALF with Chroma Fixed Filter Input
Cross 9x9 (0…21) for SAO Luma Input
Cross 3x3 (22…26) for Luma Residual Input
Cross 3x3 (27, 28) for ALF Fixed Filter Chroma Input

## Slide 4: Simulation results
Proposed method vs ECM-12.0
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.02% | -0.52% | -0.66% | 99.5% | 101.6% | 100.0% | 100.0%
Class A2 | 0.02% | -0.84% | -1.15% | 99.8% | 101.6% | 100.0% | 100.0%
Class B | 0.02% | -1.21% | -1.16% | 100.0% | 101.4% | 100.0% | 100.0%
Class C | 0.01% | -0.19% | -0.16% | 100.5% | 101.4% | 100.0% | 100.0%
Class E | 0.02% | -0.35% | -0.59% | 100.2% | 101.7% | 100.0% | 100.0%
Overall | 0.02% | -0.66% | -0.76% | 100.0% | 101.5% | 100.0% | 100.0%
Class D | 0.01% | -0.19% | -0.13% | 100.6% | 101.6% | 100.0% | 100.0%
Class F | 0.03% | -0.36% | -0.32% | 100.0% | 100.7% | 100.0% | 100.0%
Class TGM |  |  |  |  |  |  | 
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | 0.02% | -0.87% | -0.64% | 100.0% | 99.9% | 100.3% | 99.8%
Class C | 0.03% | -0.09% | -0.06% | 99.7% | 99.5% | 100.2% | 100.0%
Class E |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  | 
Class D | 0.01% | -0.19% | -0.17% | 99.8% | 100.4% | 100.1% | 100.0%
Class F |  |  |  |  |  |  | 
Class TGM |  |  |  |  |  |  | 

## Slide 5: Conclusions
This contribution proposes to add additional taps in CCALF and use the chroma ALF fixed filter’s output as the input for these new taps to further improve CCALF. The simulation results show that the proposed method can improve the coding efficiency of ECM. It is suggested to further study this method in EE2.
Thanks to Qualcomm and Nokia for cross-checking!