## Slide 1: AHG12: Eliminating division operations in DIMD and TIMD
Sharp Corporation
Zheming Fan
Takeshi Chujoh Tomohiro Ikai
JVET-AH0072

## Slide 2: Background
Location-dependent weighting method is used in DIMD and TIMD, which involves a considerable number of division operations.
Such operations can be costly for hardware and software implementations.
Copyright © All rights reserved, SHARP CORPORATION
 | TIMD | DIMD
floating-point division | 4 | 2
integer division | [height+1, width*(2*height+1)] （depending on the situation) | [height+1, width*(2*height+1)] （depending on the situation)
In my contribution, it is proposed to replace all the division operations in DIMD/TIMD with the existing lookup table method.

## Slide 3: Proposal
An existing lookup table method is used in DIMD and TIMD to replace division operations. Approximations for Gx/Gy can be calculated as follows:
Copyright © All rights reserved, SHARP CORPORATION
x = Floor( Log2( Gy ) )
norm_Gy = ( (Gy << 5 >> x ) & 31
v = DivSigTable[ normDiff ] | 16
x += (norm_s1 != 0)
shift = x + 4
result = (Gx * v ) >> shift
where
DivSigTable[32] = { 0, 15, 14, 13, 12, 12, 11, 10, 10, 9, 8, 8, 7, 7, 6, 6, 5, 5, 4, 4, 4, 3, 3, 3, 2, 2, 2, 1, 1, 1, 0, 0 }
x = Floor( Log2( Gy ) )
norm_Gy = ( (Gy << 4 >> x ) & 15
v = DivSigTable[ normDiff ] | 8
x += (norm_s1 != 0)
shift = x + 3
result = (Gx * v ) >> shift
where
DivSigTable[16] = { 0, 7, 6, 5 ,5, 4, 4, 3, 3, 2, 2, 1, 1, 1, 1, 0 }
Using a table of length 16
(already used in ECM)
Using a table of length 32

## Slide 4: Results
Copyright © All rights reserved, SHARP CORPORATION
Test2(table_32)
Test1(table_16)
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.08% | 0.15% | 0.16% | 99.3% | 100.6% | 100.7% | 100.0%
Class A2 | 0.04% | 0.05% | 0.03% | 100.4% | 101.3% | 98.8% | 99.8%
Class B | 0.03% | 0.08% | 0.07% | 99.7% | 100.8% | 102.0% | 100.1%
Class C | 0.04% | 0.00% | 0.13% | 99.4% | 101.3% | 100.0% | 100.0%
Class E | 0.06% | 0.04% | -0.11% | 100.3% | 101.1% | 99.0% | 100.0%
Overall | 0.05% | 0.06% | 0.06% | 99.8% | 101.0% | 100.3% | 100.0%
Class D | 0.00% | 0.34% | -0.15% | 100.2% | 100.8% | 100.0% | 100.0%
Class F | 0.00% | -0.08% | -0.04% | 100.4% | 101.4% | 100.8% | 100.1%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.02% | 0.17% | 0.00% | 100.2% | 100.4% | 100.2% | 100.0%
Class A2 | 0.00% | -0.11% | 0.18% | 100.3% | 99.4% | 99.4% | 100.0%
Class B | 0.01% | 0.18% | -0.19% | 100.3% | 99.2% | 100.0% | 100.0%
Class C | 0.05% | -0.02% | 0.09% | 100.4% | 99.9% | 100.0% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | 0.02% | 0.06% | 0.00% | 100.3% | 99.6% | 99.9% | 100.0%
Class D | 0.03% | -0.31% | 0.01% | 100.6% | 100.2% | 100.2% | 100.0%
Class F | -0.06% | -0.39% | -0.09% | 99.6% | 100.0% | 100.3% | 100.0%
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.02% | 0.06% | 0.01% | 99.6% | 101.0% | 100.8% | 100.0%
Class A2 | 0.00% | 0.08% | 0.03% | 100.9% | 101.8% | 100.7% | 99.9%
Class B | 0.00% | 0.09% | 0.07% | 100.5% | 100.4% | 101.1% | 100.2%
Class C | 0.01% | 0.01% | 0.07% | 99.6% | 101.0% | 100.0% | 100.0%
Class E | 0.02% | 0.16% | -0.10% | 100.4% | 101.4% | 100.2% | 100.0%
Overall | 0.01% | 0.08% | 0.03% | 100.2% | 101.0% | 100.6% | 100.0%
Class D | -0.02% | 0.15% | 0.05% | 100.1% | 100.9% | 100.0% | 100.0%
Class F | -0.02% | 0.12% | -0.05% | 99.9% | 100.7% | 101.2% | 99.9%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.01% | 0.02% | 0.05% | 100.1% | 100.3% | 100.1% | 100.0%
Class A2 | 0.04% | 0.03% | 0.05% | 100.9% | 99.4% | 99.5% | 100.0%
Class B | -0.01% | 0.11% | 0.03% | 99.8% | 98.6% | 100.0% | 100.0%
Class C | 0.04% | 0.07% | 0.14% | 100.5% | 100.3% | 100.0% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | 0.02% | 0.07% | 0.07% | 100.3% | 99.5% | 99.9% | 100.0%
Class D | 0.01% | 0.09% | 0.09% | 100.1% | 100.1% | 100.2% | 100.0%
Class F | 0.05% | -0.06% | -0.08% | 99.9% | 99.5% | 100.1% | 100.0%

## Slide 5: Conclusion
Removing the floating-point and integer division operation in DIMD and TIMD.
We observed results as follow without change in runtime.
No significant loss and no significant difference between test1 and test2.
Test1: [0.05%, 0.02%] loss in AI and RA. Test2: [0.01%, 0.02%] loss in AI and RA.
Thanks oppo and ericsson for crosschecking
Copyright © All rights reserved, SHARP CORPORATION