## Slide 1: JVET-AH0081 EE1-1.3: Training from scratch for the joint LOP model with inputs transformed
Du Liu, Jacob Ström, Mitra Damghanian, Per Wennersten (Ericsson)
Dmytro Rusanovskyy, Yun Li, Marta Karczewicz (Qualcomm)
Tong Shao, Peng Yin, Sean McCarthy (Dolby)
Jay N. Shingala, Ajay Shyam, Ajat Suneja, Siddarth P. Badya (Ittiam)

## Slide 2: Overview
EE1-1.3 trains the model in EE1-1.2 from scratch
  The model in EE1-1.2 uses transformed inputs on top of EE1-1.1
  Complexity: 16.9 kMAC/pixel, 0.21M parameters
  (Ref) LOP: 17.1 kMAC/pixel, 0.05M parameters
  (Ref) EE1-1.1: 17.0 kMAC/pixel, 0.05M parameters
Three stages of training are performed
Performance of stage 3 int16 model vs. NNVC-8.0: RA {-0.71%, -0.96%, -0.09%}, AI {-0.44%, -1.71%, -1.16%}
Performance vs. EE1-1.2: RA {-0.26%, -1.03%, -1.15%}, AI {-0.15%, -0.64%, -0.67%}
Performance vs. EE1-1.1: RA {-0.37%, -2.52%, -1.55%}, AI {-0.36%, -3.10%, -2.45%}

## Slide 3: Proposed inputs with DCT transform
Current
Proposed inputs using 2x2 DCT
RecEXTY
RecEXTUV
2↑
Rec
conv 3x3, d1
144x144x3
144x144x1
72x72x2
…
144x144xd1
RecEXTY
RecEXTUV
2↑
DCT-II
conv 3x3, d1
72x72x6
144x144x1
72x72x2
…
2↓
Rec
72x72x4
72x72x2
72x72xd1

## Slide 4: Architecture of EE1-1.2 and EE1-1.3
RecEXTY
[C1,h,w]
Back Bone Block C1
[C1,h,w]
sCONV 1  3 CC21
CONV 1  1 C1C
sCONV 3  1 C21C
CONV 1  1 CC1
PReLU
Rec [6]
Pred [6]
BS [6]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV
1  1, C
PReLU
CONV 11, C
Rec Y
Rec UV [2]
RecEXT UV [2]
2, 2
Crop
NY
Crop
IPB [4]
CONV 11,d5
NUV
Back Bone Block, CY1
Back Bone Block, CY1
...
CONV 33 CY16
Pixel Shuffle
sCONV 13 CYCY21
sCONV 31 CY21CY
CONV 11 CYCY
PReLU
Back Bone Block, CUV1
Back Bone Block, CUV1
...
CONV 33 CUV8
sCONV 13 CUVCUV21
sCONV 31 CUV21CUV
CONV 11 CUVCUV
PReLU
IDCT
IDCT
CONV 11 CUVCUV1
CONV 11 CYCY1
CONV 11 CUV1CUV
CONV 11 CY1CY
sCONV2 13, C
sCONV2 31, C
DCT
Architecture changes compared to LOP2

## Slide 5: Complexity
Spatial resolution inside the network is reduced by a factor of 4 , while the final output still has 128x128 pixels
Complexity is reduced by a factor of four
Further adjustment to meet 17 kMAC/pixel of LOP
Head d1: 12  16 d2: 8 d3: 4 d4: 2 d5: 2 C: 24  64 | Backbone NY: 14 NUV: 4 CY: 16  32 CUV: 16  32 CY1: 64  144 CUV1: 32  128 C21: 16  32
16.9 kMAC/pixel
Parameters 205108 (0.2M)

## Slide 6: Training from scratch
Stage1
  Data generation: (AI) DIV2K dataset (same as LOP and HOP)
  Training model: JVET-AG0069-s1 model (LOP + trans. input), 16.9 kMAC/pixel
  Training parameters: batch size 128, lr 4e-4, 130 epochs, YUV 6:1:1, milestones [120, 123, 126]
  Performance: AI {-5.13%, -13.99%, -14.12%} (NNVC-7.1) over VTM
Stage2
  Data generation: (RA) BVI and TVD dataset using JVET-AG0069-s1
  Training model: JVET-AG0069-s2 model, 16.9 kMAC/pixel
  Training parameters: batch size 128, lr 4e-4, 60 epochs, YUV 6:1:1, milestones [55, 57, 58]
  Performance: RA {-5.43%, -15.27%, -13.69%} AI {-5.07%, -13.71%, -13.94%} (NNVC-7.1) over VTM
Stage3
  Data generation : (RA) BVI and TVD dataset using JVET-AG0069-s2
  Training model: EE1-1.2 model, 16.9 kMAC/pixel
  Training parameters: batch size 64, lr 4e-4, 60 epochs, YUV 12:1:1, milestones [41, 51, 55]

## Slide 7: Results over NNVC-8.0 (NNIntra + LOP)
The proposed float model (NNIntra on) vs. NNVC-8.0 float
The proposed int16 model (NNIntra on) vs. NNVC-8.0 int16
 | Random access |  | 
 | BD-rate Over NNVC-8.0 float anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.07% | -3.64% | -2.35%
Class A2 | -1.01% | -1.34% | 1.36%
Class B | -0.61% | -1.43% | 0.29%
Class C | -0.35% | 0.05% | 1.63%
Class E |  |  | 
Overall | -0.71% | -1.46% | 0.33%
Class D | 0.19% | 0.89% | 2.55%
Class F | -0.08% | 2.55% | 3.07%
 | All Intra |  | 
 | BD-rate Over NNVC-8.0 float anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.68% | -2.46% | -3.01%
Class A2 | -0.44% | -1.73% | 0.05%
Class B | -0.37% | -1.68% | -1.43%
Class C | -0.07% | -0.07% | 0.80%
Class E | -0.43% | -3.04% | -2.29%
Overall | -0.38% | -1.69% | -1.09%
Class D | 0.21% | 0.60% | 2.82%
Class F | 0.12% | 2.26% | 1.87%
 | Low delay B |  | 
 | BD-rate Over NNVC-8.0 float anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.63% | -2.26% | 3.48%
Class C | -0.23% | -2.76% | 3.23%
Class E | -0.25% | -5.40% | 4.55%
Overall | -0.40% | -3.21% | 3.66%
Class D | 0.24% | -3.71% | 2.56%
Class F | 0.03% | 2.05% | 4.03%
 | Random access |  | 
 | BD-rate Over NNVC-8.0 int anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.21% | -2.82% | -2.72%
Class A2 | -1.06% | -0.65% | 0.90%
Class B | -0.59% | -0.97% | -0.24%
Class C | -0.22% | 0.20% | 1.33%
Class E |  |  | 
Overall | -0.71% | -0.96% | -0.09%
Class D | 0.23% | 0.60% | 2.41%
Class F | -0.09% | 2.45% | 3.09%
 | All Intra |  | 
 | BD-rate Over NNVC-8.0 int anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.05% | -2.47% | -3.25%
Class A2 | -0.45% | -1.85% | 0.06%
Class B | -0.39% | -1.70% | -1.51%
Class C | -0.01% | -0.09% | 0.78%
Class E | -0.47% | -3.02% | -2.31%
Overall | -0.44% | -1.71% | -1.16%
Class D | 0.30% | 0.54% | 2.58%
Class F | 0.21% | 2.19% | 2.01%
 | Low delay B |  | 
 | BD-rate Over NNVC-8.0 int anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.48% | -2.04% | 3.74%
Class C | -0.14% | -2.19% | 3.29%
Class E | -0.07% | -3.73% | 4.51%
Overall | -0.26% | -2.51% | 3.78%
Class D | 0.23% | -3.96% | 4.15%
Class F | 0.06% | 2.68% | 5.95%

## Slide 8: Results over EE1-1.2 and EE1-1.1
The proposed int16 model vs. EE1-1.2 (NNIntra on)
The proposed int16 model vs. EE1-1.1 (NNIntra on)
 | Random access |  | 
 | BD-rate Over EE1-1.2 |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.26% | -1.05% | -0.85%
Class A2 | -0.26% | -1.14% | -0.86%
Class B | -0.23% | -0.75% | -1.06%
Class C | -0.29% | -1.27% | -1.70%
Class E |  |  | 
Overall | -0.26% | -1.03% | -1.15%
Class D | -0.36% | -2.20% | -1.99%
Class F | -0.01% | 0.19% | -0.73%
 | All Intra |  | 
 | BD-rate Over EE1-1.2 |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.37% | -0.71% | -0.28%
Class A2 | -0.03% | -0.88% | -0.68%
Class B | -0.10% | -0.49% | -0.62%
Class C | -0.10% | -0.49% | -0.80%
Class E | -0.20% | -0.81% | -0.96%
Overall | -0.15% | -0.64% | -0.67%
Class D | -0.12% | -0.70% | -0.72%
Class F | 0.13% | 0.66% | 0.02%
 | Low delay B |  | 
 | BD-rate Over EE1-1.2 |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.28% | -5.85% | -2.08%
Class C | -0.39% | -4.53% | -3.75%
Class E | -0.35% | -7.61% | -3.86%
Overall | -0.33% | -5.85% | -3.08%
Class D | -0.35% | -6.97% | -4.03%
Class F | 0.02% | -0.08% | -1.65%
 | Random access |  | 
 | BD-rate Over EE1-1.1 |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.17% | -3.95% | -2.14%
Class A2 | -0.60% | -2.47% | -0.66%
Class B | -0.19% | -2.79% | -2.28%
Class C | 0.18% | -1.16% | -0.85%
Class E |  |  | 
Overall | -0.37% | -2.52% | -1.55%
Class D | 0.63% | -0.61% | 0.33%
Class F | 0.11% | 1.26% | 1.11%
 | All Intra |  | 
 | BD-rate Over EE1-1.1 |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.14% | -3.94% | -3.41%
Class A2 | -0.42% | -2.91% | -1.17%
Class B | -0.25% | -2.87% | -2.62%
Class C | 0.10% | -2.02% | -1.13%
Class E | -0.31% | -4.27% | -4.24%
Overall | -0.36% | -3.10% | -2.45%
Class D | 0.43% | -1.29% | 0.40%
Class F | 0.26% | 0.41% | 1.24%

## Slide 9: Conclusions
The model architecture is the same as EE1-1.2, which combines transformed inputs and EE1-1.1
The model is trained from scratch
The proposed model has a complexity of 16.9 kMAC/pixel and 0.2M parameters
BD-rate PSNR impact
  Over NNVC-8.0 int16 is RA {-0.71%, -0.96%, -0.09%}, AI {-0.44%, -1.71%, -1.16%}
  Over EE1-1.2 is RA {-0.26%, -1.03%, -1.15%}, AI {-0.15%, -0.64%, -0.67%}
  Over EE1-1.1 is RA {-0.37%, -2.52%, -1.55%}, AI {-0.36%, -3.10%, -2.45%}
It is proposed to adopt the proposed model into NNVC
Thanks to Nokia for training and inference crosscheck!