## Slide 1: JVET-AH0082 Non-EE2: GPM with CCCM for intra chroma prediction
Yongkai Huo, Yutian Liu (Transsion)

## Slide 2: Introduction
GPM splits a block into two non-rectangular partitions, which may be predicted independently.
CCCM predicts chroma samples from reconstructed luma samples using a 7-tap filter. The current 6 CCCM modes.
  Single-model CCCM from above and left templates
  Single-model CCCM from above template
  Single-model CCCM from left template
  Multi-model CCCM from above and left templates
  Multi-model CCCM from above template
  Multi-model CCCM from left template
  This proposal combines GPM with CCCM.

## Slide 3: Proposal
Combines GPM with CCCM for intra chroma prediction
Each chroma block is split into two partitions and both partitions are predicted using a CCCM mode.
For each block, 64 partition modes are designed consisting of 8 partitioning angles each with 8 partitioning shifts, while only the “LM_CHROMA_IDX” and “MMLM_CHROMA_IDX” are allowed for predicting the chroma partitions.
Usage of the mode is signalled with a CABAC coded PU level flag, followed by a maximum of truncated binary coded 6 bits indicating the partitioning mode.
Example of two CCCM partitions

## Slide 4: Results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0.02% | -0.34% | -0.29% | 1.09 | 0.99 | 0.99 | 1.00
Class C | -0.01% | -0.31% | -0.13% | 1.13 | 1.00 | 1.00 | 1.00
Class E | -0.05% | 0.00% | -0.15% | 1.14 | 1.00 | 1.01 | 1.00
Overall |  |  |  |  |  |  | 
Class D | -0.01% | -0.23% | -0.32% | 1.09 | 0.99 | 1.01 | 1.00
Class F | -0.03% | -0.32% | -0.47% | 1.07 | 0.99 | 1.03 | 1.00
Class TGM |  |  |  |  |  |  | 

## Slide 5: Conclusion
Combines GPM with CCCM for intra chroma prediction
Simulation proves that performance gain may be achieved and the imposed complexity may be further decreased.
It is recommended to study the proposal in the next round of EE2.

## Slide 6: Thanks
www.transsion.com