## Slide 1: JVET-AH0083 AHG12: Additional TIMD mode with a different cost metric
Döne Buğdaycı Şanslı, Saverio Blasi, Jani Lainema
April 2024

## Slide 2
Introduction
TIMD
ECM supports Template based intra mode derivation (TIMD).
Sum of Absolute Transform Differences (SATD) is used as the cost metric.
Above template has a height of 2 for blocks with height less than or equal to 8, and 4 otherwise.
Left template has a width of 2 for blocks with width less than or equal to 8, and 4 otherwise.
A number of modes are tested including MPMs, DC, HOR, VER, wide angle etc.

## Slide 3
Proposed Method
Additional TIMD mode – TIMD SAD
An additional TIMD mode is proposed to be signaled as a sub mode of TIMD.
Main difference with original TIMD is in the way the modes are derived.
  SATD is replaced with Mean Removed SAD as the cost metric.
  Above and Left template height and width are doubled.
  List of modes that are tested are modified to exclude the modes selected by original TIMD mode.
Fusion of derived TIMD modes and weight derivation parts are left unchanged.

## Slide 4
Experimental Results
Proposal against ECM-12.0 anchor
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.12 % | 0.06 % | 0.02 % | 103.2% | 100.9% | 100.5% | 100.0%
Class A2 | -0.06 % | 0.06 % | 0.03 % | 102.7% | 99.9% | 100.6% | 100.1%
Class B | -0.10 % | 0.10 % | 0.03 % | 104.2% | 100.5% | 98.7% | 100.0%
Class C | -0.07 % | 0.00 % | 0.09 % | 103.8% | 101.1% | 100.3% | 99.8%
Class E | -0.05 % | 0.08 % | -0.20 % | 104.1% | 100.8% | 100.0% | 99.9%
Overall | -0.08 % | 0.06 % | 0.01 % | 103.7% | 100.6% | 99.9% | 99.9%
Class D | -0.10 % | 0.15 % | -0.12 % | 105.5% | 97.6% | 100.0% | 99.8%
Class F | 0.00 % | 0.17 % | -0.02 % | 103.9% | 100.3% | 100.0% | 99.9%
Class TGM |  |  |  |  |  |  | 
Random Access Main 10 |  |  |  |  |  | 
Over ECM-12.0 |  |  |  |  |  | 
Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
-0.05 % | 0.00 % | -0.17 % | 101.5% | 98.6% | 99.8% | 100.1%
-0.01 % | -0.08 % | -0.05 % | 102.3% | 99.6% | 99.4% | 99.2%
0.00 % | 0.03 % | 0.07 % | 101.7% | 102.0% | 98.9% | 99.6%
-0.03 % | -0.09 % | 0.03 % | 101.6% | 99.0% | 98.0% | 100.2%

## Slide 5
Experimental Results
Combination with EE2 2.1 EE2 2.1 (results from EE document)
JVET-AH0083 + EE2 2.1 ( TIMD merge tool )
All Intra Main 10 |  |  |  |  |  | 
Over ECM-12.0 |  |  |  |  |  | 
Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
-0.07 % | -0.06 % | 0.11 % | 99.7% | 95.0% | 100.9% | 100.5%
-0.10 % | -0.01 % | -0.04 % | 98.7% | 98.3% | 101.2% | 100.5%
-0.09 % | 0.02 % | -0.01 % | 101.1% | 97.2% | 103.1% | 100.3%
-0.06 % | -0.02 % | 0.09 % | 101.6% | 104.0% | 100.4% | 100.2%
-0.04 % | 0.06 % | 0.12 % | 101.2% | 103.5% | 100.2% | 100.2%
-0.07 % | 0.00 % | 0.05 % | 100.6% | 99.5% | 101.3% | 100.3%
-0.08 % | 0.03 % | 0.14 % | 99.1% | 100.9% | 100.2% | 100.1%
-0.04 % | 0.16 % | -0.01 % | 100.6% | 101.8% | 100.8% | 100.3%
0.00 % | 0.02 % | -0.14 % | 93.7% | 92.8% | 99.8% | 100.3%
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.18 % | 0.01 % | 0.06 % |  |  | 100.5% | 100.4%
Class A2 | -0.15 % | 0.01 % | -0.08 % |  |  | 100.5% | 100.6%
Class B | -0.17 % | 0.09 % | 0.04 % |  |  | 98.3% | 100.4%
Class C | -0.13 % | 0.13 % | 0.14 % |  |  | 100.1% | 100.0%
Class E | -0.07 % | 0.17 % | 0.09 % |  |  | 100.4% | 100.0%
Overall | -0.14 % | 0.08 % | 0.05 % |  |  | 99.8% | 100.3%
Class D | -0.12 % | 0.25 % | 0.02 % |  |  | 100.5% | 99.8%
Class F | -0.03 % | 0.14 % | 0.10 % |  |  | 100.3% | 100.1%
Class TGM |  |  |  |  |  |  | 

## Slide 6
Summary
An additional TIMD mode is proposed.
Consistent coding efficiency gains (average -0.08% luma AI gains) with room to improve runtime (No optimization in the current implementation).
Orthogonal to the TIMD related EE test.
It is proposed to study the technique in the next round of EEs.