## Slide 1: JVET-AH0100 EE1-4.2-related: Multiple scaling ratios coding for NNVC with NNSR Zhuoyi lv, Chuan Zhou vivo Mobile Communication Co., Ltd

## Slide 2
Encoder strategy for supporting multi-scaling ratios
s=1.5 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.27% | 0.19% | 1.28% | -2.72% | 0.02% | 0.74%
Class A2 | -2.65% | 7.00% | 7.92% | -1.19% | 6.95% | 6.65%
Overall | -0.65% | 1.20% | 1.53% | -0.78% | 1.39% | 1.48%
s=2, 1.5 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.75% | 4.40% | 4.35% | -3.13% | 1.19% | 2.40%
Class A2 | -1.64% | 12.17% | 12.84% | -0.51% | 8.57% | 8.37%
Overall | -0.56% | 2.76% | 2.86% | -0.73% | 1.95% | 2.15%
s=2 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.48% | 3.38% | 4.33% | -3.06% | 1.25% | 2.77%
Class A2 | -0.85% | 9.15% | 11.64% | 0.09% | 10.28% | 9.82%
Overall | -0.39% | 2.09% | 2.66% | -0.59% | 2.31% | 2.52%
EE1-4.1
Proposed
Multiple scaling ratios coding with RPR
QP offset = -5
QP offset = -4

## Slide 3: Encoder strategy for supporting multi-scaling ratios
Scaling ratio | Coded resolution
2.0 | 0.5
1.5 | 0.67 (2/3)
1.0 | 1.0
Chart: CatRobot
| 0 | 1 | 2 | 3 | 4
QP37 | 0.5 | 0.67 | 0.5 | 0.67 | 0.67
QP32 | 1 | 1 | 1 | 0.5 | 1
QP42 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
Chart: 
| 0 | 1 | 2 | 3 | 4
QP37 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67
QP32 | 1 | 1 | 1 | 0.67 | 1
QP42 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67
EE1-4.1 s=1.5
Proposed
GOP
Example 1: CatRobot
Coded resolution
Coded resolution
GOP

## Slide 4: Encoder strategy for supporting multi-scaling ratios
Scaling ratio | Coded resolution
2.0 | 0.5
1.5 | 0.67 (2/3)
1.0 | 1.0
Example 2: Campfire
Chart: Campfire @ QP42
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Proposed | 0.67 | 1 | 0.67 | 0.67 | 0.67 | 0.67 | 0.5 | 0.67 | 0.5 | 0.5
EE1-4.1 s=1.5 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67
GOP
Coded resolution

## Slide 5
CNN-based super resolution – Model 1
CNN-based super-resolution model in EE1-4.2.
Training configurations for generating compressed training data: Turn on NNLF-LOP2 and NNIntra
Complexity: 13kMAC/pxl, 0.05M
- Sr = 0, scaling ratio = 1.0x
- Sr = 1, scaling ratio = 2.0x
- Sr = 2, scaling ratio = 1.5x

## Slide 6: CNN-based super resolution – Model 2
To further reduce complexity, modifications are made on top of the CNN-based super-resolution model in EE1-4.2.
  The stride of convolution is set to 2 for all input feature extraction layers
  The stride of 2 in the transition layer is removed.
Training configurations for generating compressed training data: Turn on NNLF-LOP2 and NNIntra
Complexity: 12kMAC/pxl, 0.05M
- Sr = 0, scaling ratio = 1.0x
- Sr = 1, scaling ratio = 2.0x
- Sr = 2, scaling ratio = 1.5x

## Slide 7
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -2.07% | 4.00% | 2.95% | -3.59% | 0.40% | 0.27%
Class A2 | -3.60% | 7.06% | 7.75% | -1.46% | 5.68% | 5.45%
Overall | -0.94% | 1.84% | 1.78% | -1.01% | 1.22% | 1.14%
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -2.15% | 3.83% | 3.12% | -3.70% | 0.28% | 0.60%
Class A2 | -3.56% | 6.80% | 7.68% | -1.47% | 5.49% | 5.43%
Overall | -0.95% | 1.77% | 1.80% | -1.03% | 1.16% | 1.21%
Model 1: EE1-4.2 model
Model 2: Proposed model
CNN-based super resolution

## Slide 8: Conclusions
This contribution introduces a generic method for NNVC, which handles multi-scaling ratios in one coding process.
For NNSR model 1, since CNN-based super-resolution model in EE1-4.2 has already been cross-checked in terms of both training and inference, it’s recommended to adopt the encoder strategy + NNSR (EE1-4.2 model) in NNVC.
For NNSR model 2, it is proposed to be investigated in the next round of EE1.
Thanks Bytedance for cross-checking.

## Slide 9
THANK
YOU