## Slide 1: JVET-AH0155 AHG12: Restricting BT CUs to apply QT-like partitioning structure
Waqas Ahmad, Per Wennersten, Kenneth Andersson
Ericsson

## Slide 2: Background
In current version of ECM (ECM-12.0), the BT CUs are allowed to apply QT-like partitioning structure even though the QT split is allowed for such CUs.
This redundant partitioning structure exist in two ways for BT CUs.
  When a square CU is partitioned by BTH split and each subblock is further partitioned by BTV splitting.
  When a square CU is partitioned by BTV split and each subblock is further partitioned by BTH splitting.
BTH
BTV
BTV
BTV
BTH
BTH
CU with size
CU with size
a) BTH split applied on square CU followed by BTV splits on its both subblocks
b) BTV split applied on square CU followed by BTH splits on its both subblocks
Figure 1: BT CUs apply QT-like structure.

## Slide 3
A condition is proposed on BT CUs to restrict applying QT-like structure as shown in figure 2.
The proposed condition is only applied to a square CU for which QT split is allowed.
A new cabac context is added to signal split_cu_flag. The context is used when the binary split is applied on a luma channel CU, and the first block chooses a different binary split compared to binary split selected by its parent CU.
The proposed condition is applied based on maximum CTU size. When maximum CTU size is 256 the proposed condition is applied to 128x128 and 64x64 CUs. The proposed condition is applied to CU sizes 128x128, 64x64 and 32x32 when maximum CTU size is 128.
Proposal
BTH
BTV
BTV
BTV
BTH
BTH
CU with size
CU with size
a) BTH split applied on square CU followed by BTV splits on its both subblocks
b) BTV split applied on square CU followed by BTH splits on its both subblocks
Figure 2: The proposed restriction on BT splitting to disallow QT-like structure.

## Slide 4: Test 1: ECM CTC
 | Random Access Main 10 |  |  |  |  |  | 
 | BD-rate Over ECM-12.0 |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.04% | -0.03% | -0.04% | 99.1% | 100.1% | 99.7% | 99.9%
Class A2* | -0.03% | -0.02% | 0.04% | 99.2% | 99.9% | 99.5% | 100.1%
Class B | -0.05% | -0.02% | -0.23% | 99.2% | 99.9% | 100.0% | 100.1%
Class C | 0.03% | 0.01% | 0.11% | 98.7% | 99.9% | 100.0% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | -0.02% | -0.02% | -0.05% | 99.1% | 99.9% | 99.9% | 100.0%
Class D | -0.02% | -0.14% | 0.16% | 99.3% | 99.9% | 99.9% | 100.0%
Class F | -0.08% | -0.18% | -0.03% | 99.3% | 100.1% | 100.1% | 100.1%
Class TGM | -0.08% | -0.07% | -0.05% | 99.2% | 99.8% | 100.2% | 100.0%
Results
 | All Intra Main 10 |  |  |  |  |  | 
 | BD-rate Over ECM-12.0 |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.01% | 0.02% | 0.04% | 100.1% | 99.9% | 99.9% | 100.2%
Class A2 | 0.00% | -0.02% | -0.01% | 100.0% | 99.9% | 100.0% | 100.0%
Class B | 0.00% | 0.07% | 0.11% | 99.2% | 100.1% | 100.0% | 100.0%
Class C | 0.01% | 0.10% | -0.03% | 99.6% | 99.9% | 99.6% | 100.0%
Class E | 0.00% | -0.03% | 0.05% | 98.9% | 99.6% | 100.1% | 99.9%
Overall | 0.00% | 0.04% | 0.04% | 99.5 | 99.9% | 99.9% | 100.0%
Class D | 0.00% | 0.16% | 0.02% | 99.5% | 100.1% | 99.8% | 100.0%
Class F | 0.03% | -0.14% | -0.01% | 99.7% | 100.0% | 99.1% | 100.0%
Class TGM | -0.02% | 0.00% | -0.10% | 99.6% | 100.1% | 99.1% | 100.1%
 | Low delay B Main 10 |  |  |  |  |  | 
 | BD-rate Over ECM-12.0 |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT | EncVmPeak | DecVmPeak
Class B* | -0.04% | -0.06% | -0.14% | 98.6% | 99.8% | 99.8% | 99.0%
Class C | 0.02% | -0.04% | -0.16% | 98.9% | 99.8% | 99.6% | 100.1%
Class E | 0.01% | 0.24% | 0.48% | 98.6% | 100.0% | 99.4% | 100.2%
Overall | -0.01% | 0.02% | 0.01% | 98.7% | 99.8% | 99.6% | 99.7%
Class D | -0.22% | 0.31% | -0.35% | 99.2% | 99.8% | 99.8% | 100.0%
Class F* | 0.05% | -0.26% | -0.69% | 99.5% | 99.9% | 99.7% | 100.1%
Class TGM* | -0.24% | -0.33% | -0.14% | 99.3% | 99.9% | 100.2% | 100.3%

## Slide 5: Summary
In this contribution, a restriction is proposed on BT CUs to avoid applying QT-like structure when QT split is allowed for such CUs.
A new CABAC context is added to signal split_cu_flag syntax to facilitate the proposed restriction.
The results show a reduction in encoding runtime for AI, RA, and LDB configurations with improvements in coding efficiency for RA and LDB configurations.
It is suggested to study the proposed method in the next cycle of EE2.
Thanks to Sharp for cross-checking.

## Slide 6
Thank you