## Slide 1: JVET-AHxxxx AHG9: Improvements to the film grain regions characteristics SEI message
Shaowei Xie, Ping Wu, Ying Gao, Yaxian Bai, Menghu Jia, Weihong Niu, Cheng Huang (ZTE Corporation)
Apr. 2024

## Slide 2: Introduction
JVET-AG2032: Film grain regions characteristics SEI message
  existing FGC SEI message syntax, and
  elements to describe a list of picture regions.
Observations for FGR application:
  one single “fgr_model_id” for different regions.
  one single “fgr_blending_mode_id” for different regions.
Evaluation results and comments in JVET-AC0199:
  The frequency based FGS method and auto-regressive (AR) based method show different results under different circumstances.
    How to select the proper method for a film grain test video is important.

## Slide 3: Proposed Solution
Proposal #1: Allowing separate “fgr_model_id”
fgr_single_model_flag equal to 1 indicates that the film grain simulation models used in current picture have the same fgr_model_id.
fgr_single_model_flag equal to 0 indicates that the film grain simulation models used in different regions of the current picture may have different fgr_model_id.
fgr_model_id identifies the film grain simulation model as specified in Table 5. The value of fgr_model_id shall be in the range of 0 to 1, inclusive.

## Slide 4: Proposed Solution
Proposal #2: Allowing separate “fgr_blending_mode_id”
fgr_single_blending_mode_flag equal to 1 indicates that the blending modes used to blend the simulated film grains with the input image regions have the same fgr_blending_mode_id.
fgr_single_blendng_mode_flag equal to 0 indicates that the blending modes used to blend the simulated film grains with the input image regions may have different fgr_blending_mode_id.
fgr_blending_mode_id identifies the blending mode used to blend the simulated film grain with the input images as specified in Table 6. fgr_blending_mode_id shall be in the range of 0 to 1, inclusive.

## Slide 5
Conclusion
It is proposed to extend the functionality of the film grain regions characteristics SEI message, through the following two improvement approaches:
  Allowing separate “fgr_model_id” to be applied in different regions, instead of restricting only one single “fgr_model_id” in the whole SEI message.
  Allowing separate “fgr_blending_mode_id” to be applied in different regions, instead of restricting only one single “fgr_blending_mode_id” in the whole SEI message.
Recommend to adopt these improvements into FGR SEI message.

## Slide 6
Thank you