## Slide 1: JVET-AH0181 AHG12: Adaptation of intra/inter LFNST/NSPT for low-delay configuration Charles Bonnineau, Fabrice Le Léannec, Karam Naser, Saurabh Puri, Ismail Marzuki, Renan Utida

## Slide 2: LFNST/NSPT in ECM-12.0
Enabled only in RA and AI
Proposed adaptation for LDB
  LFNST/NSPT for intra in I-frame only
  LFNST/NSPT for inter unchanged
  Encoder only
Tested configurations
  Test 1: LFNST/NSPT ON (ECM-12.0)
  Test 2: Proposed adaptation (ECM-12.0)

## Slide 3: Results
Test 2
Test 1
 | Low delay B Main 10 |  |  |  | 
 | Over ANCHOR |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1.14% | -0.30% | -0.44% | 104.1% | 104.0%
Class C | -1.83% | 0.12% | 0.27% | 105.1% | 104.6%
Class E | -1.39% | 0.25% | -1.62% | 104.2% | 104.1%
Overall | -1.43% | -0.02% | -0.50% | 104.4% | 104.2%
Class D | -1.21% | 0.22% | -0.26% | 103.8% | 103.2%
Class F | -1.07% | -0.28% | -1.40% | 102.3% | 101.3%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main 10 |  |  |  | 
 | Over ANCHOR |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1.31% | -0.44% | -0.61% | 114.2% | 102.3%
Class C | -2.06% | -0.67% | -0.39% | 115.4% | 102.1%
Class E | -1.40% | 0.04% | -1.97% | 109.3% | 100.0%
Overall | -1.58% | -0.40% | -0.88% | 113.4% | 101.6%
Class D | -1.30% | 0.55% | -0.93% | 112.7% | 101.0%
Class F | -1.20% | -1.16% | -1.59% | 109.0% | 100.5%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 4: Conclusion
The proposed adaptation offers -1.43% of average gain with 104.4% EncT compared to ECM-8.0 in LDB.
We recommend adoption of the proposed method in ECM-12.0
Thanks KDDI for crosschecking