## Slide 1: On the requirements and use cases of new-generation video coding standard
Y. Zhao, X. Gu, H. Yang, W. Xu, X. Ma, K. Cai, J. Wang, J. Zhou, J. Sauer, E. Alshina (Huawei)
S. Wenger (Tencent)
F. Le Léannec, K. Naser, F. Galpin, S. Puri, E. Francois (InterDigital)
JVET-AH0199

## Slide 2: Video applications
Entertainment
Productivity
Device collaboration
Video Conferencing
Virtual Desktop Infrastructure (VDI)
…
TV broadcasting
OTT services
  Video on Demand (VoD)
  Live-streaming
Cloud gaming
…
Screen casting (wireless)
  Smartphone to PC
  Laptop to TV
  Laptop to XR glasses
  …
Low latency (E2E < 500 ms)
Ultra low latency (E2E < 50 ms)
 | VoD | Cloud gaming | Video conferencing | VDI
Global Market size (2023), Billion USD | 97.19 | 5.76 | 28.61 | 12.72
Global Market size (2032), Billion USD | 399.05 | 126.62 | 60.17 | 80.82
Compound annual growth rate (CAGR) | 17.0% | 37.9% | 7.8% | 22.8%
Source: https://www.fortunebusinessinsights.com/
67% of VoD in 2032
(more from a consumer application perspective)

## Slide 3: Video applications market trends
4.6
2023 2032
Global Market size, Billion USD
Chart: Compound annual growth rate (CAGR)
| VoD | Cloud gaming | Video conferencing | VDI
CAGR | 0.17 | 0.379 | 0.078 | 0.228
CAGR is the average rate at which some value (investment) grows over a certain period of time
Source: https://www.fortunebusinessinsights.com

## Slide 4: Trends on video applications for entertainment (1)
HDR content is more and more popular
  Premium-quality VoD content in 4K HDR
  More screens support HDR
  Smartphones support HDR recording
  Gaming with HDR
Increased popularity of UGC/PUGC
  User Generated Video (UGC) and Professional User Generated Content (PUGC) content has become part of people’s life
  Deloitte’s study found that a full 60% of Gen Zs surveyed prefer watching UGC videos [2]
[1] https://ultrahdforum.org/climbing-the-ultra-hd-ott-ladder-2/
[2] https://www2.deloitte.com/content/dam/insights/articles/us176942_tmt_digital-media-trends-2024/DI_Digital-media-trends-2024.pdf
Short Video:
…
Long Video:
…
[1]

## Slide 5: Trends on video applications for entertainment (2)
Live-streaming has become very popular
  for product launches and promotion
  for a personal channel/chat room of an influencer
  for gaming streaming
  …
Cloud gaming is developing rapidly
  NVidia GeForce Now, Xbox Cloud Gaming, PlayStation Now, Amazon Luna, Taptap, …
  NVIDIA GeForce NOW had over 25 million users by 2023, but back to 2020 the number is 1 million [1]
  High frame rate, resolution and quality are needed, e.g., GeForce Now requires at least 45Mbps for 4K@120fps [2]
  The major restraining factor is the latency and responsiveness. More users are expected with such issues being mitigated by Internet infrastructure improvement (like 5G and fiber to the home) and more advanced coding and transmission technologies
[1] https://levvvel.com/geforce-now-statistics/
[2] https://www.nvidia.com/en-us/geforce-now/system-reqs/#windows-pc
[3] https://support.apple.com/zh-cn/guide/apple-vision-pro/tanc09caabb3/visionos
Stereoscopic 3D may become popular yet again with new XR devices
  Recently, Apple Vision Pro demonstrates immersive video experience with wide-angle high-resolution stereoscopic 3D video
[3]

## Slide 6: Trends on video applications for productivity
Video conferencing is common in daily life
  Support remote work and collaboration
VDI is growing even faster
  VDI has advantages in elastic computing and storage resources, cloud-based AI assistance, data security, lower capital expense, etc.
  It may not only virtualize Personal Computer (PC) but also smartphone, and works for Cloud-based video production
Unlike VoD, the VDI and Video conferencing (as well as cloud gaming), which involve intensive interaction and require rapid responsiveness, have much higher requirement in end-to-end latency to maintain good service quality
≤ 50 ms end-to-end latency for VDI and cloud gaming
≤ 200 ms end-to-end latency for video conferencing
 | Video conferencing | VDI
Global Market size (2023), Billion USD | 28.61 | 12.72
Global Market size (2032), Billion USD | 60.17 | 80.82
Compound annual growth rate (CAGR) | 7.8% | 22.8%

## Slide 7: Trends on video applications for device collaboration
Multi-device collaboration via wireless connection
[1] https://www.youtube.com/watch?v=EeSTacjfmJw
[2] https://www.youtube.com/watch?v=ShYnwbbU67c
[3] https://support.apple.com/en-hk/102597
[4] https://support.apple.com/zh-cn/guide/apple-vision-pro/tan357ede966/visionos
[5] https://www.benq.com/en-hk/knowledge-center/knowledge/how-to-connect-your-laptop-to-a-tv-wired-and-wireless-options.html
DLNA
AirPlay
Cast+
Miracast
Codecs: H.264/AVC, H.265/HEVC, VP8
…
Control smartphone via Pad/PC [1]
2-in-1 Laptop: Android tablet & Windows PC [2]
Project laptop screen to a meeting room TV [5]
Use a pad as a second screen [3]
Challenge: low latency, packet loss by interference, high quality, low power consumption
See computer screen on XR glasses [4]

## Slide 8: On implementation cost and commercialization
Modern mobile video applications which provide premium class experience to the user are 4K 60+fps
  4K@60fps video recording & playback is common for high-end smartphones nowadays, and is going up to 8K
  Mobile devices have higher resolution screen with the advances of display technology
Mobile devices are sensitive to power consumption and chip area size.
  As was estimated by Hisilicon codec development team, if encoding time is same as HEVC and complexity constrained to operate on middle class Smartphone in real time the VVC encoder would provide around 20-30% bits saving, but hardware area needed for encoder may increase by three times.
  This tradeoff may limit the use of VVC for low delay applications and for devices with limited power capabilities (e.g., smartphone). If a new coding standard provides a similar trade-off, this concern will remain.
It is recommended during exploring and developing video coding standard to more carefully consider the trade-off between coding efficiency, implementation cost and encoding complexity, in the context of low delay coding application scenarios.
Mate X5
2224 x 2496
MatePad Pro
2880 x 1920
MacBook Pro (16 inch)
3456 x 2234
Apple Vision Pro
3660×3200 per eye

## Slide 9: Reality vs Expectation
BQTerrace, Low Delay Encoder
VTM: 5 days  ECM: 14 days
Ultra low delay
E2E 5…50 ms
Vivid Colours
Fast motion
HDR
8K
Complex
Texture

## Slide 10: Suggestions to CTC
New test sequences:
HDR content: It is suggested to add 4K/8K HDR sequences to the CTC as mandatory test sequences. Preferable to use colorful content generated by recent devices, not limiting study to HDR sequences captured almost 10 years ago.
SCC content: Some screen content is outdated compared with the current software/OS UI. To support more versatile applications in VDI besides basic office work, e.g., cloud-based video production, VDI for Computer Aided Design (CAD) like 3D modeling/animation. SCC test sequences should include more challenging sequences in these cases. So far JVET CTC doesn’t have content of this type.
Gaming content: Gaming sequences (as was demonstrated in AhG15) require higher bitrate compare to JVET CTC sequences. Cloud gaming content or live-streaming examples should be a part of the CTC.
Post-production content: Natural test sequences in CTC are mostly the direct output of cameras, while the production of PUGC and PGC (movie/episode) content may further include post production like content composition/transition, chroma keying and color grading. Noise in the raw YUV may be reduced after the post production. Such content is then coded for distribution. Therefore, CTC may include videos with typical post-production processing. Video Clips from real PGC/PUGC content (with complex motion and/or lighting) may be used.
UGC content: The source video segments used to produce the UGC video may be already compressed by H.264/AVC or H.265/HEVC. CTC might further include UGC data.
Test conditions:
The Low Delay configuration may be further combined with low complexity constraint to solicit more advanced coding technologies.
Additional tests outside of CTC:
Nowadays HEVC is widely deployed codec. Regular performance comparison with HEVC (additionally to VVC) gives good understanding for maturity and deployment perspective of technologies developed in JVET.

## Slide 11
Thank you.