## Slide 1: JVET-AH0206
[EE1 related]: Additional inference test for EE1-2.3 to adjust luma-chroma balance
17-24 April 2024
Y. Li , D. Rusanovskyy, M. Karczewicz (Qualcomm)

## Slide 2: Overview
  Integer implementation of HOP In-loop filter with Transformer blocks was proposed in EE1-2.3 (JVET-AH0205).
  Significant coding gain has been obtained compared to HOP3.
  This contribution aims to rebalance the luma-chroma coding gain in inference process by adjusting chroma offset.

## Slide 3: Results of EE1-2.3 (Transformer model)
Proposed (int16) vs. HOP3
Test: EE1-2.3 Transformer model
Anchor1: HOP3
Anchor2: VTM
NNIntra ON for Test and Anchors
Proposed(int 16) vs. VTM
 | AI |  |  | RA |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.15% | -7.73% | -6.56% | -1.30% | -9.43% | -8.81%
Class A2 | -1.16% | -13.04% | -18.18% | -0.66% | -12.59% | -22.58%
Class B | -1.03% | -13.25% | -8.62% | -0.83% | -18.37% | -9.90%
Class C | -0.84% | -3.55% | -4.04% | -1.03% | -2.85% | -3.58%
Class E | -0.90% | -7.30% | -7.50% |  |  | 
Overall | -1.01% | -9.15% | -8.67% | -0.94% | -11.29% | -10.53%
Class D | -0.39% | -3.66% | -4.21% | -0.59% | -4.47% | -4.13%
Class F | -1.11% | -3.18% | -4.26% | -0.44% | -1.08% | -2.47%
 | AI |  |  | RA |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -13.85% | -15.43% | -21.22% | -16.34% | -18.17% | -25.78%
Class A2 | -13.51% | -22.07% | -25.21% | -15.34% | -24.50% | -31.00%
Class B | -12.05% | -21.37% | -18.06% | -13.19% | -29.06% | -21.43%
Class C | -13.02% | -15.91% | -18.44% | -14.31% | -19.65% | -19.71%
Class E | -16.57% | -21.44% | -21.25% |  |  | 
Overall | -13.56% | -19.30% | -20.40% | -14.55% | -23.46% | -23.76%
Class D | -12.18% | -15.05% | -18.72% | -15.06% | -20.68% | -20.41%
Class F | -9.87% | -14.31% | -14.00% | -8.98% | -13.75% | -13.05%

## Slide 4: Proposed method
It is proposed to increase the chroma offset to 2 from 1 when running the NNVC

## Slide 5: Results (Transformer model)
Proposed (int16) vs. HOP3
Test: The proposed
Anchor1: HOP3
Anchor2: VTM
NNIntra ON for Test and Anchors
Proposed(int16) vs. VTM

## Slide 6: Conclusion
Inference is conducted for the EE1-2.3 Transformer model with the adjusted chroma offset (increased from 1 to 2).
Compared to NNVC-8.0 HOP anchor (NNIntra ON),
  AI: {-2.3%, 3.3%, 3.5%} and RA: {-2.3%, 0.7%, 0.6%}.
Compared to VTM
  AI: {-14.6%, -9.1%, -10.5%}, and RA: {-15.7%, -13.5%, -14.3%}
It is proposed to study the proposed method in the next round of EE1.
Thank you to Tencent for the cross-checking.

## Slide 7: Thank you