## Slide 1: JVET-AH0211: Non-EE2: Intra merge mode
Yao-Jen Chang, Vadim Seregin, Marta Karczewicz

## Slide 2: Proposal
Motivation
  Current and neighboring blocks may have similar behavior and the mode selections may be similar or the same
  In ECM, there are inter merge modes and CCP merge mode to reuse the modes from a selected neighbouring block
  Many intra coding tools beyond VVC codec, such as DIMD, TIMD, IntraTMP, TMRL, etc. are employed.
Proposed method
  This contribution proposes to reuse the intra mode used in a selected neighboring block to predict a current coding block.
  A flag is signaled to indicate whether to enable the proposed intra merge mode. A list index is signaled to decide which intra merge list is selected. A candidate index is further signalled to indicate which candidate is used for this CU.

## Slide 3: Example
Example of a candidate list construction: {Cand0, Cand1, Cand2}
Cand0 stores DIMD information {intra angular indexes, weighting factors, location dependency index} retrieved from a neighbour block coded by DIMD mode
Cand1 stores TIMD information {intra angular indexes, weighting factors} retrieved from a neighbour block coded by TIMD mode
Cand2 stores intraTMP fusion information {BVs, weighting factors, LIC info} retrieved from a neighbour block coded by intraTMP fusion mode

## Slide 4: Test results
On top of ECM-12.0
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.19% | 0.11% | 0.01% | 104.6% | 99.4% | 100.1% | 100.1%
Class A2 | -0.20% | 0.01% | -0.03% | 103.6% | 99.2% | 100.1% | 100.1%
Class B | -0.14% | 0.07% | 0.01% | 104.4% | 99.8% | 100.1% | 100.1%
Class C | -0.11% | 0.07% | 0.11% | 104.2% | 99.6% | 99.7% | 100.0%
Class E | -0.05% | -0.04% | 0.01% | 104.3% | 99.2% | 100.1% | 100.0%
Overall | -0.14% | 0.05% | 0.02% | 104.2% | 99.5% | 100.0% | 100.1%
Class D | -0.11% | 0.20% | -0.13% | 104.2% | 101.3% | 99.9% | 100.0%
Class F | -0.07% | 0.25% | -0.10% | 101.6% | 98.9% | 100.1% | 100.0%

## Slide 6: Test results
On top of ECM-12.0
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class B | -0.08% | 0.02% | -0.08% | 100.5% | 99.0% | 100.0% | 100.0%
Class C | -0.01% | 0.03% | 0.06% | 100.7% | 99.5% | 99.5% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | -0.03% | -0.37% | 0.49% | 101.2% | 100.3% | 100.0% | 100.0%
Class F | -0.08% | -0.12% | 0.03% | 100.4% | 100.1% | 100.3% | 99.8%