## Slide 1: JVET-AH0213 Non-EE2: MVP extension
Zhi Zhang, Jian-Liang Lin, Han Huang,
Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction and Proposal
        In ECM-12, for TMVP and SbTMVP, it determines a reference picture and the MV is then scaled accordingly. This contribution proposes to add additional candidates using a selected reference picture with a scaled MV.
        For merge candidates, it adds a candidate with the reference index 1 when the existing candidates has reference index 0, otherwise it adds a candidate with the reference index 0, and a TMVP candidate with a spatial MV offset (as in SbTMVP in ECM-12).
        For TMVP and SbTMVP, it adds a candidate with a reference index corresponding to the collocated block’s reference picture.
        Finally, it adds a bi-TMVP candidate (MV0, MV1 are shown in the next figure) if a motion trajectory between a block in a reference picture and its reference block crosses the current block.

## Slide 3: Simulation Results
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class B | -0.08% | -0.18% | 0.21% | 100.3% | 101.1% | 100.0% | 99.3%
Class C | -0.09% | -0.06% | -0.25% | 100.7% | 100.6% | 99.6% | 100.1%
Class E | -0.09% | -0.87% | -0.23% | 99.7% | 100.4% | 99.9% | 99.1%
Overall | -0.09% | -0.31% | -0.05% | 100.3% | 100.7% | 99.8% | 99.5%
Class D | -0.34% | 0.42% | 0.41% | 100.2% | 101.1% | 99.6% | 100.0%
Class F | -0.03% | 0.12% | -0.69% | 100.2% | 101.0% | 97.5% | 99.7%
Class TGM | -0.22% | -0.09% | -0.03% | 99.1% | 99.8% | 99.7% | 99.2%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.17% | -0.18% | -0.19% | 100.2% | 101.5% | 100.8% | 101.4%
Class A2 | -0.07% | -0.07% | -0.05% | 99.7% | 101.6% | 100.6% | 101.2%
Class B | -0.10% | -0.05% | -0.04% | 100.9% | 102.5% | 100.6% | 102.1%
Class C | -0.17% | -0.20% | -0.09% | 100.9% | 102.0% | 102.2% | 102.0%
Class E |  |  |  |  |  |  | 
Overall | -0.13% | -0.12% | -0.09% | 100.5% | 102.0% | 101.1% | 101.8%
Class D | -0.16% | -0.07% | -0.23% | 98.6% | 102.6% | 102.8% | 102.0%
Class F | -0.12% | -0.12% | -0.17% | 99.7% | 100.1% | 101.5% | 101.8%
Class TGM | -0.01% | 0.00% | -0.06% | 100.1% | 100.6% | 100.9% | 101.6%
1 QP22 point in ClassA1, 2 QP22 and 1 QP27 point in ClassA2 are copied from ECM12 anchor.