## Slide 1: JVET-AH0215 Non-EE2: Adaptive cost function selection in merge mode
Kai Cui, Zhi Zhang, Yan Zhang, Han Huang, Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction and proposal
In ECM: multiple cost functions are defined
  SAD, SATD, SSE, … + mean removal, mean scaled, weighted, ...
  Applied to different tools and different stages
Proposal: use the parity of the merge index to select the cost function for refinement of the merge candidates
  If the merge index is an even number, cost function 1 is selected. Otherwise, cost function 2 is selected
  Bilateral matching merge and affine merge, selected between SATD and SAD
  Template matching merge, selected between weighted SAD and SAD
  The method is not applied to low-delay pictures

## Slide 3: Simulation results
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.06% | 0.00% | -0.24% | 100.9% | 100.5% | 100.1% | 99.9%
Class A2 | -0.07% | -0.06% | -0.08% | 99.9% | 100.1% | 99.9% | 100.0%
Class B | -0.07% | -0.04% | 0.02% | 100.3% | 100.8% | 99.7% | 99.9%
Class C | -0.04% | -0.14% | -0.17% | 99.3% | 100.5% | 99.6% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | -0.06% | -0.06% | -0.10% | 100.1% | 100.5% | 99.8% | 99.9%
Class D | -0.03% | -0.09% | 0.03% | 99.8% | 100.3% | 100.0% | 100.0%
Class F | -0.03% | -0.29% | -0.19% | 100.5% | 100.7% | 100.1% | 99.8%
Class TGM | 0.02% | 0.03% | 0.04% | 100.6% | 99.3% | 99.9% | 100.1%