## Slide 1: AHG7 Statistical analysis of luma and chroma intra tools in ECM versions
Mohsen Abdoli, Ramin G. Youvalari, Alexandre Tissier (Xiaomi)
Karam Naser, Kevin Reuzé, Fabrice Le Léannec (InterDigital)

## Slide 2: Tools
Luma
Intra Block Copy (IBC) for natural content
Intra with Template Matching (IntraTmp)
Decoder-side Intra Mode Derivation (DIMD)
Spatial Geometric Partition Mode (SGPM)
Template-based Intra Mode Derivation (TIMD)
Regular luma Intra Prediction Mode (IPM)
Template-based Multiple Reference Line (TMRL)
Extrapolation filter-based Intra Prediction (EIP)
Matrix-based Intra Prediction (MIP)
Chroma
Regular chroma IPM
Direct Mode (DM)
Chroma DIMD
Cross-Component Linear Model (CCLM)
Convolutional Cross-Component Model (CCCM)
Gradient-based Linear Model (GLM)
Cross Component Prediction (CCP) merge
Direct Block Vector (DBV)
IPM-based
BV-based
Other
IPM-based
Cross-comp
BV-based

## Slide 3: Methodology - Metrics
Tool selection rate:
Granularity:
  Block-wise
  Pixel-wise (normalized)
Block-wise Pixel-wise
1
1
4
8
4
8
Class D (416x240)
Class B (1920x1080)
:
CU
CU

## Slide 4: Methodology - Metrics
Parameters
  ECM version: ECM-1.0 … ECM-12.0
  QP: 22,27,32,37
  CTC class
  Dataset: JVET CTC, BVI-DVC

## Slide 5: ECM gains(*)
(*) Minor inaccuracy due to changes in anchor performance measurement, in particular around ECM-4.0

## Slide 6: Block-wise – ECM versions – Luma
Observations:
Significant drop in regular IPM
(69%  32%)
TIMD and DIMD also have stable behavior
MIP seems to have overlap only with EIP
IntraTmp has a boost at ECM-9.0
IBC accounts for a large gain with a very low selection rate. Reason unclear…

## Slide 7: Block-wise – ECM versions – Chroma
Observations:
Regular IPM not as popular as in luma
Major change of distribution upon adoption of CCCM.
Significant drop in CCLM (52%  8%)
Boost in CCP merge in ECM-12.0

## Slide 8: Block-wise vs. pixel-wise – ECM-12.0 – Luma
How to interpret:
When pixel-wise selection rate is larger, the tool tends to get selected for larger CUs (vice versa)
Reasons:
Normative constraints: tool is enabled for certain CU sizes (e.g. EIP etc.)
Encoder choice: tool is simply more interesting for certain CU sizes
Observations:
IBC, IntraTmp and MIP tend to get selected for larger blocks
TIMD, regular IPM and EIP tend to get selected for smaller blocks
Other tools (DIMD, SGPM and TMRL) do not show any particular tendency

## Slide 9: Block-wise vs. pixel-wise – ECM-12.0 – Chroma
Observations:
Regular IPM tends to be used for smaller blocks.
DBV tends to be used for larger blocks.
DM slightly tends to be used for smaller blocks.
CCP merge slightly tends to be used for larger blocks.
Other tools (DIMD, CCLM, CCCM, GLM) do not show any particular tendency

## Slide 10: Block-wise – CTC classes – ECM-12.0 – Luma
Observations:
All tools mostly stable, except for IntraTmp that has a relatively high fluctuation over different classes.

## Slide 11: Block-wise – CTC classes – ECM-12.0 – Chroma
Observations:
CCCM selection rate tends to increase with the video resolution
CCP merge also has a higher selection rate in large resolutions
DM mode is selected less often in high resolutions

## Slide 12: Block-wise – QP – ECM-12.0 – Luma
Observations:
As QP increases, the regular IPM is selected less often, while TIMD gets selected more frequently.
MIP gets selected more often in high QPs
Other tools seem stable

## Slide 13: Block-wise – QP – ECM-12.0 – Chroma
Observations:
CCCM gets selected less often in higher QPs
CCLM gets more selected in higher QPs
CCP merge gets selected more often in higher QPs

## Slide 14: BVI DVC vs. JVET CTC – ECM-12.0 – Luma
Everything seems pretty stable (good news!)
MIP in particular: By putting together the stable statistics of MIP from earlier, one can roughly conclude that MIP has had reliable matrix training with almost no over-fitting.

## Slide 15: BVI DVC vs. JVET CTC – ECM-12.0 – Chroma
No noticeable difference.
BVI-DVC CTC

## Slide 16: Conclusion
Selection rate of tools (block-wise and pixel-wise) presented under different coding parameters/settings.
Intra tools (luma and chroma) were studied. Some interesting behaviors and patterns have been identified.
Possibly useful when a formal standardization is to be kicked-off.
Many more analysis possible:
Intra in P/B-slices
Inter tools
AHG7 tool-off bitstreams
Any suggestion?
Follow up contributions for next versions of ECM

## Slide 17
Thank you!