## Slide 1: JVET-AH0307 AHG12: Multiple Transform Set Selection for Intra MTS Charles Bonnineau , Karam Naser, Saurabh Puri, Fabrice Le Léannec

## Slide 2: MTSS for MTS
Explicit intra MTS in current ECM
  LUT which maps a transform set to the intra mode of the block
  Each transform set is composed of 6 separable transform pairs candidates
  1, 4 or 6 transform pair candidates are tested depending on the sum of absolute value of transform coefficients
  Some modes derive a VIPM to select a transform set in the LUT
EE2-4.1 proposes MTSS which tests one additional transform set for LFNST/NSPT for some modes using a VIPM

## Slide 3: Proposed method
We propose MTSS for intra MTS for DIMD, TIMD, IntraTMP and EIP modes
  Planar transform set is used as alternative transform set
  The number of candidates in the alternative transform set depends on number of candidates in the initial transform set
A flag is used to signal if the alternative transform set is selected by the encoder
#tr pair candidates in initial tr set | #tr pair candidates in alternative tr set
1 | 1
4 | 2
6 | 3

## Slide 4: Results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.19% | 0.21% | 102.5% | 100.4%
Class A2 | -0.11% | 0.15% | 0.10% | 103.8% | 98.4%
Class B | -0.05% | 0.15% | 0.22% | 103.8% | 97.7%
Class C | -0.03% | 0.16% | 0.20% | 105.0% | 103.6%
Class E | -0.01% | 0.26% | 0.12% | 100.5% | 105.9%
Overall | -0.05% | 0.18% | 0.18% | 103.3% | 100.9%
Class D | -0.07% | 0.35% | 0.17% | 105.9% | 105.9%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
MTSS for intra MTS on top of ECM-12.0

## Slide 5: Combination with MTSS for LFNST/NSPT
Gains are additive with MTSS LFNST/NSPT combinations:
  MTSS MTS + JVET-AH0184 Test1 + JVET-AH0237
 | All Intra Main 10 |  |  |  | 
 | Over ANCHOR |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.18% | 0.27% | 101.5% | 95.5%
Class A2 | -0.17% | 0.15% | 0.13% | 102.0% | 90.5%
Class B | -0.12% | 0.24% | 0.30% | 107.1% | 97.5%
Class C | -0.11% | 0.26% | 0.22% | 107.2% | 100.5%
Class E | -0.10% | 0.27% | 0.11% | 106.2% | 100.2%
Overall | -0.13% | 0.22% | 0.22% | 105.2% | 97.0%
Class D | -0.10% | 0.36% | 0.04% | 108.2% | 99.6%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | All Intra Main 10 |  |  |  | 
 | Over ANCHOR |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11% | -0.06% | 0.07% | 102.9% | 99.6%
Class A2 | -0.06% | 0.02% | 0.02% | 103.2% | 99.0%
Class B | -0.07% | 0.00% | 0.16% | 102.6% | 100.3%
Class C | -0.04% | -0.01% | 0.04% | 101.2% | 98.4%
Class E | -0.07% | 0.01% | -0.05% | 102.3% | 97.5%
Overall | -0.07% | -0.01% | 0.06% | 102.4% | 99.1%
Class D | -0.06% | 0.09% | -0.08% | 100.9% | 96.7%
Class F | #VALUE! | #VALUE! | #VALUE! | 100.9% | 98.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
  JVET-AH0184 Test1 + JVET-AH0237

## Slide 6: Conclusion
We recommend further study of the proposed method in EE2.