## Slide 1: Report on subjective performance evaluation of the ECM JVET-AH0344
Mathias Wien (RWTH Aachen University) Vittorio Baroncini (VABTech) Giacomo Baroncini (GBTech)
15th AG 5 Meeting, 34th JVET Meeting,
April 17-24th, 2024, Rennes, FR

## Slide 2: Test data
Comparison points:
  VTM-11ecm-12 as anchor
  ECM 12.0
  ECM-nTM (git hash 6da105bb) Configuration using no Template Matching tools
3 UHD sequences (RA cfg), 3 HD sequences (LDB cfg)
Rate matching: ECM rate ≤ VTM rate (dev. max 2%) ECM rate ≤ ECM-nTM rate (dev. max 2%)
 | Sequences | rate points | codecs | # PVS
UHD VTM/ECM | CrossRoad2s500 | 4 | 2 | 8
UHD VTM/ECM/nTM | DrivingPOV3 BeachMountain2 | 4 | 3 | 24
HD VTM/ECM | DOTA2 GTAVs090 | 4 | 2 | 16
HD VTM/ECM/nTM | Beatriz | 4 | 3 | 12

## Slide 3: Test set PSNR-Y BD rate numbers
UHD sequences | ECM | ECM-nTM
BeachMountain2 | -20.05 | -18.98
CrossRoad2s500 | -19.00 | 
DrivingPOV3 | -24.39 | -21.90
AVG | -22.22 | -20.44
HD sequences | ECM | ECM-nTM
Beatriz | -14.85 | -9.33
DOTA2s360 | -12.18 | 
GTAVs090 | -16.88 | 
AVG | -14.85 | -9.33

## Slide 4: Test logistics in Rennes
PC with playout to HDMI via video board
Distribution to displays via HDMI splitter
4× 65“ display Samsung TQ65S90CAT
Confirmed 4K 60fps 10 bit playout
Viewers
24 JVET experts, confirmed for visual acuity and normal color vision
Efficiency: 3 viewers at 1.5H distance per screen
HD displayed without scaling centered on UHD screen with gray background

## Slide 5: Test setup
DCR method using the 11-grade scale
  “Original” (1sec)
  [uncompressed sequence] (10sec)
  “PVS” (1sec)
  [PVS] (10sec)
  “Vote <N>” (5sec)
UHD: 1 test session with 38 PVS
HD: 1test sessions with 34 PVS

## Slide 6: Test design and data processing
Training
  Feedback training method as used in JVET-AF0311
Session design
  Stabilization phase (results not considered in evaluation)
  Session including original vs. original comparison
Processing of results
  1 viewer voting below score of 8 for the original: results not regarded
  All evaluated viewers above Pearson correlation threshold of 85%
  Outlier detection: z-score (trs=2.5),
  Further refinement: removal of isolated outliers

## Slide 7: Results: UHD
BeachMountain2
Assessment of VTM, ECM and ECM-nTM
Indicative BD-rate savings from MOS (partially overlapping CIs)
  ECM: -12.7%
  ECM-nTM -29.7%

## Slide 8: Results: UHD
CrossRoad2s500
Assessment of VTM and ECM
Indicative BD-rate savings from MOS (partially overlapping CIs)
  ECM: -25.3%

## Slide 9: Results: UHD
DrivingPOV3
Assessment of VTM, ECM and ECM-nTM
Indicative BD-rate savings from MOS (partially overlapping CIs)
  ECM -28.8%
  ECM-nTM -26.1%

## Slide 10: Comparison JVET-AB0270 / JVET-AH0344

## Slide 11: Results: HD
Beatriz
Assessment of VTM, ECM and ECM-nTM
Indicative BD-rate savings from MOS (partially overlapping CIs)
  ECM -21.5%
  ECM-nTM -16.6%

## Slide 12: Comparison JVET-AB0270 / JVET-AH0344

## Slide 13: Results: HD
DOTA2s360
Assessment of VTM and ECM
Indicative BD-rate savings from MOS (overlapping CIs)
  ECM 1.9%

## Slide 14: Results: HD
GTAVs090
Assessment of VTM and ECM
Indicative BD-rate savings from MOS (partially overlapping CIs)
  ECM: -18.2%

## Slide 15: Conclusions
Presentation of preliminary results!
Improved performance for ECM clearly demonstrated
  Gains appear to be similar to PSNR gains, might be due to evolutionary approach
  Performance impact of template matching tools variable, partially significant: further study suggested

## Slide 16: Thanks
Thanks to volunteers for ECM and VTM encoding and crosscheck!
  Alibaba, Bytedance, Ericsson, Google, HHI, Huawei, InterDigital, Kwai, MediaTek, Oppo, Qualcomm, Vivo
Thanks for providing the equipment at meeting site!
  Couvent des Jacobins for the four 65” displays
  HHI for PCs
  VABTech for bringing a backup PC
Thanks to Christian Lehmann and Fabrice Urban for help with site setup
Thanks to Vittorio and Giacomo Baroncini for the laboratory tests in Rome
Thanks to the 24 volunteers in Rennes