## Slide 1: JVET-AI0169 Non-EE2: On sub-block merge mode
Fan Wang, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction （1）
In VVC and ECM, sub-block merge mode includes affine merge mode and SBTMVP mode. During the development of ECM, both the affine merge mode and the SBTMVP mode are enhanced.
The CU size restriction of sub-block merge mode is specified as “cbWidth >= 8 && cbHeight >= 8”.

## Slide 3: Proposed aspect 1
It is proposed to modify the CU size restriction of sub-block merge mode as “cbWidth * cbHeigh >= 32”.
With this modification, CUs of size 4*8, 4*16, 4*32… and 8*4, 16*4, 32*4… can apply sub-block merge mode.

## Slide 4: Simulation results
Aspect 1

## Slide 5: Introduction （2）
The usage of affine merge is highly related to the neighboring area of the current block.
  If current block is in an affine motion area, it has high probability to use affine merge. On the other hand, if current block is in a translational motion area, it has low probability to use affine merge.

## Slide 6: Proposed aspect 2
If at least one of the spatial neighboring blocks and non-adjacent blocks is coded with sub-block merge mode or inter affine mode, sub-block merge mode is allowed for current block. Otherwise, sub-block merge mode is forbidden for current block.
If sub-block merge mode is forbidden in current block, the encoder will not try sub-block merge mode and do not signal sub-block merge flag, the decoder will not parse this flag.
  Reduce unnecessary encoding time.
  Reduce unnecessary signaling.

## Slide 7: Simulation results
Aspect 1
Aspect 1 + aspect 2

## Slide 8: Conclusions
The proposed method brings -0.09% coding gain in RA with 1.2% EncT increase. It is recommended to investigate the proposed methods in EE2.
Thanks Qualcomm for crosschecking