## Slide 1: EE2-2.5 related: Intra Merge Mode extension with BV improvement
Jiaye Fu (Peking Univ.) Sapporo, 2024.07

## Slide 2: Introduction
EE2-2.5: Intra Merge Mode
  A list of intra mode candidates is constructed using the intra modes from the neighbour blocks coded by DIMD and TIMD modes. A flag is signalled to indicate whether to enable the proposed intra merge mode.
  Uses the same BV mode extension strategy as DIMD (JVET-AG0152)
Notes: # It uses polynomials to make predictions about the current block

## Slide 3: Intra Merge Mode extension with BV improvement
BV modes from merged BV list (same as BV list used in IntraTMP) can replace all intra modes in intra merge mode candidate according to the template cost analysis.
Weight and locDepth in intra merge mode candidate is remained.
Same prediction method of Intra Merge Mode is performed

## Slide 4: Results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.09% | 0.03% | 0.04% | 101.63% | 97.47% | 100.97% | 100.17%
Class A2 | -0.10% | 0.01% | 0.05% | 103.60% | 103.00% | 101.37% | 99.96%
Class B | -0.07% | -0.08% | -0.06% | 101.64% | 99.34% | 99.02% | 100.11%
Class C | -0.06% | 0.04% | 0.14% | 101.82% | 100.20% | 100.17% | 100.11%
Class E | -0.06% | 0.04% | 0.00% | 105.80% | 102.04% | 101.04% | 100.06%
Overall | -0.08% | 0.00% | 0.03% | 102.69% | 100.26% | 100.33% | 100.09%
Class D | -0.04% | 0.09% | -0.03% | 104.84% | 102.66% | 100.28% | 100.05%
Class F | -0.03% | -0.06% | 0.06% | 101.10% | 100.66% | 101.34% | 100.11%
Class TGM | -0.01% | -0.02% | -0.04% | 100.84% | 94.72% | 101.43% | 100.23%

## Slide 5: Conclusion
This contribution suggests an improved BV mode extension to the Intra Merge Mode. The results show that the proposed method can improve the coding efficiency of ECM on the top of EE2-2.5. It is suggested to further study this method in EE2.
Thanks to Qualcomm Inc. for cross-checking!

## Slide 6
Thank you