## Slide 1: JVET-AJ2023: Exploration Experiments on Neural Network-based Video Coding (EE1)
E. Alshina, F. Galpin, Y. Li, D. Rusanovskyy, M. Santamaria, J. Ström, R. Chang, Z. Xie (EE coordinators)

## Slide 2: List of EE1 tests (1/2)
EE1-1: LOP and VLOP in-loop filter
  EE1-1.1 – Partial Convolution and Over-Parameterization
    Report: JVET-AJ0080, cross-check: JVET-AJ0150
  EE1-1.2 – LOP with residual groups and Attention
    Report:JVET-AJ0165, cross-check JVET-AJ0327
  EE1-1.3 - NN in-loop filters using early cropping
    Report: JVET-AJ0054, cross-check: JVET-AJ0133
  EE1-1.4 – Reduced complexity input feature extraction for LOP & VLOP
    Report: JVET-AJ0066 cross-check: JVET-AJ0163
  EE1-1.5 - Multiscale blocks in LOP3 and VLOP2 filter
    Report: JVET-AJ0182 cross-check: JVET-AJ0206

## Slide 3: List of EE1 tests (2/2)
EE1-2: HOP in-loop filter
  EE1-2.2 – Block-size invariant implementation of HOP
    Report:JVET-AJ0166 cross-check: JVET-AJ0177
  EE1-2.3 – Block based QP information in NN loop filters
    Report:JVET-AJ0124 cross-check: JVET-AJ0324
EE1-3: NN-inter prediction
  E1-3.1 – RA/LDB Unified Reference Frame Synthesis for VVC Inter Coding
    Report: JVET-AJ0099 cross-check: Nokia
EE1-4: NN-based super resolution
  EE1-4.1 – Wavelet transform for super-resolution loss function
    Report:JVET-AJ0056, cross-check: JVET-AJ0291

## Slide 4: EE1 anchor
BD-rate Over NNVC-8.0 VTM |  |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Random access |  |  |  |  |  |  |  | 
Class A1 | -7.9% | -10.1% | -10.6% | -8.6% | -11.3% | -10.6% | 122% | 7629%
Class A2 | -6.8% | -12.7% | -9.7% | -6.9% | -11.6% | -7.5% | 114% | 7025%
Class B | -6.6% | -13.9% | -12.7% | -6.8% | -13.1% | -12.1% | 121% | 7467%
Class C | -6.6% | -14.9% | -14.4% | -7.1% | -13.2% | -13.0% | 121% | 7162%
Class E |  |  |  |  |  |  |  | 
Overall | -6.9% | -13.2% | -12.1% | -7.3% | -12.5% | -11.1% | 120% | 7326%
Class D | -7.2% | -14.8% | -15.0% | -6.5% | -13.0% | -13.0% | 117% | 7268%
Class F | -3.7% | -9.5% | -9.4% | -4.5% | -10.5% | -10.2% | 129% | 3275%
Low delay B |  |  |  |  |  |  |  | 
Class B | -5.3% | -13.7% | -13.4% | -6.2% | -15.2% | -17.2% | 113% | 7591%
Class C | -5.5% | -13.9% | -15.1% | -7.4% | -15.9% | -17.2% | 110% | 7143%
Class E | -6.2% | -8.6% | -11.9% | -8.0% | -10.1% | -13.3% | 119% | 7827%
Overall | -5.6% | -12.5% | -13.6% | -7.0% | -14.1% | -16.2% | 113% | 7496%
Class D | -6.5% | -13.1% | -15.1% | -7.4% | -14.2% | -18.0% | 110% | 7026%
Class F | -3.1% | -8.6% | -9.1% | -4.5% | -10.2% | -13.9% | 121% | 3871%
All Intra |  |  |  |  |  |  |  | 
Class A1 | -8.6% | -12.7% | -12.3% | -9.0% | -14.9% | -12.6% | 168% | 5248%
Class A2 | -7.1% | -12.7% | -11.3% | -7.4% | -12.1% | -9.3% | 160% | 4409%
Class B | -7.3% | -13.0% | -13.5% | -7.5% | -13.3% | -13.4% | 167% | 4381%
Class C | -7.5% | -13.8% | -14.5% | -7.9% | -14.3% | -14.6% | 165% | 3524%
Class E | -10.7% | -14.1% | -15.1% | -10.9% | -13.5% | -14.2% | 168% | 5078%
Overall | -8.1% | -13.3% | -13.4% | -8.4% | -13.6% | -13.0% | 166% | 4414%
Class D | -7.7% | -12.7% | -15.0% | -7.5% | -13.6% | -15.4% | 157% | 3460%
Class F | -5.3% | -10.8% | -10.4% | -5.1% | -11.2% | -11.5% | 133% | 3832%
NNVC-8.0 SW tools:
NNLF- LOP2 (ON by default)
NNLF-Intra (ON by default)
NNLF-Intra-low complexity
NNLF-HOP
NNSR
NNPostFilter
Test results provided by AhG14
For comparison

## Slide 5: EE1 anchor
BD-rate Over NNVC-9.1 VTM |  |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Random access |  |  |  |  |  |  |  | 
Class A1 | -8.8% | -11.8% | -12.5% | -9.4% | -13.3% | -14.4% | 122% | 8345%
Class A2 | -7.6% | -12.2% | -8.0% | -8.1% | -12.9% | -7.9% | 120% | 7883%
Class B | -6.9% | -14.2% | -12.1% | -7.5% | -15.4% | -14.4% | 124% | 8291%
Class C | -6.5% | -13.5% | -11.9% | -7.5% | -14.1% | -12.8% | 120% | 7846%
Class E |  |  |  |  |  |  |  | 
Overall | -7.3% | -13.1% | -11.3% | -8.0% | -14.1% | -12.7% | 122% | 8098%
Class D | -6.7% | -11.8% | -11.1% | -6.8% | -12.0% | -12.0% | 122% | 7597%
Class F | -3.8% | -7.5% | -6.1% | -5.0% | -10.7% | -9.1% | 131% | 3845%
Low delay B |  |  |  |  |  |  |  | 
Class B | -5.5% | -10.0% | -7.9% | -6.5% | -9.5% | -12.7% | 115% | 7876%
Class C | -5.3% | -11.8% | -9.0% | -6.9% | -10.2% | -9.1% | 113% | 6950%
Class E | -5.7% | -4.3% | -3.3% | -7.9% | -1.9% | -4.4% | 130% | 8302%
Overall | -5.5% | -9.2% | -7.1% | -7.0% | -7.8% | -9.4% | 118% | 7654%
Class D | -6.1% | -9.9% | -7.9% | -7.2% | -4.8% | -9.3% | 111% | 6863%
Class F | -3.0% | -6.2% | -2.2% | -5.2% | -6.3% | -7.4% | 123% | 3760%
All Intra |  |  |  |  |  |  |  | 
Class A1 | -9.2% | -14.2% | -14.9% | -9.4% | -16.7% | -16.4% | 177% | 5844%
Class A2 | -7.5% | -13.5% | -10.6% | -8.2% | -14.1% | -10.3% | 174% | 5098%
Class B | -7.6% | -14.1% | -14.3% | -8.0% | -15.9% | -16.1% | 173% | 4941%
Class C | -7.4% | -13.4% | -13.1% | -8.3% | -16.1% | -15.7% | 164% | 3691%
Class E | -11.0% | -16.0% | -16.2% | -11.8% | -16.3% | -17.0% | 173% | 5427%
Overall | -8.4% | -14.2% | -13.9% | -9.0% | -15.8% | -15.2% | 172% | 4862%
Class D | -7.3% | -11.6% | -12.2% | -7.6% | -14.6% | -15.4% | 156% | 3266%
Class F | -5.2% | -9.5% | -8.7% | -5.6% | -12.1% | -11.7% | 136% | 4106%
NNVC-9.1 SW tools:
NNLF- LOP3 (ON by default)
NNLF-Intra (ON by default)
NNLF-Intra-low complexity
NNLF-HOP, VLOP
NNSR
NNPostFilter
Test results provided by AhG14

## Slide 6: EE1 anchor
NNVC-10.0 SW tools:
NNLF- LOP4 (ON by default)
NNLF-Intra (ON by default)
NNLF-Intra-low complexity
NNLF-HOP, VLOP
NNSR
NNPostFilter
Test results provided by AhG14
BD-rate Over NNVC-10.0 VTM |  |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Random access |  |  |  |  |  |  |  | 
Class A1 | -8.8% | -12.0% | -12.7% | -9.4% | -13.7% | -14.8% | 116% | 3451%
Class A2 | -7.7% | -12.9% | -8.5% | -8.3% | -13.7% | -8.6% | 114% | 3264%
Class B | -7.0% | -14.8% | -12.5% | -7.7% | -16.3% | -15.2% | 117% | 3519%
Class C | -6.6% | -13.8% | -12.1% | -7.6% | -14.7% | -13.3% | 120% | 3349%
Class E |  |  |  |  |  |  |  | 
Overall | -7.4% | -13.6% | -11.6% | -8.1% | -14.9% | -13.3% | 117% | 3408%
Class D | -6.7% | -12.7% | -11.1% | -6.7% | -13.3% | -12.4% | 118% | 3283%
Class F | -3.9% | -7.9% | -6.4% | -5.1% | -11.2% | -9.7% | 124% | 1635%
Low delay B |  |  |  |  |  |  |  | 
Class B | -5.5% | -10.3% | -8.4% | -6.5% | -9.9% | -13.5% | 108% | 3332%
Class C | -5.3% | -11.8% | -9.2% | -7.0% | -10.1% | -8.2% | 109% | 3194%
Class E | -6.0% | -5.0% | -3.9% | -8.1% | -3.5% | -5.3% | 114% | 3343%
Overall | -5.5% | -9.5% | -7.5% | -7.1% | -8.3% | -9.7% | 110% | 3288%
Class D | -5.9% | -9.4% | -7.8% | -7.0% | -4.1% | -9.4% | 105% | 3005%
Class F | -3.1% | -6.5% | -2.5% | -5.6% | -6.7% | -6.8% | 113% | 1690%
All Intra |  |  |  |  |  |  |  | 
Class A1 | -9.2% | -14.2% | -14.9% | -9.4% | -16.8% | -16.4% | 177% | 2708%
Class A2 | -7.8% | -13.9% | -11.0% | -8.5% | -14.4% | -10.6% | 173% | 2262%
Class B | -7.7% | -14.2% | -14.4% | -8.1% | -16.2% | -16.4% | 176% | 2255%
Class C | -7.5% | -13.5% | -13.1% | -8.4% | -16.2% | -15.8% | 166% | 1773%
Class E | -10.9% | -16.0% | -16.3% | -11.7% | -16.2% | -17.3% | 171% | 2395%
Overall | -8.5% | -14.3% | -14.0% | -9.0% | -16.0% | -15.4% | 173% | 2227%
Class D | -7.3% | -11.7% | -12.1% | -7.7% | -14.9% | -15.2% | 155% | 1621%
Class F | -5.2% | -9.5% | -8.7% | -5.6% | -12.4% | -11.8% | 134% | 1808%

## Slide 7: EE1 HOP
NNVC-10.0 SW tools:
NNLF- HOP5 (option)
NNLF-Intra (ON by default)
NNLF-Intra-low complexity
NNLF-LOP4 (default), VLOP
NNSR
NNPostFilter
Test results provided by AhG14
BD-rate Over NNVC-10.0 VTM |  |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Random access |  |  |  |  |  |  |  | 
Class A1 | -15.6% | -13.5% | -21.6% | -17.2% | -18.9% | -23.7% | 282% | 131372%
Class A2 | -15.1% | -20.8% | -26.6% | -14.4% | -20.4% | -23.7% | 264% | 117932%
Class B | -13.1% | -24.2% | -17.3% | -12.0% | -22.6% | -16.6% | 278% | 115538%
Class C | -13.9% | -17.3% | -16.9% | -12.5% | -14.5% | -14.2% | 217% | 98690%
Class E |  |  |  |  |  |  |  | 
Overall | -14.2% | -19.5% | -19.9% | -13.7% | -19.2% | -18.8% | 258% | 114132%
Class D | -14.8% | -17.5% | -17.3% | -11.0% | -13.0% | -11.4% | 211% | 87883%
Class F | -9.0% | -11.4% | -10.5% | -9.2% | -12.1% | -10.8% | 382% | 51677%
Low delay B |  |  |  |  |  |  |  | 
Class B | -9.9% | -12.3% | -7.3% | -9.4% | -9.2% | -5.1% | 253% | 108842%
Class C | -11.7% | -9.5% | -6.9% | -10.5% | -4.7% | -0.1% | 206% | 92539%
Class E | -10.6% | -10.6% | -4.6% | -10.5% | -10.9% | -4.1% | 495% | 85823%
Overall | -10.7% | -10.9% | -6.5% | -10.0% | -8.1% | -3.2% | 279% | 97164%
Class D | -12.8% | -7.6% | -0.5% | -10.5% | 1.2% | 14.5% | 200% | 93252%
Class F | -9.1% | -10.0% | -9.7% | -10.3% | -11.1% | -9.6% | 358% | 56653%
All Intra |  |  |  |  |  |  |  | 
Class A1 | -13.5% | -10.7% | -17.2% | -15.0% | -16.6% | -19.5% | 386% | 103774%
Class A2 | -13.6% | -17.6% | -21.3% | -14.3% | -18.6% | -18.3% | 279% | 79847%
Class B | -12.1% | -17.0% | -14.4% | -12.0% | -17.1% | -14.8% | 265% | 77418%
Class C | -13.1% | -14.3% | -16.2% | -12.8% | -13.9% | -15.5% | 212% | 52916%
Class E | -16.7% | -19.9% | -18.8% | -16.4% | -18.8% | -19.5% | 278% | 87647%
Overall | -13.6% | -15.9% | -17.1% | -13.8% | -16.8% | -17.1% | 273% | 76656%
Class D | -12.2% | -12.7% | -15.8% | -11.2% | -12.7% | -14.7% | 190% | 47074%
Class F | -10.0% | -12.5% | -10.5% | -9.7% | -12.4% | -11.0% | 175% | 64025%

## Slide 8: EE1 VLOP
NNVC-10.0 SW tools:
NNLF- VLOP (option)
NNLF-Intra (ON by default)
NNLF-Intra-low complexity
NNLF-LOP4 (default), HOP
NNSR
NNPostFilter
Test results provided by AhG14
BD-rate Over NNVC-10.0 VTM |  |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Random access |  |  |  |  |  |  |  | 
Class A1 | -7.0% | -6.7% | -6.1% | -7.5% | -8.6% | -6.6% | 110% | 1601%
Class A2 | -5.7% | -7.0% | -4.9% | -6.2% | -7.7% | -4.9% | 109% | 1440%
Class B | -5.3% | -8.8% | -7.3% | -6.1% | -10.0% | -8.4% | 112% | 1575%
Class C | -4.9% | -7.3% | -6.6% | -6.0% | -8.7% | -7.7% | 111% | 1443%
Class E |  |  |  |  |  |  |  | 
Overall | -5.6% | -7.6% | -6.4% | -6.4% | -8.9% | -7.1% | 111% | 1516%
Class D | -4.7% | -6.1% | -5.9% | -5.2% | -7.1% | -7.5% | 110% | 1350%
Class F | -2.8% | -4.0% | -3.2% | -3.7% | -6.1% | -4.9% | 114% | 752%
Low delay B |  |  |  |  |  |  |  | 
Class B | -3.9% | -8.9% | -4.8% | -5.3% | -12.1% | -11.4% | 97% | 1513%
Class C | -3.5% | -7.5% | -5.5% | -5.3% | -10.7% | -8.7% | 96% | 1358%
Class E | -4.0% | -3.2% | -3.0% | -6.3% | -7.9% | -7.5% | 98% | 1556%
Overall | -3.8% | -7.0% | -4.6% | -5.5% | -10.6% | -9.5% | 97% | 1470%
Class D | -4.0% | -5.4% | -3.2% | -5.2% | -10.0% | -9.7% | 95% | 1282%
Class F | -1.8% | -2.3% | -1.7% | -3.5% | -5.5% | -5.8% | 95% | 737%
All Intra |  |  |  |  |  |  |  | 
Class A1 | -8.1% | -9.5% | -8.7% | -8.2% | -11.6% | -9.1% | 169% | 1441%
Class A2 | -6.7% | -8.9% | -7.4% | -7.1% | -9.2% | -7.0% | 173% | 1324%
Class B | -6.6% | -9.5% | -9.1% | -7.0% | -10.7% | -10.1% | 172% | 1316%
Class C | -6.1% | -8.5% | -8.0% | -7.1% | -10.3% | -9.6% | 160% | 1104%
Class E | -9.2% | -10.9% | -10.7% | -9.9% | -10.8% | -10.5% | 168% | 1380%
Overall | -7.2% | -9.4% | -8.8% | -7.7% | -10.5% | -9.4% | 168% | 1296%
Class D | -5.9% | -7.2% | -7.5% | -6.5% | -9.3% | -10.0% | 148% | 1017%
Class F | -4.1% | -5.8% | -5.5% | -4.5% | -7.2% | -7.1% | 132% | 972%

## Slide 9: NNVC tools combination performance
Test | Random Access |  |  |  |  | All Intra |  |  |  |  | Total kMAC/pxl | Total Param (Mprm) | Source
 | Y | U | V | Enc | Dec | Y | U | V | Enc | Dec |  |  | 
NN-Intra & LOP NN-filter |  |  |  |  |  |  |  |  |  |  |  |  | 
NNVC-10.0(LOP3) | -7.4% | -13.6% | -11.6% | 1.2 | 34 | -8.5% | -14.3% | -14.0% | 1.7 | 22 | 21.7 | 1.5 | JVET-AJ0014
NNVC-9.1(LOP3) | -7.3% | -13.1% | -11.3% | 1.2 | 81 | -8.4% | -14.2% | -13.9% | 1.7 | 49 | 24.8 | 1.72 | JVET-AI0014
NNVC-8.0(LOP2) | -6.9% | -13.2% | -12.1% | 1.2 | 73 | -8.1% | -13.3% | -13.4% | 1.7 | 44 | 24.9 | 1.55 | JVET-AH0014
NNVC-7.1(LOP1) | -6.9% | -13.2% | -12.1% | 1.3 | 86 | -8.1% | -13.3% | -13.4% | 1.8 | 56 | 24.9 | 1.55 | JVET-AG0014
NN-Intra & HOP NN-filter |  |  |  |  |  |  |  |  |  |  |  |  | 
NNVC-10.0(HOP) | -14.2% | -19.5% | -19.9% | 2.6 | 1441 | -13.6% | -15.9% | -17.1% | 2.7 | 767 | 471 | 2.7 | JVET-AJ0014
NNVC-9.1(HOP4) | -14.0% | -19.1% | -19.5% | 2.9 | 1446 | -13.3% | -16.2% | -17.7% | 2.6 | 853 | 483.6 | 3.0 | JVET-AI0014
NNVC-8.0(HOP3) | -13.7% | -13.9% | -14.5% | 2.5 | 1092 | -12.7% | -11.6% | -13.0% | 2.4 | 56 | 473.8 | 2.9 | JVET-AH0014
NN-Intra & VLOP NN-filter |  |  |  |  |  |  |  |  |  |  |  |  | 
NNVC-10.0(VLOP) | -5.6% | -7.6% | -6.4% | 1.1 | 15 | -7.2% | -9.4% | -8.8% | 1.7 | 13 | 10.0 | 1.4 | JVET-AJ0014
NNVC-9.1(VLOP) | -5.3% | -5.4% | -5.2% | 1.2 | 40 | -7.1% | -7.8% | -7.7% | 1.8 | 29 | 5.1 | 0.2 | JVET-AI0014
NN-Intra & LOP NN-filter & adaptive resolution |  |  |  |  |  |  |  |  |  |  |  |  | 
NNVC-10. (NNSR) | -8.1% | -10.3% | -8.9% |  |  | -9.2% | -11.5% | -11.0% |  |  | 26.4 | 1.5 | JVET-AI0074
NNVC-8.0 RPR(*) | -7.5% | -10.9% | -9.7% |  |  | -8.5% | -11.3% | -11.0% |  |  | 24.9 | 1.55 | JVET-AH0014
NNVC-8.0 NNSR(*) | -7.8% | -11.9% | -10.5% |  |  | -8.6% | -11.8% | -11.3% |  |  | 45.2 | 1.63 | JVET-AH0014

## Slide 10: EE1-1: LOP and VLOP in-loop filter
  EE1-1.1 – Partial Convolution and Over-Parameterization , (UESTC), (Transsion)
  EE1-1.2 – Simplified residual groups with attention (Qualcomm)
  EE1-1.3 - NN in-loop filters using early cropping (Ericsson)
  EE1-1.4 – Reduced complexity input feature extraction for LOP & VLOP (Qualcomm) – incomplete results!
  EE1-1.5 - LOP filter with multiscale blocks Nokia
Test | Random Access |  |  | All Intra |  |  | kMAC/pxl |  |  | Param,M |  |  | Source | 
 | Y | U | V | Y | U | V | Total | Filter | Intra | Total | Filter | Intra |  | 
NNVC-LOP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 21.7 | 16.9 | 4.8 | 1.5 | 0.21 | 1.3 | JVET-AJ0014 | 
EE1-1.1 (int) | -0.1% | 1.2% | 1.2% | -0.1% | 1.0% | 0.9% | 21.7 | 16.9 | 4.8 | 1.5 | 0.20 | 1.3 | JVET-AJ0080 | 
EE1-1.1 (fl) | 0.0% | 1.1% | 1.1% | -0.1% | 0.9% | 0.8% | 21.7 | 16.9 | 4.8 | 1.5 | 0.20 | 1.3 | JVET-AJ0080 | 
EE1-1.2 | -0.4% | 0.0% | 0.3% | -0.4% | -0.1% | 0.4% | 21.7 | 16.9 | 4.8 | 1.5 | 0.49 | 1.3 | JVET-AJ0165 | 
EE1-1.3 | -0.3% | -1.2% | -1.0% | -0.3% | -1.1% | -0.9% | 21.6 | 16.8* | 4.8 | 1.5 | 0.21 | 1.3 | JVET-AJ0054 | 
EE1-1.4.1 | 0.0% | 0.8% | 0.4% | 0.0% | 0.6% | 0.6% | 21.7 | 16.9 | 4.8 | 1.5 | 0.21 | 1.3 | JVET-AJ0066 | 
EE1-1.5.1 | -0.2% | -0.4% | -0.8% | -0.1% | -0.4% | -0.4% | 21.7 | 16.9 | 4.8 | 1.5 | 0.21 | 1.3 | JVET-AJ0182 | 
EE1-1.5.2 | 0.0% | -2.5% | -3.2% | 0.0% | -2.4% | -2.8% | 21.7 | 16.8 | 4.8 | 1.5 | 0.21 | 1.3 | JVET-AJ0182 | 
Test | Random Access |  |  | All Intra |  |  | kMAC/pxl |  |  | Param,M |  |  | Source
 | Y | U | V | Y | U | V | Total | Filter | Intra | Total | Filter | Intra | 
NNVC-VLOP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 10.0 | 5.2 | 4.8 | 1.5 | 0.06 | 1.3 | JVET-AJ0014
EE1-1.3 | 0.0% | 0.2% | -0.1% | -0.1% | 0.0% | -0.1% | 9.9 | 5.1 | 4.8 | 1.5 | 0.06 | 1.3 | JVET-AJ0054
EE1-1.4.1 | -0.1% | 1.3% | 1.0% | -0.1% | 1.4% | 1.3% | 10.0 | 5.2 | 4.8 | 1.5 | 0.06 | 1.3 | JVET-AJ0066
EE1-1.5.3 | -0.1% | 1.9% | 1.5% | -0.2% | 1.8% | 1.4% | 10.0 | 5.2 | 4.8 | 1.5 | 0.06 | 1.3 | JVET-AJ0182
EE1-1.5.4 | 0.0% | 0.1% | 0.1% | -0.1% | 0.1% | 0.3% | 10.0 | 5.2 | 4.8 | 1.5 | 0.06 | 1.3 | JVET-AJ0182

## Slide 11: LOP and VLOP NN-filters (NNVC-10)
Rec [6]
Pred [6]
BS [6]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV
1  1, C
PReLU
sCONV2
13, C
CONV
1  1, C
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
Crop
NY
[C1,h,w]
Back Bone Block C
[C1,h,w]
Crop
IPB [4]
CONV 11,d5
Parameters selection (LOP):
d1 =16 NY = 14 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 144 C UV 1 =128
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2
d6 = 64
sCONV 1  3 CC21
CONV 1  1 C1C
sCONV 3  1 C21C
CONV 1  1 CC1
PReLU
NUV
Back Bone Block, C1Y
Back Bone Block, C1Y
...
CONV 33 CY16
Pixel Shuffle
CONV 13 CYCY21
sCONV 31 CY21CY
sCONV 11 CYCY
PReLU
Back Bone Block, C1UV
Back Bone Block, C1UV
...
CONV 33 CUV8
CONV 13 CUVCUV21
sCONV 31 CUV21CUV
sCONV 11 CUVCUV
PReLU
sCONV2
31, C
CONV
1  1, C C1Y
CONV
1  1, C C1UV
CONV
1  1, C1Y CY
CONV
1  1, C1UV CUV
DCT
DCT-1
DCT-1
2, 2
 | kMACs | kPrms
LOP | 16.9 | 205.1
VLOP | 5.2 | 61
Parameters selection (VLOP):
d1 =4 NY = 6 NUV = 1
d2 = 2 C Y = 32 C UV = 16
d3 = 1 C Y 1 = 96 C UV 1 =32
d4 = 1 C Y 21= 32 C UV 21= 16
d5 = 1
d6 = 16

## Slide 12: EE1-1.1 – Partial Convolution and Over-Parameterization
Rec [6]
Pred [6]
BS [6]
QPbase
[1]
QPslice[1]
OP blk d1 d1
OP blk d2 d2
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV
1  1, C
PReLU
sCONV2
13, C
CONV
1  1, C
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
Crop
NY
[C1,h,w]
Back Bone Block C
[C1,h,w]
Crop
IPB [4]
CONV 11,d5
Parameters selection:
d1 =16 NY = 13 NUV = 2
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 144 C UV 1 =80
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2 k= 0.5
d6 = 64
total convolution 65 (76 in LOP NNVC 10)
CONV 1  1 C1C2
CONV 1  1 C3C1
PReLU
NUV
Back Bone Block, C1Y
Back Bone Block, C1Y
...
OP blk
CY16
Pixel Shuffle
sCONV 11 CYCY
PReLU
Back Bone Block, C1UV
Back Bone Block, C1UV
...
OP blk
CUV8
sCONV 11 CUVCUV
PReLU
sCONV2
31, C
CONV
1  1, C C1Y
CONV
1  1, C C1UV
CONV
1  1, C1Y CY
CONV
1  1, C1UV CUV
DCT
DCT-1
DCT-1
PPC block
CY,CY21
PPC block
CUV,CUV21
PPC block
C2,C3
2, 2
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.1 | 16.9 | 203.9
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | -0.1% | 1.2% | 1.3% | 99% | 93%
All Intra | -0.1% | 1.0% | 0.9% | 98% | 95%
Results vs relevant anchor (int16)

## Slide 13: Over-Parameterization
Rec [6]
Pred [6]
BS [6]
QPbase
[1]
QPslice[1]
OP blk d1 d1
OP blk d2 d2
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV
1  1, C
PReLU
sCONV2
13, C
CONV
1  1, C
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
Crop
NY
[C1,h,w]
Back Bone Block C
[C1,h,w]
Crop
IPB [4]
CONV 11,d5
Parameters selection:
d1 =16 NY = 14 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 144 C UV 1 =128
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2
d6 = 64
sCONV 1  3 CC21
CONV 1  1 C1C
sCONV 3  1 C21C
CONV 1  1 CC1
PReLU
NUV
Back Bone Block, C1Y
Back Bone Block, C1Y
...
OP blk
CY16
Pixel Shuffle
CONV 13 CYCY21
sCONV 31 CY21CY
sCONV 11 CYCY
PReLU
Back Bone Block, C1UV
Back Bone Block, C1UV
...
OP blk
CUV8
CONV 13 CUVCUV21
sCONV 31 CUV21CUV
sCONV 11 CUVCUV
PReLU
sCONV2
31, C
CONV
1  1, C C1Y
CONV
1  1, C C1UV
CONV
1  1, C1Y CY
CONV
1  1, C1UV CUV
DCT
DCT-1
DCT-1
2, 2
CONV 3  3 C1 (p*C1)
CONV 1  1 (p*C1) C2
CONV 3  3 C1C2
Training stage
Inference stage
Layer fusion
Over-Parameterization Block (OP Block), C1, C2 , p
[C1,h,w]
[C2,h,w]
vs NNVC-9.1 |  |  | 
cfg | Y | U | V
RA |  |  | 
AI | 0.0% | 2.3% | 2.3%

## Slide 14: Partial Convolution
Rec [6]
Pred [6]
BS [6]
QPbase
[1]
QPslice[1]
CONV 11,d3
CONV 11,d4
CONV 11,d4
CONV
1  1, C
PReLU
sCONV2
13, C
CONV
1  1, C
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
Crop
NY
[C1,h,w]
Back Bone Block C
[C1,h,w]
Crop
IPB [4]
CONV 11,d5
Parameters selection:
d1 =16 NY = 14 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 144 C UV 1 =128
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2 C Y 2= ?
d6 = 64 C Y 3= ?
CONV 1  1 C1C2
CONV 1  1 C3C1
PReLU
NUV
Back Bone Block, C1Y
Back Bone Block, C1Y
...
Pixel Shuffle
sCONV 11 CYCY
PReLU
Back Bone Block, C1UV
Back Bone Block, C1UV
...
sCONV 11 CUVCUV
PReLU
sCONV2
31, C
CONV
1  1, C C1Y
CONV
1  1, C C1UV
CONV
1  1, C1Y CY
CONV
1  1, C1UV CUV
DCT
DCT-1
DCT-1
PPC block
CY,CY21
PPC block
CUV,CUV21
PPC block
C2,C3
CONV 33 CY16
CONV 33 CUV8
CONV 33,d1
CONV 33,d2
 | kMACs | kPrms
LOP3 | 16.9 | 205.1
EE1-1.1 | 16.9 | 203.9
2, 2
vs NNVC-9.1 |  |  | 
cfg | Y | U | V
RA |  |  | 
AI | 0.0% | -1.2% | -1.7%
Number of convolution layers
94  74
Partial Convolution Block (PC Block), C1, k
[C1,h,w]
[C1,h,w]
CONV 3  3 k*C1  k*C1
Concat
(1-k) * C1

## Slide 15: EE1-1.2 – Simplified residual groups with attention
New design elements
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | -0.4% | 0.0% | 0.3% | 100% | 107%
All Intra | -0.4% | -0.1% | 0.4% | 100% | 108%
Results vs relevant anchor (SIMD for DW conv)

## Slide 16: EE1-1.3 – NN in-loop filters using early cropping
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.3 | 16.8 | 205.1
Results vs relevant anchor (LOP)
Parameters selection (LOP):
d1 =16 NY = 15 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 176 C UV 1 =128
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2
d6 = 64
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | -0.3% | -1.2% | -0.9% |  | 109%
All Intra | -0.3% | -1.1% | -0.9% |  | 111%

## Slide 17: EE1-1.3 – NN in-loop filters using early cropping
 | kMACs | kPrms
VLOP | 5.2 | 61
EE1-1.3 | 5.1 | 61
Results vs relevant anchor (VLOP)
Parameters selection (VLOP):
d1 =4 NY = 6 NUV = 1
d2 = 2 C Y = 32 C UV = 16
d3 = 1 C Y 1 = 112 C UV 1 =32
d4 = 1 C Y 21= 32 C UV 21= 16
d5 = 1
d6 = 16
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | 0.0% | 0.2% | -0.1% |  | 107%
All Intra | -0.1% | 0.0% | -0.1% |  | 105%

## Slide 18: EE1-1.4 – Reduced complexity input feature extraction for LOP & VLOP
Rec [6]
Pred [6]
BS [1]
Qpbase
[1]
CONV 33,d1
CONV 33,d2
CONV 11,d3
CONV 11,d4
CONV
1  1, C
PReLU
sCONV2
13, C
CONV
1  1, C
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
Crop
NY
[C1,h,w]
Back Bone Block C
[C1,h,w]
Crop
IPB [1]
CONV 11,d5
Parameters selection (LOP):
d1 =16 NY = 14 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 144 C UV 1 =128
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2
d6 = 64
sCONV 1  3 CC21
CONV 1  1 C1C
sCONV 3  1 C21C
CONV 1  1 CC1
PReLU
NUV
Back Bone Block, C1Y
Back Bone Block, C1Y
...
CONV 33 CY16
Pixel Shuffle
CONV 13 CYCY21
sCONV 31 CY21CY
sCONV 11 CYCY
PReLU
Back Bone Block, C1UV
Back Bone Block, C1UV
...
CONV 33 CUV8
CONV 13 CUVCUV21
sCONV 31 CUV21CUV
sCONV 11 CUVCUV
PReLU
sCONV2
31, C
CONV
1  1, C C1Y
CONV
1  1, C C1UV
CONV
1  1, C1Y CY
CONV
1  1, C1UV CUV
DCT
DCT-1
DCT-1
2, 2
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.4.1 | 16.9 | 205.1
EE1-1.4.2 | 16.9 | 205.1
VLOP | 5.2 | 61
EE1-1.4.1 | 5.2 | 61
EE1-1.4.2 | 5.2 | 61
Parameters selection (VLOP):
d1 =4 NY = 6 NUV = 1
d2 = 2 C Y = 32 C UV = 16
d3 = 1 C Y 1 = 96 C UV 1 =32
d4 = 1 C Y 21= 32 C UV 21= 16
d5 = 1
d6 = 16
EE1-1.4.1
bypass DCT for BS, QP and IPB
EE1-1.4.2
Additionally combine QPslice & QPbase
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | -0.1% | 1.3% | 1.0% |  | 
LDB | -0.1% | 1.4% | 1.1% |  | 
All Intra | -0.1% | 0.4% | 0.3% |  | 
EE1-1.4.1 vs relevant anchor
(VLOP)
Qpslice
[1]
CONV 11,d5

## Slide 19: EE1-1.5.1 – LOP filter with multiscale blocks
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.5.1 | 16.9 | 208.8
EE1-1.5.2 | 16.9 | 206.5
VLOP | 5.2 | 61
EE1-1.5.3 | 5.2 | 62
EE1-1.5.4 | 5.2 | 61
Parameters selection (LOP):
d1 =16 NY = 14 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 144 C UV 1 =125
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2
d6 = 64
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | -0.2% | -0.4% | -0.8% |  | 
All Intra | -0.1% | -0.4% | -0.4% |  | 
Results vs relevant anchor (LOP)

## Slide 20: EE1-1.5.2 – LOP filter with multiscale blocks
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.5.1 | 16.9 | 208.8
EE1-1.5.2 | 16.9 | 206.5
VLOP | 5.2 | 61
EE1-1.5.3 | 5.2 | 62
EE1-1.5.4 | 5.2 | 61
Parameters selection (LOP):
d1 =16 NY = 14 NUV = 4
d2 = 8 C Y = 32 C UV = 32
d3 = 4 C Y 1 = 145 C UV 1 =129
d4 = 2 C Y 21= 32 C UV 21= 32
d5 = 2
d6 = 64
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | 0.0% | -2.5% | -3.2% |  | 
All Intra | 0.0% | -2.4% | -2.8% |  | 
Results vs relevant anchor (LOP)

## Slide 21: EE1-1.5.3 – LOP filter with multiscale blocks
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.5.1 | 16.9 | 208.8
EE1-1.5.2 | 16.9 | 206.5
VLOP | 5.2 | 61
EE1-1.5.3 | 5.2 | 62
EE1-1.5.4 | 5.2 | 61
Parameters selection (VLOP):
d1 =4 NY = 6 NUV = 1
d2 = 2 C Y = 32 C UV = 16
d3 = 1 C Y 1 = 96 C UV 1 =27
d4 = 1 C Y 21= 32 C UV 21= 16
d5 = 1
d6 = 16
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | -0.1% | 1.9% | 1.5% |  | 
All Intra | -0.2% | 1.8% | 1.4% |  | 
Results vs relevant anchor (VLOP)

## Slide 22: EE1-1.5.1 – LOP filter with multiscale blocks
 | kMACs | kPrms
LOP | 16.9 | 205.1
EE1-1.5.1 | 16.9 | 208.8
EE1-1.5.2 | 16.9 | 206.5
VLOP | 5.2 | 61
EE1-1.5.3 | 5.2 | 62
EE1-1.5.4 | 5.2 | 61
Parameters selection (VLOP):
d1 =4 NY = 6 NUV = 1
d2 = 2 C Y = 32 C UV = 16
d3 = 1 C Y 1 = 96 C UV 1 =39
d4 = 1 C Y 21= 32 C UV 21= 16
d5 = 1
d6 = 16
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | 0.0% | 0.1% | 0.1% |  | 
All Intra | -0.1% | 0.1% | 0.3% |  | 
Results vs relevant anchor (VLOP)

## Slide 23: EE1-2: HOP in-loop filter
Test | Random Access |  |  | All Intra |  |  | tools in combination | kMAC/pxl |  |  | Param,M |  |  | Source
 | Y | U | V | Y | U | V |  | Total | Filter | Intra | Total | Filter | Intra | 
NNVC10-HOP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 2 | 471 | 466 | 4.8 | 2.96 | 1.439 | 1.3 | 
EE1-2.2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 2 | 471 | 466 | 4.8 | 2.96 | 1.439 | 1.3 | JVET-AJ0166
EE1-2.3 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 2 | 471 | 466 | 4.8 | 2.96 | 1.439 | 1.3 | JVET-AJ0124
  EE1-2.1 – Attention block with transformers (Qualcomm)
  EE1-2.2 – Block-size invariant implementation of HOP (Qualcomm)
  EE1-2.3 – Block based QP information in NN loop filters (InterDigital)
“--AdaptiveQP -aqr 12 --MaxCuDQPSubdiv=2”
Test | Random Access |  |  | All Intra |  | 
 | Y | U | V | Y | U | V
HOP3 (avg QP) vs HOP3 (slice) | 0.8% | 2.0% | 2.4% | 1.4% | 2.6% | 2.6%
HOP3 block QP(retrained) vs HOP3 (slice) | -0.8% | -0.9% | -1.3% | -0.9% | -1.2% | -1.3%
HOP5 (avg QP) vs HOP5 (slice) | 0.6% | 1.2% | 1.3% | 0.7% | 2.0% | 2.6%
HOP5 block QP(retrained) vs HOP5 (slice) | -1.0% | 0.5% | 0.4% | -1.6% | 0.4% | -0.3%

## Slide 24
gCONV 3  1 CC21
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 11,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Back Bone Block, C
Back Bone Block, C
...
CONV
3  3
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
gCONV 1  3 CC31
CONV 3  1 C31C
PReLU
Backbone Block C
[C,h,w]
Parameters selection:
d1 =192 C = 64 N = 23
d2 = 32 C1 =192 d6 = 48
d3 = 16 C21= 32
d4 = 16 C22= 80
d5 = 16 C31= 48
Crop
IPB [1]
CONV 11,d5
PReLU
Attention block
 | kMACs | kPrms
HOP4 | 466 | 1408
Group size =8
HOP in NNVC-10

## Slide 25: HOP architecture - Attention block
head=2
C=64
CONV 1x1, CxC*3
CONV 3x3, C*3xC*3, group=3C
qkv(3*c,h,w)
q(C,h,w)
k(C,h,w)
v(C,h,w)
q(head,…,h*w)
k(head,…,h*w)
v(head,…,h*w)
Reshape
Trans.(-2, -1)
Reshape (c, h, w)
CONV 1x1, CxC
[c,h,w]
Attention Block
CONV 3  1 CC21
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 1  3 CC31
CONV 3  1 C31C
PReLU
Backbone Block C
[C,h,w]
Attention block
g
g

## Slide 26: EE1-2.2 Block-size invariant implementation of HOP
1-7,9-14, 16-24 Res. Blocks
8th and 15th Res. Blocks
 | kMACs | kPrms
HOP5 | 466 | 1408
E1-2.2 | 466 | 1408
cfg | Y | Cb | Cr | Enc | Dec
Rand.Ac. | 0.0% | 0.0% | 0.0% | 100% | 101%
All Intra | 0.0% | 0.0% | 0.0% | 100% | 96%
Results vs relevant anchor (HOP)
Attention Map
  M(x,y)=
Attention Map proposed
  M=M>>2 if h*w>72x72
  M(x,y)
M

## Slide 27: EE1-2.3 Block based QP information in NN loop filters
1-7,9-14, 16-24 Res. Blocks
8th and 15th Res. Blocks
 | kMACs | kPrms
HOP5 | 466 | 1408
EE1-2.3 | 466 | 1408
Only re-training
With block level QP change
EE1-2.3.1
Test with perceptual QP optimization from VTM , no model change, feed model with avg QP
EE1-2.3.2
+ retrain model and feed with real block QP
BlockQP 1

## Slide 28: EE1-3: NN-inter prediction
  EE1-3.1 – RA/LDB Unified Reference Frame Synthesis for VVC Inter Coding (Xidian Univ.)
Test | Random Access |  |  | Low-delay B |  |  | kMAC/pxl |  |  |  | Param (Mprm) |  |  |  | Source
 | Y | U | V | Y | U | V | Total | Filter | Intra | Inter | Total | Filter | Intra | Inter | 
NNVC-10.0-LOP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 21.7 | 16.9 | 4.8 | 0 | 1.5 | 0.21 | 1.3 | 0 | 
EE1-3.1.2 | -3.5% | -4.4% | -4.3% | -3.6% | -3.9% | -0.3% | 748.7 | 16.9 | 4.8 | 727 | 5.3 | 0.21 | 1.3 | 3.8 | JVET-AJ0099

## Slide 29: EE1-3.1 – RA/LDB Unified Reference Frame Synthesis for VVC Inter Coding
 | kMACs | kPrms
E1-3.1 | 727 | 1935
EE1-3.1.1: Trained on Vimeo-90K triplet (compressed data by VTM-11.0-NNVC-4.0).
EE1-3.1.2: Trained on Vimeo-90K triplet (compressed data by VTM-11.0-NNVC-9.0).
EE1-3.1.3: Trained on BVI and TVD datasets (using compressed data at lower QP as label).
EE1-3.1.4: Trained on BVI and TVD datasets (using uncompressed data as label).
EE1-3.1.5: Try to port code into NNVC-10.0 SW.
Training set Vimeo-90K triplet
No decoding run time reported

## Slide 30: EE1-4: NN-super-resolution
  EE1-4.1 – Wavelet transform for super-resolution loss function, (HUST)
  Not clear what the anchor is, decoding run time is missed
Test | Random Access |  |  | All Intra |  |  | kMAC/pxl |  |  |  | Param (Mprm) |  |  |  | Source
 | Y | U | V | Y | U | V | Total | Filter | Intra | SR | Total | Filter | Intra | SR | 
EE1-4.1.1 | -0.8% | 3.1% | 2.6% | -0.8% | 2.9% | 3.1% | 26.4 | 16.9 | 4.8 | 4.7 | 1.6 | 0.21 | 1.3 | 0.05 | JVET-AJ0056
EE1-4.1.2 (DWT loss) | -0.8% | 2.2% | 2.4% | -0.8% | 2.9% | 2.8% | 26.4 | 16.9 | 4.8 | 4.7 | 1.6 | 0.21 | 1.3 | 0.05 | JVET-AJ0056

## Slide 31: NNVC-10 NNSR
 | kMACs | kPrms
NNSR | 4.7 | 50

## Slide 32: EE1-4.1. Wavelet transform for super-resolution loss function
 | kMACs | kPrms
NNSR | 4.7 | 50
EE1-4.1 | 4.7 | 50
Only re-training