## Slide 1
JVET-AJ0043 - Template Matching Picture Boundary Padding in ECM 14
Nicolas Neumann and Mathias Wien

## Slide 2
Overview
Reference Picture Padding
Template Matching for Reference Picture Padding
Complexity Reduction of Template Matching-based Reference Picture Padding
Combination with Motion Compensated Padding
Results
Conclusion
Intro

## Slide 3
Reference Picture Padding
Intro
Standard Padding
Template Matching Padding

## Slide 4
Template Matching
Intro
Target block to be predicted
Template adjacent to target block
Find matching structure (candidate)
Extract source block and use as prediction

## Slide 5
Template Matching-based Reference Picture Padding
Intro
Divide the area surrounding the reference picture into target blocks and do prediction
Complexity needs to be managed

## Slide 6
Virtual Target Block Increase
Complexity Reduction of Template Matching
Target block size defines forbidden area
Forbidden area ensures availability of source block pixels

## Slide 7
Virtual Target Block Increase
Complexity Reduction of Template Matching
Assume Target block / forbidden area of 1 pixel depth and execute search and store displacement vectors in memory

## Slide 8
Virtual Target Block Increase
Complexity Reduction of Template Matching
Predict first line of pixels

## Slide 9
Virtual Target Block Increase
Complexity Reduction of Template Matching
Predict next line with stored displacement vectors
Process can be repeated for defined number of lines

## Slide 10
Virtual Target Block Increase
Complexity Reduction of Template Matching
Predict next line with stored displacement vectors
Process can be repeated for defined number of lines

## Slide 11
Parameters
For this experiment:
  Target Block Size 12x16 (with virtual increase)
  Template Size 16x2
Scheme is flexible, multiple configurations could be designed and usage signaled in bitstream
Complexity Reduction of Template Matching

## Slide 12
Template Matching Search Area
Search area is grown progressively, can be stopped by early termination
Fixed parameters for test
  Stopping criterion: SAD Threshold changed from 24 to 128
  Search area: Triangle area minimum size 3 and maximum size 12
Averaging 1-4 best candidates with SAD-based selection process
Early Termination of TM-Search

## Slide 13
Search only on Luma
search on luma only
up- and downsampling for chroma subsampling?
Chroma can be calculated directly without need for up- and downsampling
Complexity Reduction of Template Matching

## Slide 14
Motion Compensated Padding and Template Matching Padding
Motion compensated padding (JVET-AA0096) currently used in ECM
Area where MC padding is not applicable is filled with TM padding (combined approach)

## Slide 15
Test Overview
Anchor ECM 14
2 Methods:
  Template Matching Padding (instead of MC-Padding)
  Motion Compensated and Template Matching Padding (combined)
Padding margin for all methods: 16 pixels (repetitive padding beyond that)
Results

## Slide 16
CTC for SDR – TM Method
Results
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0,08% | -0,14% | -0,07% | 100,0% | 100,0% | 99,7% | 100,8%
Class A2 | 0,10% | 0,00% | 0,02% | 100,1% | 99,9% | 99,9% | 100,5%
Class B | 0,06% | -0,02% | 0,02% | 99,7% | 100,1% | 99,6% | 99,5%
Class C | 0,08% | 0,17% | 0,22% | 100,3% | 99,6% | 98,9% | 98,0%
Class E |  |  |  |  |  |  | 
Overall | 0,08% | 0,01% | 0,06% | 100,0% | 99,9% | 99,5% | 99,6%
Class D | 0,21% | -0,02% | 0,34% | 100,1% | 99,3% | 99,2% | 96,2%
Class F | 0,05% | 0,03% | 0,03% | 100,0% | 99,5% | 99,4% | 98,5%
Class TGM | -0,02% | 0,05% | -0,04% | 100,3% | 100,2% | 100,2% | 99,3%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0,06% | -0,03% | -0,42% | 100,5% | 100,2% | 99,7% | 99,7%
Class C | -0,09% | 0,21% | -0,46% | 100,2% | 99,9% | 99,7% | 97,3%
Class E | -0,13% | 0,06% | -1,39% | 100,5% | 100,8% | 100,5% | 98,2%
Overall | -0,09% | 0,07% | -0,68% | 100,4% | 100,2% | 99,9% | 98,5%
Class D | -0,06% | 0,53% | 0,25% | 100,6% | 99,7% | 99,1% | 96,2%
Class F | -0,38% | -0,63% | 0,08% | 110,2% | 101,4% | 98,9% | 98,6%
Class TGM | 0,05% | 0,03% | 0,21% | #ZAHL! | #ZAHL! | #ZAHL! | #ZAHL!
 | Low delay P Main 10 |  |  |  |  |  | 
 | Over ECM-14 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0,08% | 0,22% | -0,04% | 99,6% | 100,0% | 99,8% | 97,1%
Class C | -0,11% | 0,20% | -0,63% | 98,5% | 100,4% | 100,9% | 96,2%
Class E | -0,04% | 0,14% | -0,18% | 99,7% | 100,4% | 98,7% | 96,7%
Overall | -0,08% | 0,19% | -0,27% | 99,2% | 100,2% | 99,9% | 96,7%
Class D | -0,27% | -1,02% | -0,04% | 99,2% | 99,0% | 100,1% | 96,1%
Class F | 0,12% | -0,05% | 0,14% | 99,0% | 100,2% | 99,5% | 97,9%
Class TGM | 0,00% | -0,08% | 0,01% | 98,7% | 100,2% | 101,4% | 100,5%

## Slide 17
CTC for SDR – MC-TM Method
Results
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0,02% | -0,14% | -0,20% | 99,0% | 100,8% | 99,9% | 99,8%
Class A2 | -0,01% | 0,05% | -0,11% | 99,0% | 100,3% | 99,8% | 99,6%
Class B | -0,02% | -0,01% | 0,08% | 99,2% | 100,4% | 100,0% | 99,7%
Class C | -0,04% | -0,05% | 0,10% | 99,4% | 100,1% | 99,7% | 99,8%
Class E |  |  |  |  |  |  | 
Overall | -0,02% | -0,04% | -0,01% | 99,2% | 100,4% | 99,9% | 99,7%
Class D | -0,02% | -0,14% | 0,29% | 99,2% | 100,2% | 100,0% | 100,0%
Class F | -0,01% | -0,03% | 0,17% | 99,2% | 101,0% | 100,3% | 99,9%
Class TGM | -0,03% | 0,07% | -0,02% | 100,0% | 100,4% | 100,4% | 100,1%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | 0,03% | 0,09% | 0,00% | 99,1% | 100,1% | 100,0% | 99,8%
Class C | -0,01% | 0,03% | -0,48% | 99,7% | 100,5% | 99,6% | 100,0%
Class E | 0,00% | -0,07% | -0,53% | 99,6% | 101,6% | 100,8% | 100,3%
Overall | 0,01% | 0,03% | -0,29% | 99,4% | 100,6% | 100,1% | 100,0%
Class D | -0,21% | 0,17% | 0,00% | 100,8% | 100,0% | 100,1% | 100,0%
Class F | -0,48% | -0,94% | 0,43% | 109,4% | 102,1% | 99,6% | 100,0%
Class TGM | -0,02% | 0,03% | 0,13% | #ZAHL! | #ZAHL! | #ZAHL! | #ZAHL!
 | Low delay P Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0,05% | 0,39% | -0,06% | 99,1% | 100,2% | 100,0% | 99,9%
Class C | -0,03% | 0,24% | -0,25% | 97,8% | 100,0% | 100,7% | 99,9%
Class E | -0,06% | -1,02% | 0,70% | 98,7% | 100,4% | 99,0% | 100,1%
Overall | -0,05% | -0,01% | 0,07% | 98,6% | 100,2% | 100,0% | 99,9%
Class D | -0,14% | -1,13% | -0,86% | 98,8% | 101,2% | 100,6% | 100,0%
Class F | 0,28% | -0,18% | 1,46% | 98,5% | 100,2% | 101,6% | 100,0%
Class TGM | -0,02% | 0,03% | -0,10% | 98,3% | 98,7% | 100,4% | 99,9%

## Slide 18
Conclusion
TM Reference Picture Padding outperforms MC-Padding in low delay configurations
  LDB: -0,09% luma BD-rate for 100.2% DecT
  LDP: -0,08% luma BD-rate for 100.2% DecT
Therefore, study in an Exploration Experiment is proposed