## Slide 1: AhG11: Attention based CNN for Chroma Intra Prediction
Mouad Aderdor, Gosala Kulupana, Marc Gorriz Blanch, Luka Murn
36th JVET meeting, Kemer, Turkiye, 1-8 Nov 2024
JVET-AJ0062

## Slide 2: Overview
A CNN based intra prediction mode for Chroma is proposed:
It uses cross component information such as Collocated Luma and Cross Component Boundary.
Combines features from both branches via Attention.
Infers both Chroma blocks at once

## Slide 3: Pipeline
Preprocessing
Collocated Luma downsampled to match chroma
One reference line of length from each channel is extracted, flattened and stacked
Both inputs are converted to float32 and normalized by
Inference
Float32
MIP method
Postprocessing
Output is m

## Slide 4: Features
Attention module
Cross component boundary and collocated luma blocks are merged via the attention mechanism
It measures the contribution of each reference samples location to the output
Block size adaptability
Fully convolutional
The model is jointly trained on multiple block sizes
Signalling
Implemented as a new mode. Undergoes RD checks if chroma PU size

## Slide 5: Performance results

## Slide 6: Performance results
Table1: Attention CNN for chroma results over NNVC anchor. Both ref and test encoders are limited to partition square CUs with dimensions between 8 and 32

## Slide 7: Conclusion
A new Neural Network intra prediction mode is proposed for Chroma
Average Results on NNVC 10 report following BD rates
    AI: -0.14% (Y), -0.80% (U), -0.60% (V) for 108% (encoder) and 158% (decoder) complexities
Average Results on NNVC 10 with square CUs only report following BD rates
    AI: -0.34% (Y), -2.75% (U), -2.14% (V) for 158% (encoder) and 578% (decoder) complexities
Most gains can be found on high resolution sequences (Class A1)
We are currently working on:
    Supporting more block sizes
    Retrain on JVET training set
    SADL implementation
    Model quantization

## Slide 8: Thank you !
Email: Mouad.Aderdor@bbc.co.uk