## Slide 1: JVET-AJ0087 Non-EE2: Block vector guided DIMD
Lai Zhang, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction
The DIMD process in ECM derives up to five intra modes from the reconstructed neighbor samples, and those five predictors are combined with the non-directional predictor (planar or a block vector based predictor) with the weights derived from the histogram of gradients (HoG)
It is proposed to use the reference samples pointed at by the block vectors instead of the neighboring samples to build HoG and derive intra modes

## Slide 3: Proposed – Block vector guided DIMD
Up to 5 block vectors are obtained by a searching process like in IntraTMP. With each block vector, a reference area in the current picture is determined. All located reference areas are used to construct the HoG and derive five intra modes.
The proposed method is explicitly signaled as a sub-mode of DIMD. The encoder will always check this mode with a full RD, like DIMD and OBIC
Five derived intra modes are used to generate the five intra predictions and the prediction of the current block is the blending of these five intra predictors and a non-directional predictor, like DIMD and OBIC
The non-directional predictor is the blending of up to 5 BV-based predictors obtained using the searched block vectors
Current CU
Reference
BV
Sobel operator

## Slide 4: Simulation results
proposed method over ECM-14.0:
 | All Intra Main 10 |  |  |  | 
 | Over ECM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.03% | -0.03% | 104.9% | 105.7%
Class A2 | -0.13% | -0.03% | -0.09% | 103.8% | 105.8%
Class B | -0.14% | -0.05% | 0.09% | 105.0% | 106.0%
Class C | -0.15% | -0.06% | 0.02% | 104.1% | 108.7%
Class E | -0.11% | 0.12% | 0.22% | 104.0% | 103.1%
Overall | -0.14% | 0.00% | 0.05% | 104.4% | 106.0%
Class D | -0.10% | 0.12% | 0.03% | 104.2% | 106.3%
Class F | -0.16% | -0.12% | -0.05% | 102.6% | 103.6%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.05% | 0.10% | 0.09% | 101.1% | 99.9%
Class C | -0.07% | 0.05% | 0.23% | 101.0% | 101.1%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.05% | -0.24% | -0.15% | 100.3% | 101.1%
Class F |  |  |  |  | 

## Slide 5: Conclusions
Block vector guided DIMD (BVG-DIMD) method is proposed
It brings -0.14%/0.00%/0.05% BD-rates performance for AI on top of ECM-14.0
It is suggested to further study the proposed method in EE2.
Thanks to vivo for cross-checking!