## Slide 1: Non-EE2: On MPM with matrix-based position dependent intra prediction JVET-AJ0088
Zexing Sun, Yue Yu, Haoping Yu, Luhang Xu, Dong Wang (OPPO)

## Slide 2: Introduction
Matrix-based position-dependent intra-prediction (MPDIP) is an adopted coding tool in the current ECM-14.0. MPDIP replaces a part of conventional intra-prediction modes(IPMs).
The L-shaped reference samples multiply the matrix to generate
final prediction samples.
Coding block size | #IPMs replaced by MPDIP
Coding block size | #IPMs replaced by MPDIP

## Slide 3: Proposed method
It is proposed to use MPDIP based MPM list construction.
If the current CU is eligible for MPDIP predictions, some non-MPDIP modes in the primary MPM list are converted to MPDIP.
For MPDIP modes in the primary MPM, if the current CU is eligible for MPM sort, MPDIP template cost instead of regular angular template cost is used for sorting.
Reference samples for the above template
Reference samples for the left template

## Slide 4: Simulation results
An average of -0.07%/-0.02% coding gain for AI/RA over ECM14.0 with a slight decoding time increase.
Thanks to Alibaba for crosschecking this proposal.
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.08% | -0.20% | -0.14% | 99.4% | 99.2% | 98.8% | 100.0%
Class A2 | -0.04% | -0.05% | -0.08% | 99.6% | 99.9% | 100.0% | 100.0%
Class B | -0.06% | 0.05% | 0.04% | 100.5% | 101.0% | 102.2% | 99.9%
Class C | -0.06% | -0.15% | -0.12% | 100.0% | 101.8% | 98.8% | 100.1%
Class E | -0.10% | -0.02% | 0.05% | 100.4% | 100.8% | 99.7% | 100.0%
Overall | -0.07% | -0.06% | -0.04% | 100.0% | 100.6% | 100.1% | 100.0%
Class D | -0.10% | 0.05% | -0.16% | 100.0% | 103.1% | 100.0% | 100.0%
Class F | -0.08% | -0.09% | 0.07% | 100.6% | 101.8% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.03% | -0.26% | -0.21% | 100.3% | 100.3% | 100.0% | 99.8%
Class A2 | 0.01% | -0.17% | -0.12% | 99.8% | 99.7% | 99.8% | 99.7%
Class B | -0.03% | -0.07% | 0.16% | 99.7% | 99.8% | 100.0% | 100.1%
Class C | -0.04% | -0.15% | 0.24% | 100.3% | 99.8% | 100.0% | 100.1%
Class E |  |  |  |  |  |  | 
Overall | -0.02% | -0.15% | 0.05% | 100.0% | 99.9% | 100.0% | 100.0%
Class D | -0.05% | -0.16% | 0.26% | 100.4% | 100.2% | 99.9% | 100.0%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!