## Slide 1: Non-EE2: GPM extension JVET-AJ0089
Hongli Zhang, Fan Wang, Yue Yu, Haoping Yu, Dong Wang (OPPO)

## Slide 2: Introduction
The CU size restriction of GPM is currently specified as “cbWidth >= 8 && cbHeight >= 8 && cbWidth <= 64 && cbHeight <= 64 && cbHeight < 8 * cbWidth && cbWidth < 8 * cbHeight”.
For the offset parameters of GPM, the minimum value at each angle is currently set to width/8 or height/8 for all block sizes.

## Slide 3: Proposed method
It is proposed to modify the CU size restriction of GPM as “cbWidth >= 4 && cbHeight >= 4 && cbWidth <= 128 && cbHeight <= 128”.
The minimum offset is set as cbHeight /4 or cbWidth /4 for CUs of size 4*cbHeight or cbWidth*4.
width/height | 4 | 8 | 16 | 32 | 64 | 128
4 | 4x4 | 8x4 | 16x4 | 32x4 | 64x4 | 128x4
8 | 4x8 | 8x8 | 16x8 | 32x8 | 64x8 | 128x8
16 | 4x16 | 8x16 | 16x16 | 32x16 | 64x16 | 128x16
32 | 4x32 | 8x32 | 16x32 | 32x32 | 64x32 | 128x32
64 | 4x64 | 8x64 | 16x64 | 32x64 | 64x64 | 128x64
128 | 4x128 | 8x128 | 16x128 | 32x128 | 64x128 | 128x128

## Slide 4: Simulation results
The proposed method brings -0.12% coding gain in RA.
It is recommended to further study the proposed method in the next round of EE2.
Thanks to Bytedance for crosschecking this proposal.
Test 1: block size restricted from 4 to 128
Test 2: block size restricted from 8 to 128
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.12% | -0.22% | -0.23% | 105.7% | 99.9% | 100.6% | 100.4%
Class A2 | -0.18% | -0.17% | -0.40% | 104.5% | 98.6% | 100.9% | 100.3%
Class B | -0.08% | -0.11% | -0.09% | 106.0% | 100.0% | 101.6% | 100.2%
Class C | -0.11% | -0.22% | -0.17% | 107.6% | 99.5% | 103.5% | 100.6%
Class E |  |  |  |  |  |  | 
Overall | -0.12% | -0.17% | -0.20% | 106.3% | 99.5% | 101.8% | 100.4%
Class D | -0.17% | -0.64% | -0.40% | 106.7% | 99.4% | 105.3% | 100.6%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.16% | -0.32% | -0.36% | 103.8% | 99.9% | 100.7% | 100.5%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class B | -0.06% | -0.02% | 0.04% | 102.9% | 99.8% | 101.6% | 100.3%
Class C | -0.02% | -0.13% | 0.17% | 101.7% | 100.1% | 103.9% | 100.5%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class D | -0.02% | -0.14% | -0.04% | 100.8% | 98.7% | 105.3% | 100.6%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!