## Slide 1: Non-EE2: OBIC with improved sampling strategy and scaling weights
Yutian Liu, Yongkai Huo(Transsion)
Gang Li, Junjie Chen, Lei Luo, Hongwei Guo, Ce Zhu(UESTC)
JVET-AJ0098

## Slide 2: Introduction
OBIC in ECM14.0：
  The spatial neighboring blocks of the current block are identified using 13 adjacent and 18 non-adjacent sampling points.
  For DIMD, TIMD, SGPM, or OBIC blocks, it may produce multiple area-related amplitudes corresponding to different angular modes.

## Slide 3: Proposed Method
Aspect #1. Sampling strategy of spatial neighborhood blocks
  For adjacent sampling points, we extend the number from 13 to 21. These points are selected from the top area, left area, and top-left area of the current block for locating the adjacent spatial neighborhood blocks.
  For non-adjacent sampling points, we extend the number from 18 to 48.
Figure 1. Adjacent sampling strategy
Figure 2. Non-adjacent sampling strategy

## Slide 4: Proposed Method
Aspect #2. Scaling weights for area-related amplitudes
  Fristly, weights are applied on all the original area-related amplitudes. The weights are selected from {1/4,1/2,1,0}, depending on the current block size and the distance of the sampling points from the current block.
  Secondly, weights are applied on area-related amplitudes derived from DIMD, TIMD, SGPM, or OBIC blocks by individually counting their IPM mode number and dividing accordingly.
Table 1. weights for DIMD, TIMD, SGPM, or OBIC blocks
blocks | minimum value of weight
DIMD | 1/6
TIMD | 1/3
SGPM | 1/2
OBIC | 1/6

## Slide 5: Results
The proposed method is implemented on top of the ECM-14.0 software and tested with JVET ECM common test conditions in AI configurations.
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | -0.04% | -0.09% | 103.4% | 102.2% | 99.9% | 100.0%
Class A2 | -0.01% | -0.06% | 0.02% | 103.0% | 102.2% | 100.0% | 100.0%
Class B | -0.02% | 0.06% | 0.12% | 102.6% | 101.4% | 97.9% | 100.0%
Class C | -0.01% | 0.05% | -0.10% | 102.4% | 102.1% | 99.6% | 100.0%
Class E | -0.03% | 0.12% | 0.27% | 103.1% | 101.6% | 102.1% | 100.0%
Overall | -0.02% | 0.03% | 0.04% | 102.8% | 101.8% | 99.6% | 100.0%
Class D | -0.01% | -0.01% | -0.10% | 102.7% | 101.9% | 99.9% | 100.0%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Table 2: Test results of JVET-AJ0098 over ECM-14.0

## Slide 6: Summary
This contribution proposes to expand the sampling strategy of spatial neighborhood blocks and scaling weights are applied on area-related amplitudes.
The proposed method brings some coding gains.
It is proposed to study this method in EE2.

## Slide 7: Thanks
www.transsion.com