## Slide 1: JVET-AJ0122 - AhG14: SADL implementation improvements for sparse models
Fabrice Urban, Franck Galpin, Thierry Dumas

## Slide 2: Introduction
In NNVC, some networks have sparse layers. Intra prediction models for example have up to 95% of zero coefficients in the largest layer.
This contribution brings two improvement aspects:
  Optimization of sparse implementation of matrix multiplication,
  Reduction of the data storage requirement for the models.

## Slide 3: Optimization for sparse matrix multiplication 1/3
Sparsity reduces number of operations
But requires indirections to access elements. Need to fill SIMD buffers element-by-element before multiply-accumulate operations.
X
X
=
A
A0’
B0
B0’

## Slide 4: Optimization for sparse matrix multiplication 2/3
sparsity with packing: Non-zero elements processed by packs to ease the use of SIMD operation.
Packing constraints can be enforced at learning for best performances
X
X
=
A
A0’
B0
B0’

## Slide 5: Optimization for sparse matrix multiplication 3/3
Best performances when packing constraints enforced during learning
X
X
=
A
A0’
B0
B0’

## Slide 6: Optimization of sparse model storage
Store model data using sparse representation: non-zero-elements, packing size, position indices, number of non-zero elements per column.
  reduces the model storage size: more than 80% of space saved
  avoids the need for sparsity analysis at initialization.
  Memory usage is also reduced since the full matrix is not needed.
Intra model | Current version | Sparse version | Size ratio
graph_output_16_16_int16.sadl | 3 934 444 | 1 055 753 | 27%
graph_output_4_16_int16.sadl | 3 778 450 | 623 247 | 16%
graph_output_4_32_int16.sadl | 4 245 394 | 826 955 | 19%
graph_output_4_4_int16.sadl | 1 937 298 | 291 345 | 15%
graph_output_4_8_int16.sadl | 2 017 170 | 418 451 | 21%
graph_output_8_16_int16.sadl | 4 634 514 | 921 561 | 20%
graph_output_8_8_int16.sadl | 4 245 394 | 777 857 | 18%

## Slide 7: Running time
Up to 2% decoding time improvement are achieved in AI over NNVC with lop3.
 | BD-rate Over NNVC-10.0 LOP |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU
Class A1 | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 99%
Class A2 | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 99%
Class B | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 98%
Class C | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 98%
Class E | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 99%
Overall | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 99%
Class D | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 98%
Class F | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | 0,00% | #NUM! | 99%
Table 2. decoding time on NNVC-10.0 LOP

## Slide 8: Conclusion
Reduces the model storage size: more than 80% of space saved
Up to 2% decoding time improvement are achieved in AI over NNVC with lop3.
We propose to adopt these modifications to the SADL software.
MR !112 on SADL GIT repository.