## Slide 1: JVET-AJ0155 AhG12: SGPM Improvements
Keqin Ding, Hongdong Qin, Jacek Konieczny, Alexey Filippov, Vasily Rufitskiy, Tianyu Dong
2024-11-03

## Slide 2: Introduction
SGPM [JVET-AB0155] is an intra mode which partitions a coding block into two parts and generates two corresponding intra predictions.
  A SPGM index is uniformly coded to determine the combination of two intra modes and a partition line in the SGPM candidate list.
  As to transform coding, the LFNST transform kernel is determined by the direction of its partitioning mode.

## Slide 3: Proposal
It is proposed to introduce binary coding with context for SGPM index.
SGPM index | Code word | Context
0 | 0000 | 
1 | 0001 | 
2-3 | 001 + 1-bit binary | 
4-7 | 01 + 2-bit binary | 
8-15 | 1 + 3-bit binary | 
SGPM index | Code word | Context
0 | 0000 | 
1 | 0001 | 
2-3 | 001 + 1-bit binary | 
4-7 | 01 + 2-bit binary | 
8-15 | 1 + 3-bit binary | 

## Slide 4: Proposal
It is proposed to apply HoG-based VIPM derivation to SGPM. The DIMD-liked method is used to derive a VIPM based on the SGPM prediction samples
  The LFNST/NSPT transform set is determined by the derived VIPM.
  The SGPM mode in MPM list is determined by the derived VIPM.

## Slide 5: Experimental results
Test: Multiple SGPM improvements
 | AI |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.03% | -0.14% | -0.04% | 100.5% | 101.1% | 100.1% | 100.0%
Class A2 | -0.02% | -0.02% | -0.01% | 100.4% | 101.2% | 100.8% | 100.1%
Class B | -0.03% | 0.05% | 0.04% | 100.7% | 100.6% | 103.0% | 100.1%
Class C | -0.03% | -0.06% | -0.02% | 100.4% | 101.2% | 100.0% | 100.0%
Class E | -0.05% | 0.06% | 0.16% | 101.1% | 101.7% | 100.0% | 100.0%
Overall | -0.03% | -0.01% | 0.02% | 100.6% | 101.1% | 101.0% | 100.0%
Class D | -0.02% | 0.06% | -0.04% | 100.6% | 101.4% | 100.0% | 100.0%
Class F | -0.08% | -0.18% | -0.02% | 100.3% | 101.1% | 97.9% | 100.0%
Class TGM(-3) | -0.10% | -0.12% | -0.15% | 100.4% | 101.3% | 101.2% | 100.0%
(-x): missing x lines of data and filled with anchor |  |  |  |  |  |  | 

## Slide 6: Conclusion
In this contribution, context coding of SGPM index, HoG-based VIPM derivation for SGPM are proposed.
It is recommended that the proposed methods be studied in the next round of EE2.
Thank you!