## Slide 1: JVET-AJ0156 Non-EE2 Adaptive interpolation filter for reference sample in angular mode
Tianyu Dong, Alexey Filippov, Jacek Konieczny, Vasily Rufitskiy, Hongdong Qin, Keqin Ding
2024-11-05, Kemer, Türkiye

## Slide 2: Introduction
A 6-tap Lagrange interpolation filter is used in the process for reference sample in the fractional prediction slope. In this proposal, an 8-tap interpolation filter are implemented with conditional filter switch on top of 6-tap filter.
Bumyoon Kim et al.: Intra Coding Tools of Enhanced Compression beyond VVC Capability, 2022
Proposed
OR

## Slide 3: Proposal: Adaptive filter selection for reference sample interpolation
It is proposed to introduce an adaptive filter selection for reference sample interpolation in angular mode of intra prediction
  8-taps Lagrange interpolation filters (Page 4 for coefficients)
    2 more sample are used in the interpolation
    Usage of filter coefficients
  Filter adaptive selection (Page 7 for detailed condition)
    Prediction angle distance to HOR or VER
    Block size

## Slide 4: 8-taps interpolation filter
32 phases and 64 phases 8-tap interpolation filter
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 8192 | 0 | 0 | 0 | 0
1 | -2 | 25 | -148 | 8117 | 262 | -77 | 17 | -2
2 | -5 | 49 | -283 | 8021 | 535 | -155 | 34 | -4
3 | -7 | 71 | -407 | 7904 | 818 | -233 | 51 | -5
4 | -9 | 91 | -518 | 7768 | 1110 | -311 | 68 | -7
5 | -11 | 110 | -617 | 7612 | 1410 | -387 | 84 | -9
6 | -12 | 128 | -705 | 7438 | 1716 | -462 | 99 | -10
7 | -14 | 143 | -780 | 7246 | 2029 | -534 | 114 | -12
8 | -15 | 156 | -845 | 7038 | 2346 | -603 | 128 | -13
9 | -17 | 168 | -898 | 6815 | 2667 | -669 | 141 | -15
10 | -18 | 178 | -939 | 6576 | 2989 | -731 | 153 | -16
11 | -19 | 186 | -971 | 6324 | 3313 | -788 | 164 | -17
12 | -19 | 191 | -992 | 6060 | 3636 | -839 | 173 | -18
13 | -20 | 195 | -1003 | 5785 | 3958 | -885 | 181 | -19
14 | -20 | 197 | -1004 | 5498 | 4276 | -924 | 188 | -19
15 | -20 | 198 | -996 | 5203 | 4590 | -956 | 193 | -20
16 | -20 | 196 | -980 | 4900 | 4900 | -980 | 196 | -20
17 | -20 | 193 | -956 | 4590 | 5203 | -996 | 198 | -20
18 | -19 | 188 | -924 | 4276 | 5498 | -1004 | 197 | -20
19 | -19 | 181 | -885 | 3958 | 5785 | -1003 | 195 | -20
20 | -18 | 173 | -839 | 3636 | 6060 | -992 | 191 | -19
21 | -17 | 164 | -788 | 3313 | 6324 | -971 | 186 | -19
22 | -16 | 153 | -731 | 2989 | 6576 | -939 | 178 | -18
23 | -15 | 141 | -669 | 2667 | 6815 | -898 | 168 | -17
24 | -13 | 128 | -603 | 2346 | 7038 | -845 | 156 | -15
25 | -12 | 114 | -534 | 2029 | 7246 | -780 | 143 | -14
26 | -10 | 99 | -462 | 1716 | 7438 | -705 | 128 | -12
27 | -9 | 84 | -387 | 1410 | 7612 | -617 | 110 | -11
28 | -7 | 68 | -311 | 1110 | 7768 | -518 | 91 | -9
29 | -5 | 51 | -233 | 818 | 7904 | -407 | 71 | -7
30 | -4 | 34 | -155 | 535 | 8021 | -283 | 49 | -5
31 | -2 | 17 | -77 | 262 | 8117 | -148 | 25 | -2
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 8192 | 0 | 0 | 0 | 0
1 | -1 | 13 | -75 | 8157 | 129 | -39 | 9 | -1
2 | -2 | 25 | -148 | 8117 | 262 | -77 | 17 | -2
3 | -4 | 37 | -217 | 8072 | 397 | -116 | 26 | -3
4 | -5 | 49 | -283 | 8021 | 535 | -155 | 34 | -4
5 | -6 | 60 | -346 | 7965 | 675 | -194 | 43 | -5
6 | -7 | 71 | -407 | 7904 | 818 | -233 | 51 | -5
7 | -8 | 81 | -464 | 7839 | 963 | -272 | 59 | -6
8 | -9 | 91 | -518 | 7768 | 1110 | -311 | 68 | -7
9 | -10 | 101 | -569 | 7692 | 1259 | -349 | 76 | -8
10 | -11 | 110 | -617 | 7612 | 1410 | -387 | 84 | -9
11 | -12 | 119 | -662 | 7528 | 1562 | -424 | 91 | -10
12 | -12 | 128 | -705 | 7438 | 1716 | -462 | 99 | -10
13 | -13 | 135 | -744 | 7344 | 1872 | -498 | 107 | -11
14 | -14 | 143 | -780 | 7246 | 2029 | -534 | 114 | -12
15 | -15 | 150 | -814 | 7144 | 2188 | -569 | 121 | -13
16 | -15 | 156 | -845 | 7038 | 2346 | -603 | 128 | -13
17 | -16 | 162 | -872 | 6928 | 2506 | -637 | 135 | -14
18 | -17 | 168 | -898 | 6815 | 2667 | -669 | 141 | -15
19 | -17 | 173 | -920 | 6696 | 2828 | -700 | 147 | -15
20 | -18 | 178 | -939 | 6576 | 2989 | -731 | 153 | -16
21 | -18 | 182 | -956 | 6451 | 3151 | -760 | 158 | -16
22 | -19 | 186 | -971 | 6324 | 3313 | -788 | 164 | -17
23 | -19 | 189 | -982 | 6192 | 3474 | -814 | 169 | -17
24 | -19 | 191 | -992 | 6060 | 3636 | -839 | 173 | -18
25 | -19 | 194 | -998 | 5923 | 3796 | -863 | 177 | -18
26 | -20 | 195 | -1003 | 5785 | 3958 | -885 | 181 | -19
27 | -20 | 197 | -1004 | 5642 | 4116 | -905 | 185 | -19
28 | -20 | 197 | -1004 | 5498 | 4276 | -924 | 188 | -19
29 | -20 | 198 | -1001 | 5352 | 4434 | -941 | 190 | -20
30 | -20 | 198 | -996 | 5203 | 4590 | -956 | 193 | -20
31 | -20 | 197 | -989 | 5052 | 4746 | -969 | 195 | -20
32 | -20 | 196 | -980 | 4900 | 4900 | -980 | 196 | -20
33 | -20 | 195 | -969 | 4746 | 5052 | -989 | 197 | -20
34 | -20 | 193 | -956 | 4590 | 5203 | -996 | 198 | -20
35 | -20 | 190 | -941 | 4434 | 5352 | -1001 | 198 | -20
36 | -19 | 188 | -924 | 4276 | 5498 | -1004 | 197 | -20
37 | -19 | 185 | -905 | 4116 | 5642 | -1004 | 197 | -20
38 | -19 | 181 | -885 | 3958 | 5785 | -1003 | 195 | -20
39 | -18 | 177 | -863 | 3796 | 5923 | -998 | 194 | -19
40 | -18 | 173 | -839 | 3636 | 6060 | -992 | 191 | -19
41 | -17 | 169 | -814 | 3474 | 6192 | -982 | 189 | -19
42 | -17 | 164 | -788 | 3313 | 6324 | -971 | 186 | -19
43 | -16 | 158 | -760 | 3151 | 6451 | -956 | 182 | -18
44 | -16 | 153 | -731 | 2989 | 6576 | -939 | 178 | -18
45 | -15 | 147 | -700 | 2828 | 6696 | -920 | 173 | -17
46 | -15 | 141 | -669 | 2667 | 6815 | -898 | 168 | -17
47 | -14 | 135 | -637 | 2506 | 6928 | -872 | 162 | -16
48 | -13 | 128 | -603 | 2346 | 7038 | -845 | 156 | -15
49 | -13 | 121 | -569 | 2188 | 7144 | -814 | 150 | -15
50 | -12 | 114 | -534 | 2029 | 7246 | -780 | 143 | -14
51 | -11 | 107 | -498 | 1872 | 7344 | -744 | 135 | -13
52 | -10 | 99 | -462 | 1716 | 7438 | -705 | 128 | -12
53 | -10 | 91 | -424 | 1562 | 7528 | -662 | 119 | -12
54 | -9 | 84 | -387 | 1410 | 7612 | -617 | 110 | -11
55 | -8 | 76 | -349 | 1259 | 7692 | -569 | 101 | -10
56 | -7 | 68 | -311 | 1110 | 7768 | -518 | 91 | -9
57 | -6 | 59 | -272 | 963 | 7839 | -464 | 81 | -8
58 | -5 | 51 | -233 | 818 | 7904 | -407 | 71 | -7
59 | -5 | 43 | -194 | 675 | 7965 | -346 | 60 | -6
60 | -4 | 34 | -155 | 535 | 8021 | -283 | 49 | -5
61 | -3 | 26 | -116 | 397 | 8072 | -217 | 37 | -4
62 | -2 | 17 | -77 | 262 | 8117 | -148 | 25 | -2
63 | -1 | 9 | -39 | 129 | 8157 | -75 | 13 | -1

## Slide 5: Frequency responses of magnitude
Half of the phases are shown in these figures. RED: 6-taps BLUE: 8-taps
64 phases 32phases

## Slide 6: Frequency responses of phases
All phases are shown in these figures. RED: 6-taps BLUE: 8-taps
64 phases 32phases

## Slide 7: Filter adaptive selection
a). Intra prediction angle condition
Angle distance farther from the horizontal or vertical
Adaptive angle distance thresholds on block size
b). Block size condition: Smaller blocks
block with possible directions (only on fractional direction)
blue slope, 8-taps interpolation filer
red slope, 6-taps interpolation filter

## Slide 8: Experimental results
ECM 14.0
  Full AI result
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | 0.10% | -0.03% | 100.5% | 99.5% | 101.7% | 100.0%
Class A2 | -0.01% | -0.02% | -0.02% | 99.9% | 99.7% | 100.0% | 100.0%
Class B | -0.02% | 0.00% | 0.07% | 99.9% | 99.4% | 102.0% | 100.1%
Class C | -0.11% | 0.00% | -0.06% | 100.2% | 99.1% | 100.5% | 100.0%
Class E | -0.08% | -0.03% | 0.08% | 100.6% | 97.0% | 98.9% | 100.0%
Overall | -0.05% | 0.01% | 0.01% | 100.2% | 99.0% | 100.8% | 100.0%
Class D | -0.08% | -0.09% | -0.16% | 98.1% | 101.0% | 100.0% | 100.0%
Class F | -0.12% | -0.22% | -0.05% | 100.1% | 100.2% | 99.1% | 100.1%
Class TGM | 0.00% | -0.06% | -0.05% | 100.2% | 99.3% | 102.5% | 100.1%

## Slide 9: Experimental results
RA partial result
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class B | -0.01% | -0.06% | -0.12% | 100.5% | 100.5% | 99.9% | 99.9%
Class C | -0.05% | -0.20% | 0.22% | 100.1% | 97.8% | 99.6% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | -0.05% | 0.00% | 0.05% | 100.3% | 100.3% | 100.1% | 100.0%
Class F | 0.07% | 0.07% | 0.12% | 99.0% | 97.3% | 99.9% | 100.1%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!

## Slide 10: Conclusion
In this contribution, an 8-tap interpolation filter and an adaptive filter selection is proposed and a overall AI {-0.05%,0.01%,0.01%, 100.2%,99.0%, 100.8%,100.0%} is achieved.
It is recommended that the proposed methods be studied in the next round of EE2.
Thanks for Kyungpook National University of Crosschecking:JVET-AJ0322
Thank you for your attention.