## Slide 1: JVET-AJ0169 Non-EE2: Improvement on non-MPM
Guiqi Wang, Chuan Zhou ,Zhuoyi lv,
vivo Mobile Communication Co., Ltd

## Slide 2: Introduction
In current ECM-14.0, the primary MPM (PMPM) list consists of 6 entries and the secondary MPM (SMPM) list includes 16 entries.
After the PMPM and SMPM lists are constructed, the remaining 45 intra modes which do not belong to either the PMPM list or SMPM list compose the non-MPM list, and are arranged in ascending order of intra mode index.
The distribution of selected mode index in the non-MPM list in current ECM-14.0 was analyzed. It can be seen from the distribution histograms in Fig1 and Fig2.
Figure 1. Distribution of Campfire

## Slide 3: Introduction
The per-class distribution of selected mode index in the non-MPM list in current ECM-14.0.
Figure 2. Distribution of other sequences

## Slide 4: non-MPM list construction
In this proposal, the non-MPM list is constructed as follows:
The first non-planar mode in the MPM list is selected as the starting intra-frame mode.
From the starting intra mode, fill the non-MPM list in turns with one forward mode and then one backward with the same step, where the step increases by one in each turn. Skip the mode which has already been included in the PMPM list or the SMPM list.
For example:
The starting intra mode is 3, the non-MPM list is filled as: 2,4,1,5,66,6...
If a mode satisfies the PDP mode condition, swap it with the previous filled non-PDP mode.

## Slide 5: non-MPM list construction
By using the proposed method, a regular downward trend distribution of the selected intra mode in the non-MPM list is illustrated in Fig3.
Figure 3. Distribution using the proposed method

## Slide 6: Simulation results
Simulation results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-13.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.01% | -0.06% | 99.9% | 100.8%
Class A2 | -0.01% | -0.06% | -0.07% | 99.8% | 100.0%
Class B | -0.02% | -0.01% | 0.04% | 99.0% | 99.8%
Class C | -0.01% | -0.06% | 0.00% | 98.9% | 98.9%
Class E | -0.03% | 0.02% | 0.07% | 99.4% | 98.6%
Overall | -0.02% | -0.03% | -0.03% | 99.3% | 99.6%
Class D | -0.01% | -0.10% | -0.16% | 99.5% | 99.7%

## Slide 7: Conclusions
This contribution proposes a non-MPM list construction method.
It is suggested to investigate it in the next round of EE2.
Thanks to PKU for cross-checking.(crosscheck proposal number AJ0296)

## Slide 8
THANK
YOU