## Slide 1: JVET-AJ0171 Non-EE2: Weighted OBIC
P. Andrivon, M. Blestel, N. Zouidi

## Slide 2: Introduction
Occurrence-based intra coding mode (OBIC, JVET-AH0076) is a sub-mode of DIMD
  Based on sample-wise occurrence of IPM in the spatial neighborhood of the block (adjacent and non-adjacent blocks)
  Building a Histogram of Occurrences (HoC)
Some blocks use more than one IPM (Mi)
for shaping the predictor:
  DIMD (up to 5 ang. modes)
  TIMD (up to 2 ang. modes)
  GPM (up to 2 modes)
  OBIC (up to 5 ang. modes)
  Each mode Mi contributes equally in HoC
HoC[Mi] += w x h
  w width and h height of neigh. block
OBIC predictor is a blending of up to 6 IPM

## Slide 3: Example - current
Block 1: DIMD mode with modes {1, 4, 3, 2} in contribution order
HoC(1) = 2
HoC(2) = 2
HoC(3) = 2
HoC(4) = 2
HoC(5) =

## Slide 4: Example - current
Block 1: DIMD mode with modes {1, 4, 3, 2} in contribution order
Block 2: TIMD with modes {2, 3} in contribution order
HoC(1) = 2
HoC(2) = 2 + 1
HoC(3) = 2 + 1
HoC(4) = 2
HoC(5) =

## Slide 5: Example - current
Block 1: DIMD mode with modes {1, 4, 3, 2} in contribution order
Block 2: TIMD with modes {2, 3} in contribution order
Block 3: DIMD mode with modes {1, 5, 4, 3, 2} in contribution order
HoC(1) = 2 + 4 = 6
HoC(2) = 2 + 1 + 4 = 7
HoC(3) = 2 + 1 + 4 = 7
HoC(4) = 2 + 4 = 6
HoC(5) = 4
Although mode 1 contributes mostly (weight) to big blocks prediction, “weak” modes 2, 3 present in more neighboring blocks prevail in OBIC prediction.

## Slide 6: Proposition
For neighboring blocks:
  Inherit weights ki from blending process (TIMD/DIMD)
  Inherit location dependency state
    OBIC sample-based fusion (same as TIMD/DIMD)
  Scale s (linear) w.r.t. distance between current and neighboring blocks
HoC[Mi] += s x ki x w x h

## Slide 7: Example – proposition (weights focus)
Block 1: DIMD mode with modes {(1;30), (4;20), (3;10), (2;4)} in contribution order
Block 2: TIMD with modes {(2;34), (3;30)} in contribution order
Block 3: DIMD mode with modes {(1;22), (5;20), (4;9), (3;7), (2;4)} in contribution order
HoC(1) = 2x30 + 4x22 = 148
HoC(2) = 2x4 + 1x34 + 4x4 = 58
HoC(3) = 2x10 + 1x30 + 4x7 = 78
HoC(4) = 2x20 + 4x9 = 76
HoC(5) = 4x20 = 80

## Slide 8: Results
On top of ECM-14.0:
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | 0.04% | -0.07% | 98.8% | 100.7% | 100.1% | 100.2%
Class A2 | -0.01% | 0.02% | -0.02% | 101.0% | 100.0% | 99.8% | 100.0%
Class B | -0.01% | -0.05% | 0.06% | 99.9% | 100.5% | 97.7% | 100.2%
Class C | -0.01% | 0.04% | -0.15% | 100.7% | 100.3% | 99.2% | 100.1%
Class E | -0.03% | 0.22% | 0.19% | 100.2% | 100.9% | 99.3% | 100.1%
Overall | -0.02% | 0.04% | 0.00% | 100.1% | 100.5% | 99.0% | 100.1%
Class D | -0.01% | 0.03% | -0.09% | 101.2% | 103.0% | 99.9% | 100.0%

## Slide 9: Conclusion
Proposition of OBIC HoC weighting and sample-based fusion
Re-using:
  Weights used in fusion process (DIMD, TIMD)
  Location-dependent sample-based fusion (DIMD, TIMD)
OBIC gains increased by +20%
  Luma gains -0.02% AI {100.1% / 100.5%}
Propose for study in next round of EE2