## Slide 1: AHG12: ALF-CCCM JVET-AJ0173 Pekka Astola, Ikram Jumakulyyev, Done Bugdayci Sansli, Jani Lainema

## Slide 2
Overview of the proposed method
ALF-CCCM is a CCCM-based loop filter.
The CCCM coefficients are derived using the SAO outputs.
The CCCM convolution is applied using the ALF luma output.
The proposed method on the decoder.

## Slide 3
Details of the cross-component process
A CCCM process is applied over non-overlapping blocks.
  Each block has its own set of CCCM coefficients.
Each CTU can select from 8 block sizes and 8 cross-component filter types (64 choices).
  2x2, 3x3, 4x4, 8x8, 16x16, 32x32, 64x64, 128x128
  Filter sizes range from 2-tap to 11-tap.
For each CTU, the encoder determines the best block size and cross-component filter type.
  All blocks within a CTU share the same block size and filter type.
CTUs with luma ALF disabled are skipped.

## Slide 4
CCCM coefficient derivation
The CCCM coefficients are derived using the SAO luma and chroma outputs.
The SAO luma output is downsampled using the 6-tap downsampling filter of CCLM/CCCM.
For coefficient derivation the block size is extended symmetrically by one 1 sample in each direction.
  For example, for 2x2 blocks the coefficients are derived using 4x4 blocks.

## Slide 5
CCCM convolution
The CCCM convolution is applied using the ALF luma output.
The ALF luma output is downsampled using the 6-tap downsampling filter of CCLM/CCCM.
The final output is 50/50 blend between the SAO chroma output and the CCCM convolution output.

## Slide 6
Encoder operation and bitstream signaling
The encoder performs RDO for each CTU to select the best block size and filter type.
The block sizes and filter types are signaled per CTU using CABAC coded flags.
  CTUs with luma ALF disabled are skipped.
A CTU can inherit the block size and filter type from the left or the above CTU.
For inter-slices, the block sizes and filter types for all CTUs can be inherited from a reference picture.

## Slide 7
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.05 % | -1.30 % | -1.72 % | 101.1% | 111.7% | 102.5% | 104.2%
Class A2 | 0.03 % | -1.29 % | -1.49 % | 100.9% | 111.5% | 102.5% | 103.3%
Class B | 0.07 % | -1.95 % | -1.75 % | 100.8% | 107.7% | 101.4% | 102.5%
Class C | 0.06 % | -1.62 % | -1.85 % | 100.3% | 111.6% | 103.6% | 102.4%
Class E | 0.08 % | -1.34 % | -1.10 % | 100.7% | 107.3% | 104.7% | 102.6%
Overall | 0.06 % | -1.56 % | -1.62 % | 100.7% | 109.8% | 102.8% | 102.9%
Class D | 0.05 % | -0.86 % | -0.94 % | 100.6% | 121.2% | 101.4% | 102.7%
Class F | 0.09 % | -1.30 % | -1.55 % | 99.7% | 107.9% | 102.3% | 102.3%
Class TGM | 0.09 % | -0.34 % | -0.39 % | 100.0% | 104.4% | 103.4% | 102.0%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.07 % | -1.57 % | -2.27 % | 101.1% | 104.5% | 100.8% | 106.0%
Class A2 | 0.03 % | -1.64 % | -2.06 % | 101.0% | 103.2% | 100.4% | 104.2%
Class B | 0.02 % | -2.40 % | -1.80 % | 100.4% | 103.0% | 100.8% | 103.5%
Class C | 0.04 % | -2.04 % | -2.03 % | 100.2% | 104.6% | 99.4% | 102.5%
Class E |  |  |  |  |  |  | 
Overall | 0.04 % | -1.98 % | -2.01 % | 100.6% | 103.8% | 100.3% | 103.9%
Class D | 0.04 % | -1.44 % | -1.26 % | 100.6% | 106.1% | 101.1% | 102.4%
Class F | 0.12 % | -1.31 % | -1.27 % | 100.4% | 104.5% | 97.9% | 101.7%
Class TGM | 0.16 % | -0.65 % | -0.94 % | 100.3% | 105.3% | 100.6% | 102.7%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | 0.01 % | -5.50 % | -4.18 % | 100.7% | 107.8% | 101.1% | 103.1%
Class C | 0.03 % | -3.99 % | -4.77 % | 100.2% | 106.2% | 102.0% | 103.0%
Class E | 0.02 % | -2.80 % | -3.20 % | 100.2% | 101.3% | 100.9% | 102.8%
Overall | 0.02 % | -4.33 % | -4.13 % | 100.4% | 105.6% | 101.4% | 103.0%
Class D | 0.08 % | -3.63 % | -4.15 % | 101.0% | 105.7% | 101.9% | 102.8%
Class F | 0.05 % | -3.31 % | -3.13 % | 100.6% | 105.8% | 101.2% | 103.2%
Class TGM | -0.07 % | -1.21 % | -1.34 % | 99.9% | 102.4% | 99.3% | 103.9%
 | Low delay P Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0.08 % | -6.12 % | -4.36 % | 100.2% | 110.0% | 101.2% | 103.3%
Class C | 0.02 % | -3.86 % | -5.23 % | 101.0% | 106.7% | 102.0% | 102.8%
Class E | 0.16 % | -3.70 % | -2.38 % | 100.2% | 103.4% | 103.2% | 103.0%
Overall | 0.02 % | -4.76 % | -4.15 % | 100.5% | 107.2% | 101.9% | 103.1%
Class D | 0.05 % | -5.28 % | -4.35 % | 100.4% | 105.9% | 103.0% | 102.9%
Class F | 0.23 % | -3.26 % | -2.89 % | 100.2% | 106.5% | 101.3% | 102.9%
Class TGM | 0.09 % | -1.01 % | -1.29 % | 100.3% | 107.3% | 99.3% | 105.7%

## Slide 8
Summary
We propose a new CCCM-based loop filter.
The experimental results indicate that the proposed method can improve chroma BD-rate with acceptable encoder runtime tradeoff.
It is suggested to include the proposed method in the next round of EE2.