## Slide 1: JVET-AJxxxx AHG15: Configurations for low-delay speed-up of worst cases

## Slide 2: Motivation
AHG15 mandates
  Propose test conditions appropriate for gaming applications
  Investigate possibilities to enhance compression capability for gaming content.
ECM encoding time for LDB is still problematic for investigating new coding tools
  Reach for encoding time reduction

## Slide 3: Current problem
JVET-AH0180 proposed slight modification on LDB/LDP encoder configuration
  Reduce maximum MTT hierarchy depth in slices with slice temporal depth >= 1
    MaxMTTHierarchyDepthByTidOverrideByQP: 22 322222
This provides a large encoding time reduction for QP22. However, in many cases, the encoding time for QP27 is now higher than that for QP22, which is very undesirable.
This contribution proposes use the same configuration parameter also for QP 27, i.e., have classB_lowdelay.cfg changed to:
  MaxMTTHierarchyDepthByTidOverrideByQP: 22 322222
  MaxMTTHierarchyDepthByTidOverrideByQP: 27 322222

## Slide 4: Results (LDB)
  Highlights indicate
  EncT(QP27) > EncT(QP22)
  All EncT(QP27) are reduced considerably, to as much as 8.49 days
  For the worst case (JianlingTemple), worst encoding time reduces from 22.33 days (QP27) to 17.45 (QP22).
  Average EncT(QP27) reduction of 30%.
  Average enc loss of 0.4%

## Slide 5: Conclusion
Change in classB_lowdelay.cfg is proposed to greatly reduce encoding time of worst cases (QP27).
Overall average loss of 0.4% for an average EncT(QP27) reduction of 30%
Propose to adopt contribution in the in the CTC for gaming applications.