## Slide 1: JVET-AJ0192 AHG15: Low delay configuration for gaming content

## Slide 2: Motivation
AHG15 mandates
  Propose test conditions appropriate for gaming applications
  Investigate possibilities to enhance compression capability for gaming content.
ECM encoding time for LDB is still problematic for investigating new coding tools
  Reach for encoding time reduction

## Slide 3: Current problem
JVET-AE0163 and JVET-AH0180 proposed modifications on low delay encoder configuration.
  Reduce maximum MTT hierarchy depth in slices with slice with higher temporal depth. Currently:
    MaxMTTHierarchyDepthByTidOverrideByQP: 22 322222
JVET-AH0220 proposed to use the same configuration files in CTC also for gaming sequences.
For many gaming sequences, however, the encoding time for QP27 in low delay is now undesirably higher than that for QP22.
This contribution proposes use the same configuration parameter used in classB_lowdelay.cfg also for QP 27, i.e., to have a new classG_lowdelay.cfg with:
  MaxMTTHierarchyDepthByTidOverrideByQP: 22 322222
  MaxMTTHierarchyDepthByTidOverrideByQP: 27 322222

## Slide 4: Results (LDB)
  Highlights indicate
  EncT(QP27) > EncT(QP22)
  All EncT(QP27) are reduced considerably, to as much as 8.49 days
  For the worst case (JianlingTemple), worst encoding time reduces from 22.33 days (QP27) to 17.45 (QP22).
  Average EncT(QP27) reduction of 30%.
  Average enc loss of 0.4%

## Slide 5: Conclusion
New configuration classG_lowdelay.cfg is proposed to greatly reduce encoding time of worst cases (QP27).
Overall average loss of 0.4% for an average EncT(QP27) reduction of 30%
Propose to adopt contribution in the in the CTC for gaming applications.