## Slide 1: JVET-AJ0226 AHG12/ AHG10 : Using CABAC cost for MTT split modes selection
Waqas Ahmad, Per Wennersten, Kenneth Andersson
Ericsson

## Slide 2: Background
ECM encoding runtime is increasing with the progression of each meeting cycle.
Several proposals have been presented to reduce the encoding runtime for ECM.
  Such as JVET-AA0098, JVET-AD0197 , JVET –AD0128, JVET-AD0105, and JVET-AF0111.
In JVET-AF0111, a condition is applied on the no-split cost of 64x64 luma CUs. If the no-split cost is greater than a threshold, MTT splitting will not be evaluated. The threshold is set based on QP value as follows:
This contribution presents a modification to this MTT split modes early termination method (JVET-AF0111) for ECM/VTM.

## Slide 3
We proposed to modify the threshold defined in JVET-AF0111 as follows:
Here,
represents the threshold value.
represents value of a Slice QP.
represents value of a base QP.
represents the strength applied to the CABAC cost. It is set to 4, 2, 1, 0.5 for QP 22, 27, 32, 37.
represents the CABAC cost to code the MTT split mode flag.
Proposal
No_split
Split_QT
Split_BTH
Split_BTV
Split_TTH
Split_TTV

## Slide 4: Test 1: Condition applied to 64x64 and 32x32 luma CUs.
 | Random Access Main 10 |  |  |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.03% | 0.04% | 0.03% | 97.2% | 90.7% | 100.5% | 99.9% | 100.2%
Class A2 | 0.07% | 0.07% | -0.08% | 95.6% | 84.5% | 99.9% | 99.7% | 100.0%
Class B | 0.01% | 0.07% | 0.10% | 95.6% | 86.6% | 99.8% | 100.1% | 99.9%
Class C | 0.03% | 0.13% | 0.12% | 94.5% | 83.4% | 99.3% | 100.4% | 99.9%
Class E |  |  |  |  |  |  |  | 
Overall | 0.03% | 0.08% | 0.06% | 95.6% | 86.1% | 99.9% | 100.1% | 100.0%
Class D | 0.04% | 0.00% | -0.05% | 95.3% | 85.5% | 99.2% | 99.8% | 100.0%
Class F |  |  |  |  |  |  |  | 
Class TGM |  |  |  |  |  |  |  | 
Results (ECM)
 | Low delay B Main 10 |  |  |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  | 
Class B | 0.10% | 0.18% | -0.20% | 96.5% | 89.0% | 100.3% | 100.0% | 100.1%
Class C | 0.05% | 0.00% | 0.14% | 94.8% | 83.5% | 100.2% | 100.0% | 100.0%
Class E | 0.08% | -0.05% | -0.08% | 96.6% | 86.7% | 99.8% | 100.1% | 100.2%
Overall | 0.08% | 0.06% | -0.06% | 96.0% | 86.6% | 100.1% | 100.0% | 100.1%
Class D | 0.05% | 0.51% | 0.34% | 95.9% | 86.8% | 100.4% | 99.7% | 100.0%
Class F |  |  |  |  |  |  |  | 
Class TGM |  |  |  |  |  |  |  | 
Test 2: Condition applied to 64x64 luma CUs.
 | Random Access Main 10 |  |  |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.02% | 0.03% | 0.01% | 98.0% | 93.2% | 99.7% | 100.1% | 100.1%
Class A2 | 0.05% | 0.05% | -0.08% | 97.1% | 89.7% | 99.9% | 100.3% | 100.5%
Class B | -0.01% | 0.00% | 0.06% | 97.1% | 91.1% | 100.1% | 100.1% | 100.0%
Class C | 0.02% | 0.02% | 0.16% | 98.2% | 95.4% | 100.2% | 100.4% | 100.0%
Class E |  |  |  |  |  |  |  | 
Overall | 0.02% | 0.02% | 0.05% | 97.6% | 92.4% | 100.0% | 100.2% | 100.1%
Class D | 0.01% | 0.14% | 0.02% | 99.1% | 97.3% | 100.8% | 100.1% | 100.1%
Class F | 0.02% | 0.01% | 0.00% | 98.4% | 95.5% | 99.6% | 99.8% | 99.7%
Class TGM | 0.01% | 0.07% | 0.00% | 99.4% | 99.1% | 100.4% | 100.0% | 99.8%
 | Low delay B Main 10 |  |  |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  | 
Class B | 0.08% | 0.00% | 0.01% | 97.2% | 91.2% | 100.6% | 100.0% | 100.0%
Class C | 0.04% | -0.02% | 0.21% | 98.5% | 95.6% | 100.1% | 100.0% | 100.1%
Class E | 0.05% | 0.03% | -0.03% | 97.0% | 87.7% | 100.0% | 99.9% | 100.1%
Overall | 0.06% | 0.00% | 0.07% | 97.6% | 91.7% | 100.3% | 100.0% | 100.0%
Class D | 0.02% | 0.77% | 0.37% | 99.3% | 98.7% | 99.2% | 99.9% | 100.0%
Class F | 0.10% | -0.26% | -0.15% | 98.9% | 97.4% | 99.4% | 99.3% | 100.1%
Class TGM | -0.04% | 0.11% | 0.10% | 99.2% | 99.0% | 99.1% | 100.0% | 100.3%

## Slide 5: Test 1: Condition applied to 64x64 and 32x32 luma CUs.
 | Random Access Main 10 |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT
Class A1 | 0.05% | 0.04% | 0.01% | 95.4% | 86.2% | 100.3%
Class A2 | 0.10% | 0.05% | 0.07% | 92.8% | 78.1% | 99.8%
Class B | 0.05% | 0.13% | 0.06% | 94.7% | 83.8% | 99.3%
Class C | 0.05% | 0.10% | -0.01% | 94.1% | 83.9% | 100.3%
Class E |  |  |  |  |  | 
Overall | 0.06% | 0.09% | 0.04% | 94.3% | 83.1% | 99.9%
Class D | 0.06% | -0.04% | 0.09% | 95.3% | 86.7% | 100.6%
Class F | 0.07% | 0.11% | 0.06% | 96.5% | 89.8% | 100.7%
Results (VTM)
 | Low delay B Main 10 |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.08% | -0.14% | 0.42% | 93.6% | 82.4% | 100.1%
Class C | 0.16% | 0.01% | -0.17% | 93.4% | 83.7% | 99.4%
Class E | 0.13% | 0.18% | 0.26% | 95.9% | 86.0% | 100.4%
Overall | 0.12% | -0.01% | 0.18% | 94.1% | 83.7% | 99.9%
Class D | 0.03% | 0.33% | 0.29% | 94.8% | 84.8% | 100.5%
Class F | 0.05% | 0.28% | -0.10% | 95.7% | 88.8% | 99.1%
Test 2: Condition applied to 64x64 luma CUs.
 | Random Access Main 10 |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT
Class A1 | 0.04% | 0.05% | 0.01% | 97% | 89.6% | 100.2%
Class A2 | 0.09% | 0.02% | 0.07% | 95% | 82.9% | 100.6%
Class B | 0.04% | 0.11% | 0.01% | 95.9% | 87.5% | 99.1%
Class C | 0.02% | -0.01% | 0.02% | 96.9% | 93.5% | 100.9%
Class E |  |  |  |  |  | 
Overall | 0.04% | 0.05% | 0.02% | 96.1% | 88.5% | 100.1%
Class D | 0.00% | -0.04% | 0.01% | 98.8% | 98.1% | 100.4%
Class F | 0.02% | 0.08% | 0.05% | 97.9% | 94.2% | 100.3%
 | Low delay B Main 10 |  |  |  |  | 
 | BD-rate Over ECM-14.0 |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | EncT-QP22 | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.07% | -0.06% | 0.36% | 95.6% | 86.5% | 100.3%
Class C | 0.10% | 0.08% | -0.01% | 97.5% | 94.2% | 100.0%
Class E | 0.13% | 0.25% | 0.20% | 96.1% | 86.3% | 100.0%
Overall | 0.09% | 0.06% | 0.19% | 96.3% | 88.9% | 100.1%
Class D | -0.05% | 0.47% | 0.27% | 99.4% | 98.4% | 100.1%
Class F | -0.01% | 0.26% | -0.45% | 97.6% | 93.3% | 99.9%

## Slide 6: Summary
This contribution proposes to modify the MTT early termination method defined in ECM-14 by also considering the CABAC cost of coding the split mode.
Test1 shows on average encoding time reduction for RA and LDB by 14% for QP22 with limited degradation in coding efficiency.
Thanks to Xiaomi and Nokia for cross-checking.

## Slide 7
Thanks